## Slide 1: CS 61C: Great Ideas in Computer Architecture Functions and Numbers
Instructor:
Krste Asanovic, Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/sp12

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s Lecture

## Slide 3: Agenda
Review
Functions
Administrivia
Everything is a Number
And in Conclusion, …

## Slide 4: Agenda
Review
Functions
Administrivia
Everything is a Number
And in Conclusion, …

## Slide 5: Six Fundamental Steps in Calling a Function
Put parameters in a place where function can access them
Transfer control to function
Acquire (local) storage resources needed for function
Perform desired task of the function
Put result value in a place where calling program can access it and restore any registers you used
Return control to point of origin, since a function can be called from several points in a program

## Slide 6: Register Allocation and Numbering

## Slide 7: MIPS Function Call Instructions
Invoke function: jump and link instruction (jal)
  “link” means form an address or link that points to calling site to allow function to return to proper address
  Jumps to address and simultaneously saves the address of following instruction in register $ra
  jal ProcedureAddress
Return from function: jump register instruction (jr)
  Unconditional jump to address specified in register
  jr $ra

## Slide 8: Notes on Functions
Calling program (caller) puts parameters into registers $a0-$a3 and uses jal X to invoke X (callee)
Must have register in computer with address of currently executing instruction
  Instead of Instruction Address Register (better name), historically called Program Counter (PC)
  It’s a program’s counter; it doesn’t count programs!
jr $ra puts address inside $ra into PC
What value does jal X place into $ra? ????
Student Roulette?

## Slide 9: Notes on Functions
Calling program (caller) puts parameters into registers $a0-$a3 and uses jal X to invoke X (callee)
Must have register in computer with address of currently executing instruction
  Instead of Instruction Address Register (better name), historically called Program Counter (PC)
  It’s a program’s counter, it doesn’t count programs!
jr $ra puts address inside $ra into PC
What value does jal X place into $ra? Next PC
PC + 4

## Slide 10: Where Are Old Register Values Saved to Restore Them After Function Call
Need a place to save old values before call function, restore them when return, and delete
Ideal is stack: last-in-first-out queue (e.g., stack of plates)
  Push: placing data onto stack
  Pop: removing data from stack
Stack in memory, so need register to point to it
$sp is the stack pointer in MIPS
Convention is grow from high to low addresses
  Push decrements $sp, Pop increments $sp
(28 out of 32, 4 left!)

## Slide 11: Example
int leaf_example (int g, int h, int i, int j)
{
int f;
f = (g + h) – (i + j);
return f;
}
Parameter variables g, h, i, and j in argument registers $a0, $a1, $a2, and $a3, and f in $s0
Assume need one temporary register $t0

## Slide 12: Stack Before, During, After Function
Need to save old values of $s0 and $t0
Contents of $s0
Contents of $t0

## Slide 13: MIPS Code for leaf_example
leaf_example:
# adjust stack for 2 int items
# save $t0 for use afterwards
# save $s0 for use afterwards
# f = g + h
# t0 = i + j
# return value (g + h) – (i + j)
# restore $s0 for caller
# restore $t0 for caller
# delete 2 items from stack
# jump back to calling routine
Student Roulette?
Notes: addi $sp,$sp,-8 # adjust stack for 2 items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
addi $sp,$sp,8 # adjust stack to delete 2 items
jr $ra # jump back to calling routine

## Slide 14: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
# save $t0 for use afterwards
# save $s0 for use afterwards
# f = g + h
# $t0 = i + j
# return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine
Student Roulette?

## Slide 15: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
# save $s0 for use afterwards
# f = g + h
# $t0 = i + j
# return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine
Student Roulette?

## Slide 16: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
# f = g + h
# $t0 = i + j
# return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine
Student Roulette?

## Slide 17: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
# $t0 = i + j
# return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine
Student Roulette?

## Slide 18: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # $t0 = i + j
# return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine
Student Roulette?

## Slide 19: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # $t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
# restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine
Student Roulette?

## Slide 20: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
# restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine
Student Roulette?

## Slide 21: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # $t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
# adjust stack to delete 2 items
# jump back to calling routine
Student Roulette?

## Slide 22: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # $t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
addi $sp,$sp,8 # adjust stack to delete 2 items
# jump back to calling routine
Student Roulette?

## Slide 23: MIPS Code for leaf_example
leaf_example:
addi $sp,$sp,-8 # adjust stack for 2 int items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # $t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
addi $sp,$sp,8 # adjust stack to delete 2 items
jr $ra # jump back to calling routine

## Slide 24
Print 4
a.out will crash
None of the above
Print -4
☐
☐
☐
☐
What will the printf output?
static int *p;
int leaf (int g, int h, int i, int j)
{
int f; p = &f;
f = (g + h) – (i + j);
return f;
}
int main(void) { int x;
x = leaf(1,2,3,4);
x = leaf(3,4,1,2);
…
printf(”%d\n”,*p);
}
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 25
Print 4
a.out will crash
None of the above
Print -4
☐
☐
☐
☐
What will the printf output?
static int *p;
int leaf (int g, int h, int i, int j)
{
int f; p = &f;
f = (g + h) – (i + j);
return f;
}
int main(void) { int x;
x = leaf(1,2,3,4);
x = leaf(3,4,1,2);
…
printf(”%d\n”,*p);
}
Really?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 26: What If a Function Calls a Function? Recursive Function Calls?
Would clobber values in $a0 to $a3 and $ra
What is the solution?
Student Roulette?
Notes: Save $ra on the stack

## Slide 27: Allocating Space on Stack
C has two storage classes: automatic and static
  Automatic variables are local to function and discarded when function exits
  Static variables exist across exits from and entries to procedures
Use stack for automatic (local) variables that don’t fit in registers
Procedure frame or activation record: segment of stack with saved registers and local variables
Some MIPS compilers use a frame pointer ($fp) to point to first word of frame
(29 of 32, 3 left!)

## Slide 28: Stack Before, During, After Call

## Slide 29: Recursive Function Factorial
int fact (int n)
{
if (n < 1) return (1);
else return (n * fact(n-1));
}

## Slide 30: Recursive Function Factorial
Fact: # adjust stack for 2 items
addi $sp,$sp,-8
# save return address
sw $ra, 4($sp) # save argument n
sw $a0, 0($sp) # test for n < 1
slti $t0,$a0,1
# if n >= 1, go to L1
beq $t0,$zero,L1 # Then part (n==1) return 1
addi $v0,$zero,1 # pop 2 items off stack
addi $sp,$sp,8 # return to caller
jr $ra
L1:
# Else part (n >= 1) # arg. gets (n – 1)
addi $a0,$a0,-1 # call fact with (n – 1)
jal fact
# return from jal: restore n
lw $a0, 0($sp) # restore return address
lw $ra, 4($sp) # adjust sp to pop 2 items
addi $sp, $sp,8 # return n * fact (n – 1)
mul $v0,$a0,$v0 # return to the caller
jr $ra
mul is a pseudo instruction
Notes: Slti: set dst to 1 if src is less than imm (signed immediate)

## Slide 31: Optimized Function Convention
To reduce expensive loads and stores from spilling and restoring registers, MIPS divides registers into two categories:
Preserved across function call
  Caller can rely on values being unchanged
  $ra, $sp, $gp, $fp, “saved registers” $s0- $s7
Not preserved across function call
  Caller cannot rely on values being unchanged
  Return value registers $v0,$v1, Argument registers $a0-$a3, “temporary registers” $t0-$t9

## Slide 32: Where is the Stack in Memory?
MIPS convention
Stack starts in high memory and grows down
  Hexadecimal (base 16) : 7fff fffchex
MIPS programs (text segment) in low end
  0040 0000hex
static data segment (constants and other static variables) above text for static variables
  MIPS convention global pointer ($gp) points to static
  (30 of 32, 2 left! – will see when talk about OS)
Heap above static for data structures that grow and shrink ; grows up to high addresses

## Slide 33: MIPS Memory Allocation

## Slide 34: Register Allocation and Numbering

## Slide 35
jal saves PC+1 in %ra
The callee can use temporary registers (%ti) without saving and restoring them
The caller can rely on save registers (%si) without fear of callee changing them
MIPS uses jal to invoke a function and jr to return from a function
☐
☐
☐
☐
Which statement is FALSE?
Notes: VertLeftWhiteCheck1
B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 36
jal saves PC+1 in %ra
The callee can use temporary registers (%ti) without saving and restoring them
The caller can rely on save registers (%si) without fear of callee changing them
MIPS uses jal to invoke a function and jr to return from a function
☐
☐
☐
☐
Which statement is FALSE?
Notes: VertLeftWhiteCheck1
B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 37: Agenda
Review
Functions
Administrivia
Everything is a Number
And in Conclusion, …

## Slide 38: Project #1
  Occurrences ARandy: 4, AKrste: 2, ADave: 3
  Target word = Dave
    CRandy: 4, CKrste: 2
    Co-occurrence with Krste: CKrste * (log(CKrste))3 / AKrste = 2 * (log(2))3 / 2 = 0.03
    Co-occurrence with Randy: CRandy * (log(CRandy))3 / ARandy = 4 * (log(4))3 / 4 = 0.22
  Your task: compute and sort co-occurrence for n-gram (for small n) word sequences, using several distance weighting functions
Randy
Krste
Dave
Randy
Randy
Dave
Dave
Krste
Randy
. . .
Doc 1
Doc 2
Doc n
Mapper 1
Mapper 2
Mapper n

## Slide 39: Project #1
Document:
“It was the best of times, it was the worst of times”
1-grams: it was the best of times worst
  it-was: distance 1, it-the: distance 2, it-best: distance 3, …
2-grams: it was, was the, the best, best of, of times, times it, was the, the worst, worst of, of times
  it was—was the: distance 1, it was—the best: distance 2, it was—best of: distance 3, …
3-grams: it was the, was the best, the best of, best of times, of times it, times it was, was the worst, the worst of, worst of times
etc.

## Slide 40: Get To Know Your Professor
1997 Jaguar xk8
1997 Land Rover Defender 90
British Car Enthusiast: Glutton for Punishment!

## Slide 41: Don’t Go Driving with Randy!

## Slide 42: Get To Know Your Professor
1943 Humber Mk VI AC
1942 Daimler Dingo Mk III SC

## Slide 43: Agenda
Review
Functions
Administrivia
Everything is a Number
And in Conclusion, …

## Slide 44: Big Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
We are here!

## Slide 45: Key Concepts
Inside computers, everything is a number
But everything is of a fixed size
  8-bit bytes, 16-bit half words, 32-bit words, 64-bit double words, …
Integer and floating point operations can lead to results too big to store within their representations: overflow/underflow

## Slide 46: Number Representation
Value of i-th digit is d × Basei where i starts at 0 and increases from right to left:
12310 = 110 x 10102 + 210 x 10101 + 310 x 10100
= 1x10010 + 2x1010 + 3x110 = 10010 + 2010 + 310
= 12310
Binary (Base 2), Hexadecimal (Base 16), Decimal (Base 10) different ways to represent an integer
  We use 1two, 5ten, 10hex to be clearer (vs. 12, 48, 510, 1016 )

## Slide 47: Number Representation
Hexadecimal digits: 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
FFFhex = 15tenx 16ten2 + 15tenx 16ten1 + 15tenx 16ten0 = 3840ten + 240ten + 15ten = 4095ten
1111 1111 1111two = FFFhex = 4095ten
May put blanks every group of binary, octal, or hexadecimal digits to make it easier to parse, like commas in decimal

## Slide 48: Signed and Unsigned Integers
C, C++, and Java have signed integers, e.g., 7, -255:
  int x, y, z;
C, C++ also have unsigned integers, which are used for addresses
32-bit word can represent 232 binary numbers
Unsigned integers in 32 bit word represent 0 to 232-1 (4,294,967,295)

## Slide 49: Unsigned Integers
0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
0000 0000 0000 0000 0000 0000 0000 0010two = 2ten
... ...
0111 1111 1111 1111 1111 1111 1111 1101two = 2,147,483,645ten
0111 1111 1111 1111 1111 1111 1111 1110two = 2,147,483,646ten
0111 1111 1111 1111 1111 1111 1111 1111two = 2,147,483,647ten
1000 0000 0000 0000 0000 0000 0000 0000two = 2,147,483,648ten
1000 0000 0000 0000 0000 0000 0000 0001two = 2,147,483,649ten
1000 0000 0000 0000 0000 0000 0000 0010two = 2,147,483,650ten
... ...
1111 1111 1111 1111 1111 1111 1111 1101two = 4,294,967,293ten
1111 1111 1111 1111 1111 1111 1111 1110two = 4,294,967,294ten
1111 1111 1111 1111 1111 1111 1111 1111two = 4,294,967,295ten

## Slide 50: Signed Integers and Two’s Complement Representation
Signed integers in C; want ½ numbers <0, want ½ numbers >0, and want one 0
Two’s complement treats 0 as positive, so 32-bit word represents 232 integers from -231 (–2,147,483,648) to 231-1 (2,147,483,647)
  Note: one negative number with no positive version
  Book lists some other options, all of which are worse
  Every computers uses two’s complement today
Most significant bit (leftmost) is the sign bit, since 0 means positive (including 0), 1 means negative
  Bit 31 is most significant, bit 0 is least significant

## Slide 51: Two’s Complement Integers
0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
0000 0000 0000 0000 0000 0000 0000 0010two = 2ten
... ...
0111 1111 1111 1111 1111 1111 1111 1101two = 2,147,483,645ten
0111 1111 1111 1111 1111 1111 1111 1110two = 2,147,483,646ten
0111 1111 1111 1111 1111 1111 1111 1111two = 2,147,483,647ten
1000 0000 0000 0000 0000 0000 0000 0000two = –2,147,483,648ten
1000 0000 0000 0000 0000 0000 0000 0001two = –2,147,483,647ten
1000 0000 0000 0000 0000 0000 0000 0010two = –2,147,483,646ten
... ...
1111 1111 1111 1111 1111 1111 1111 1101two = –3ten
1111 1111 1111 1111 1111 1111 1111 1110two = –2ten
1111 1111 1111 1111 1111 1111 1111 1111two = –1ten
Sign Bit

## Slide 52
0 to +31
-16 to +15
-15 to +16
-32 to +31
☐
☐
☐
☐
Suppose we had a 5 bit word. What integers can be represented in two’s complement?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 53
0 to +31
-16 to +15
-15 to +16
-32 to +31
☐
☐
☐
☐
Suppose we had a 5 bit word. What integers can be represented in two’s complement?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 54: MIPS Logical Instructions
Logical operations | C operators | Java operators | MIPS instructions
Bit-by-bit AND | & | & | and
Bit-by-bit OR | ¦ | ¦ | or
Bit-by-bit NOT | ~ | ~ | nor
Shift left | << | << | sll
Shift right | >> | >>> | srl
Useful to operate on fields of bits within a word
  e.g., characters within a word (8 bits)
Operations to pack /unpack bits into words
Called logical operations

## Slide 55: Bit-by-bit Definition
Operation | Input | Input | Output
AND | 0 | 0 | 0
AND | 0 | 1 | 0
AND | 1 | 0 | 0
AND | 1 | 1 | 1
OR | 0 | 0 | 0
OR | 0 | 1 | 1
OR | 1 | 0 | 1
OR | 1 | 1 | 1
NOR | 0 | 0 | 1
NOR | 0 | 1 | 0
NOR | 1 | 0 | 0
NOR | 1 | 1 | 0

## Slide 56: Examples
If register $t2 contains and
0000 0000 0000 0000 0000 1101 1100 0000two
Register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
and $t0,$t1,$t2 # reg $t0 = reg $t1 & reg $t2
Student Roulette?
Notes: and $t0,$t1,$t2 # reg $t0 = reg $t1 & reg $t2
the value of register $t0 would be
0000 0000 0000 0000 0000 1100 0000 0000two
Called a mask
or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
is this value in register $t0:
0000 0000 0000 0000 0011 1101 1100 0000two
has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 57: Examples
If register $t2 contains and
0000 0000 0000 0000 0000 1101 1100 0000two
Register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
and $t0,$t1,$t2 # reg $t0 = reg $t1 & reg $t2
0000 0000 0000 0000 0000 1100 0000 0000two
Notes: and $t0,$t1,$t2 # reg $t0 = reg $t1 & reg $t2
the value of register $t0 would be
0000 0000 0000 0000 0000 1100 0000 0000two
Called a mask
or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
is this value in register $t0:
0000 0000 0000 0000 0011 1101 1100 0000two
has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 58: Examples
If register $t2 contains and
0000 0000 0000 0000 0000 1101 1100 0000two
Register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
Student Roulette?
Notes: or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
is this value in register $t0:
0000 0000 0000 0000 0011 1101 1100 0000two
has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 59: Examples
If register $t2 contains and
0000 0000 0000 0000 0000 1101 1100 0000two
Register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
0000 0000 0000 0000 0011 1101 1100 0000two
Notes: or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
is this value in register $t0:
0000 0000 0000 0000 0011 1101 1100 0000two
has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 60: Examples
If register $t2 contains and
0000 0000 0000 0000 0000 1101 1100 0000two
Register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
Student Roulette?
Notes: and $t0,$t1,$t2 # reg $t0 = reg $t1 & reg $t2
the value of register $t0 would be
0000 0000 0000 0000 0000 1100 0000 0000two
Called a mask
or $t0,$t1,$t2 # reg $t0 = reg $t1 | reg $t2
is this value in register $t0:
0000 0000 0000 0000 0011 1101 1100 0000two
has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 61: Examples
If register $t2 contains and
0000 0000 0000 0000 0000 1101 1100 0000two
Register $t1 contains
0000 0000 0000 0000 0011 1100 0000 0000two
What is value of $t0 after:
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
1111 1111 1111 1111 1100 0011 1111 1111two
Notes: has the value 0, the result of the MIPS instruction
nor $t0,$t1,$zero # reg $t0 = ~ (reg $t1 | 0)
is this value in register $t0:
1111 1111 1111 1111 1100 0011 1111 1111two

## Slide 62: Shifting
Shift left logical moves n bits to the left (insert 0s into empty bits)
  Same as multiplying by 2n for two’s complement number
For example, if register $s0 contained
0000 0000 0000 0000 0000 0000 0000 1001two= 9ten
If executed sll $s0, $s0, 4, result is:
0000 0000 0000 0000 0000 0000 1001 0000two= 144ten
And 9ten × 2ten4 = 9ten × 16ten = 144ten
Shift right logical moves n bits to the right (insert 0s into empty bits)
  NOT same as dividing by 2n (negative numbers fail)
Notes: -2
0010  1101 + 1  1110

## Slide 63: Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contained
  0000 0000 0000 0000 0000 0000 0001 1001two= 25ten
If executed sra $s0, $s0, 4, result is:
Student Roulette?
Notes: -2
0010  1101 + 1  1110

## Slide 64: Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contained
  0000 0000 0000 0000 0000 0000 0001 1001two= 25ten
If executed sra $s0, $s0, 4, result is:
0000 0000 0000 0000 0000 0000 0000 0001two= 1ten
Notes: -2
0010  1101 + 1  1110

## Slide 65: Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contained
  1111 1111 1111 1111 1111 1111 1110 0111two= -25ten
If executed sra $s0, $s0, 4, result is:
Student Roulette?
Notes: \

## Slide 66: Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contained
  1111 1111 1111 1111 1111 1111 1110 0111two= -25ten
If executed sra $s0, $s0, 4, result is:
1111 1111 1111 1111 1111 1111 1111 1110two= -2ten
  Unfortunately, this is NOT same as dividing by 2n
    Fails for odd negative numbers
    C arithmetic semantics is that division should round towards 0
Notes: \

## Slide 67: Impact of Signed and Unsigned Integers on Instruction Sets
What (if any) instructions affected?
  Load word, store word?
  branch equal, branch not equal?
  and, or, sll, srl?
  add, sub, mult, div?
  slti (set less than immediate)?
Student Roulette?

## Slide 68
The previous statement has it backwards: && and || logical ops, & and | are branches
They are redundant and mean the same thing: && and || are simply inherited from the programming language B, the predecessor of C
Logical operations AND and OR do & and | while conditional branches do && and ||
☐
☐
☐
C provides two sets of operators for AND (& and &&) and two sets of operators for OR (| and ||) while MIPS doesn’t. Why?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 69: Peer Instruction Answer
C provides two sets of operators for AND (& and &&) and two sets of operators for OR (| and ||) while MIPS doesn’t. Why?
Red:
Logical operations AND and OR implement & and | while conditional branches implement && and ||
Reason:
e.g., && is logical and: true && true is true and everything else is false
& is bitwise and: e.g., (1010two & 1000two) = 1000two

## Slide 70: “And in Conclusion, …”
C is function oriented; code reuse via functions
  Jump and link (jal) invokes, jump register (jr $ra) returns
  Registers $a0-$a3 for arguments, $v0-$v1 for return values
  Stack for spilling registers, nested function calls, C local (automatic) variables
Program can interpret binary number as unsigned integer, two’s complement signed integer, floating point number, ASCII characters, Unicode characters, …
Integers have largest positive and largest negative numbers, but represent all in between
  Two’s comp. weirdness is one extra negative number
  Integer (and floating point operations) can lead to results too big to store within their representations: overflow/underflow

## Slide 71: Goals for Floating Point
Standard arithmetic for reals for all computers
  Like two’s complement
Keep as much precision as possible in formats
Help programmer with errors in real arithmetic
  +∞, -∞, Not-A-Number (NaN), exponent overflow, exponent underflow
Keep encoding that is somewhat compatible with two’s complement
  E.g., 0 in Fl. Pt. is 0 in two’s complement
  Make it possible to sort without needing to do floating point comparison

## Slide 72: Scientific Notation (e.g., Base 10)
Normalized scientific notation (aka standard form or exponential notation):
  r x Ei, E is exponent (usually 10), i is a positive or negative integer, r is a real number ≥ 1.0, < 10
  Normalized => No leading 0s
  61 is 6.10 x 102, 0.000061 is 6.10 x10-5
r x Ei, E where is exponent, i is a positive or negative integer, r is a real number ≥ 1.0, < 10

## Slide 73: Scientific Notation (e.g., Base 10)
(r x ei) x (s x ej) = (r x s) x ei+j
(1.999 x 102) x (5.5 x 103) = (1.999 x 5.5) x 105
= 10.9945 x 105
= 1.09945 x 106
(r x ei) / (s x ej) = (r / s) x ei-j
(1.999 x 102) / (5.5 x 103) = 0.3634545… x 10-1
= 3.634545… x 10-2
For addition/subtraction, you first must align:
(1.999 x 102) + (5.5 x 103) = (.1999 x 103) + (5.5 x 103) = 5.6999 x 103

## Slide 74: Which is Less? (i.e., closer to -∞)
0 vs. 1 x 10-127?
1 x 10-126 vs. 1 x 10-127?
-1 x 10-127 vs. 0?
-1 x 10-126 vs. -1 x 10-127?
Student Roulette?

## Slide 75: Which is Less? (i.e., closer to -∞)
0 vs. 1 x 10-127?
1 x 10-126 vs. 1 x 10-127?
-1 x 10-127 vs. 0?
-1 x 10-126 vs. -1 x 10-127?

## Slide 76: Floating Point: Representing Very Small Numbers
Zero: Bit pattern of all 0s is encoding for 0.000
  But 0 in exponent should mean most negative exponent (want 0 to be next to smallest real)
  Can’t use two’s complement (1000 0000two)
Bias notation: subtract bias from exponent
  Single precision uses bias of 127; DP uses 1023
0 uses 0000 0000two => 0-127 = -127; ∞, NaN uses 1111 1111two => 255-127 = +128
  Smallest SP real can represent: 1.00…00 x 2-126
  Largest SP real can represent: 1.11…11 x 2+127

## Slide 77: Bias Notation (+127)
∞, NaN
Zero
Getting closer to zero
How it is encoded
How it is interpreted

## Slide 78: What If Operation Result Doesn’t Fit in 32 Bits?
Overflow: calculate too big a number to represent within a word
Unsigned numbers: 1 + 4,294,967,295 (232-1)
Signed numbers: 1 + 2,147,483,647 (231-1)

## Slide 79: Depends on the Programming Language
C unsigned number arithmetic ignores overflow (arithmetic modulo 232)
  1 + 4,294,967,295 =
Student Roulette?
Notes: =0

## Slide 80: Depends on the Programming Language
C signed number arithmetic also ignores overflow
  1 + 2,147,483,647 (231-1) =
Student Roulette?
Notes: -2, 147, …

## Slide 81: Depends on the Programming Language
Other languages want overflow signal on signed numbers (e.g., Fortran)
What’s a computer architect to do?

## Slide 82: MIPS Solution: Offer Both
Instructions that can trigger overflow:
  add, sub, mult, div, addi, multi, divi
Instructions that don’t overflow are called “unsigned” (really means “no overflow”):
  addu, subu, multu, divu, addiu, multiu, diviu
Given semantics of C, always use unsigned versions
Note: slt and slti do signed comparisons, while sltu and sltiu do unsigned comparisons
  Nothing to do with overflow
  When would get different answer for slt vs. sltu?
Student Roulette?

## Slide 83: What About Real Numbers in Base 2?
r x Ei, E where is exponent (2), i is a positive or negative integer, r is a real number ≥ 1.0, < 2
Computers version of normalized scientific notation called Floating Point notation

## Slide 84: Floating Point Numbers
32-bit word has 232 patterns, so must be approximation of real numbers ≥ 1.0, < 2
IEEE 754 Floating Point Standard:
  1 bit for sign (s) of floating point number
  8 bits for exponent (E)
  23 bits for fraction (F) (get 1 extra bit of precision if leading 1 is implicit)
(-1)s x (1 + F) x 2E
Can represent from 2.0 x 10-38 to 2.0 x 1038

## Slide 85: Floating Point Numbers
What about bigger or smaller numbers?
IEEE 754 Floating Point Standard: Double Precision (64 bits)
  1 bit for sign (s) of floating point number
  11 bits for exponent (E)
  52 bits for fraction (F) (get 1 extra bit of precision if leading 1 is implicit)
(-1)s x (1 + F) x 2E
Can represent from 2.0 x 10-308 to 2.0 x 10308
32 bit format called Single Precision

## Slide 86: More Floating Point
What about 0?
  Bit pattern all 0s means 0, so no implicit leading 1
What if divide 1 by 0?
  Can get infinity symbols +∞, -∞
  Sign bit 0 or 1, largest exponent, 0 in fraction
What if do something stupid? (∞ – ∞, 0 ÷ 0)
  Can get special symbols NaN for Not-a-Number
  Sign bit 0 or 1, largest exponent, not zero in fraction
What if result is too big? (2x10308 x 2x102)
  Get overflow in exponent, alert programmer!
What if result is too small? (2x10-308 ÷ 2x102)
  Get underflow in exponent, alert programmer!

## Slide 87: Floating Point Add Associativity?
A = (1000000.0 + 0.000001) - 1000000.0
B = (1000000.0 - 1000000.0) + 0.000001
In single precision floating point arithmetic, A does not equal B
    A = 0.000000, B = 0.000001
Floating Point Addition is not Associative!
  Integer addition is associative
When does this matter?

## Slide 88: MIPS Floating Point Instructions
C, Java has single precision (float) and double precision (double) types
MIPS instructions: .s for single, .d for double
  Fl. Pt. Addition single precision: Fl. Pt. Addition double precision:
  Fl. Pt. Subtraction single precision: Fl. Pt. Subtraction double precision:
  Fl. Pt. Multiplication single precision: Fl. Pt. Multiplication double precision:
  Fl. Pt. Divide single precision: Fl. Pt. Divide double precision:
Student Roulette?

## Slide 89: MIPS Floating Point Instructions
C, Java has single precision (float) and double precision (double) types
MIPS instructions: .s for single, .d for double
  Fl. Pt. Addition single precision: add.s Fl. Pt. Addition double precision: add.d
  Fl. Pt. Subtraction single precision: sub.s Fl. Pt. Subtraction double precision: sub.d
  Fl. Pt. Multiplication single precision: mul.s Fl. Pt. Multiplication double precision: mul.d
  Fl. Pt. Divide single precision: div.s Fl. Pt. Divide double precision: div.d

## Slide 90: MIPS Floating Point Instructions
C, Java have single precision (float) and double precision (double) types
MIPS instructions: .s for single, .d for double
  Fl. Pt. Comparison single precision: Fl. Pt. Comparison double precision:
  Fl. Pt. branch:
Since rarely mix integers and Floating Point, MIPS has separate registers for floating-point operations: $f0, $f1, …, $f31
  Double precision uses adjacent even-odd pairs of registers:
  $f0 and $f1, $f2 and $f3, $f4 and $f5, …, $f30 and $f31
Need data transfer instructions for these new registers
  lwc1 (load word), swc1 (store word)
  Double precision uses two lwc1 instructions, two swc1 instructions
Notes: Floating-point comparison, single (c.x.s) and comparison, double (c.x.d),
where x may be equal (eq), not equal (neq), less than (lt), less than or equal (le), greater than (gt), or greater than or equal (ge)
Floating-point branch, true (bc1t) and branch, false (bc1f)

## Slide 91: Peer Instruction Question
Suppose Big, Tiny, and BigNegative are floats in C, with Big initialized to a big number (e.g., age of universe in seconds or 4.32 x 1017), Tiny to a small number (e.g., seconds/femtosecond or 1.0 x 10-15), BigNegative = - Big. Here are two conditionals:
(Big * Tiny) * BigNegative == (Big * BigNegative) * Tiny
(Big + Tiny) + BigNegative == (Big + BigNegative) + Tiny
Which statement about these is correct?
Orange. I. is false and II. is false
Green. I. is false and II. is true
Pink. I. is true and II. is false
Yellow. I. is true and II. is true

## Slide 92: Peer Instruction Answer
Suppose Big, Tiny, and BigNegative are floats in C, with Big initialized to a big number (e.g., age of universe in seconds or 4.32 x 1017), Tiny to a small number (e.g., seconds/femtosecond or 1.0 x 10-15), BigNegative = - Big. Here are two conditionals:
(Big * Tiny) * BigNegative == (Big * BigNegative) * Tiny
(Big + Tiny) + BigNegative == (Big + BigNegative) + Tiny
Which statement about these is correct?
Yellow. I. is true and II. is false (if we don’t consider overflow)—but there are cases where one side overflows while the other does not!
I. Works ok if no overflow, but because exponents add, if Big * BigNeg overflows, then result is overflow, not -1
II. Left hand side is 0, right hand side is tiny

## Slide 93: Pitfalls
Floating point addition is NOT associative
Some optimizations can change order of floating point computations, which can change results
Need to ensure that floating point algorithm is correct even with optimizations

## Slide 94: “And in Conclusion, …”
Program can interpret binary number as unsigned integer, two’s complement signed integer, floating point number, ASCII characters, Unicode characters, …
Integers have largest positive and largest negative numbers, but represent all in between
  Two’s comp. weirdness is one extra negative numInteger and floating point operations can lead to results too big to store within their representations: overflow/underflow
Floating point is an approximation of reals