## Slide 1: CS 61C: Great Ideas in Computer Architecture Instructions as Numbers and Floating Point Numbers
Instructors:
Krste Asanovic, Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa12

## Slide 2: Big Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
We are here!

## Slide 3: Agenda
Review
Instructions as Numbers
Administrivia
Floating Point Numbers
And in Conclusion, …

## Slide 4: Optimized Function Convention
To reduce expensive loads and stores from spilling and restoring registers, MIPS divides registers into two categories:
Preserved across function call
  Caller can rely on values being unchanged
  $ra, $sp, $gp, $fp, “saved registers” $s0- $s7
Not preserved across function call
  Caller cannot rely on values being unchanged
  Return value registers $v0,$v1, Argument registers $a0-$a3, “temporary registers” $t0-$t9

## Slide 5: Where is the Stack in Memory?
MIPS convention
Stack starts in high memory and grows down
  Hexadecimal (base 16) : 7fff fffchex
MIPS programs (text segment) in low end
  0040 0000hex
static data segment (constants and other static variables) above text for static variables
  MIPS convention global pointer ($gp) points to static
  (30 of 32, 2 left! – will see when talk about OS)
Heap above static for data structures that grow and shrink ; grows up to high addresses

## Slide 6: MIPS Memory Allocation

## Slide 7: Signed Integers and Two’s Complement Representation
Signed integers in C; want ½ numbers <0, want ½ numbers >0, and want one 0
Two’s complement treats 0 as positive, so 32-bit word represents 232 integers from -231 (–2,147,483,648) to 231-1 (2,147,483,647)
  Note: one negative number with no positive version
  Book lists some other options, all of which are worse
  Every computers uses two’s complement today
Most significant bit (leftmost) is the sign bit, since 0 means positive (including 0), 1 means negative
  Bit 31 is most significant, bit 0 is least significant

## Slide 8: Twos Complement Examples
Assume for simplicity 4 bit width, -8 to +7 represented
0011
0010
3
+2
5
0101
0011
1110
3
+ (-2)
1
1 0001
0111
0001
7
+1
-8
1000
Overflow!
1101
1110
-3
+ (-2)
-5
1 1011
1000
1111
-8
+ (-1)
+7
1 0111
Underflow!
Carry into MSB =
Carry Out MSB
Carry into MSB =
Carry Out MSB

## Slide 9: Agenda
Review
Instructions as Numbers
Administrivia
Floating Point Numbers
And in Conclusion, …

## Slide 10: Everything in a Computer is Just a Binary Number
Up to program to decide what data means
Example 32-bit data shown as binary number:
0000 0000 0000 0000 0000 0000 0000 0000two
What does it mean if its treated as
Signed integer
Unsigned integer
(Floating point)
ASCII characters
Unicode characters
MIPS instruction
Student Roulette?
Notes: Unsigned integer: 0
Signed integer: 0
Floating pointP 0.0
ASCII characters: Nul, Nul, Nul, Nul
Unicode characters: Nul, Nul
6. Sll $0,$0,0

## Slide 11: Implications of Everything is a Number
Stored program concept
  Invented about 1947 (many claim invention)
As easy to change programs as to change data!
Implications?
Student Roulette?

## Slide 12: Instructions as Numbers
Instructions are also kept as binary numbers in memory
  Stored program concept
  As easy to change programs as it is to change data
Register names mapped to numbers
Need to map instruction operation to a part of number

## Slide 13: Names of MIPS fields
op: Basic operation of instruction, or opcode
rs: 1st register source operand
rt: 2nd register source operand.
rd: register destination operand (result of operation)
shamt: Shift amount.
funct: Function. This field, often called function code, selects the specific variant of the operation in the op field
op
rs
rt
rd
shamt
funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits

## Slide 14: Instructions as Numbers
addu $t0,$s1,$s2
  Destination register $t0 is register 8
  Source register $s1 is register 17
  Source register $s2 is register 18
  Add unsigned instruction encoded as number 33
Groups of bits call fields (unused field default is 0)
Layout called instruction format
Binary version called machine instruction
000000
10001
10010
01000
00000
100001
0
17
18
8
0
33
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits

## Slide 15: Instructions as Numbers
sll $zero,$zero,0
  $zero is register 0
  Shift amount 0 is 0
  Shift left logical instruction encoded as number 0
Can also represent machine code as base 16 or base 8 number: 0000 0000hex, 0000000000oct
000000
00000
00000
00000
00000
000000
0
0
0
0
0
0
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits

## Slide 16: What about Load, Store, Immediate, Branches, Jumps?
Fields for constants only 5 bits (-16 to +15)
  Too small for many common cases
#1 Simplicity favors regularity (all instructions use one format) vs. #3 Make common case fast (multiple instruction formats)?
4th Design Principle: Good design demands good compromises
Better to have multiple instruction formats and keep all MIPS instructions same size
  All MIPS instructions are 32 bits or 4 bytes

## Slide 17: Names of MIPS Fields in I-type
op: Basic operation of instruction, or opcode
rs: 1st register source operand
rt: 2nd register source operand for branches but register destination operand for lw, sw, and immediate operations
Address/constant: 16-bit two’s complement number
  Note: equal in size of rd, shamt, funct fields
address or constant
op
rs
rt
6 bits
5 bits
5 bits
16 bits

## Slide 18: Register (R), Immediate (I), Jump (J) Instruction Formats
Now loads, stores, branches, and immediates can have 16-bit two’s complement address or constant: -32,768 (-215) to +32,767 (215-1)
What about jump, jump and link?
op
rs
rt
rd
shamt
funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-type
op
rs
rt
6 bits
5 bits
5 bits
16 bits
address or constant
I-type
address
op
6 bits
26 bits
J-type

## Slide 19: Encoding of MIPS Instructions: Must Be Unique!
Instruction | Format | op | rs | rt | rd | shamt | funct | address
addu | R | 0 | reg | reg | reg | 0 | 33ten | n.a.
subu | R | 0 | reg | reg | reg | 0 | 35ten | n.a.
sltu | R | 0 | reg | reg | reg | 0 | 43ten | n.a.
sll | R | 0 | reg | n.a | reg | constant | 0ten | n.a.
addi unsigned | I | 9ten | reg | reg | n.a. | n.a. | n.a. | constant
lw (load word) | I | 35ten | reg | reg | n.a. | n.a. | n.a. | address
sw (store word) | I | 43ten | reg | reg | n.a. | n.a. | n.a. | address
beq | I | 4ten | reg | reg | n.a. | n.a. | n.a. | address
bne | I | 5ten | reg | reg | n.a. | n.a. | n.a. | address
j (jump) | J | 2ten | n.a. | n.a. | n.a. | n.a. | n.a. | address
jal | J | 3ten | n.a. | n.a. | n.a. | n.a. | n.a. | address
jr (jump reg) | R | 0 | reg | reg | reg | 0 | 8ten | n.a.

## Slide 20: Converting C to MIPS Machine code $t0 (reg 8), &A in $t1 (reg 9), h=$s2 (reg 18)
lw $t0,1200($t1)
addu $t0,$s2,$t0
sw $t0,1200($t1)
op
rs
rt
rd
shamt
funct
R-type
op
rs
rt
address or constant
I-type
address
op
J-type
Format?
_
_
_
Instruction | Format | op | rs | rt | rd | shamt | funct | address
addu | R | 0 | reg | reg | reg | 0 | 33ten | n.a.
lw (load word) | I | 35ten | reg | reg | n.a. | n.a. | n.a. | address
sw (store word) | I | 43ten | reg | reg | n.a. | n.a. | n.a. | address
A[300] = h + A[300];
Student Roulette?
Notes: First ask types of each instruciton format for each instruction
Then break into fields for each one instrution type
Then fill in fields
Write opcodes and formats on blackboard
Sll opcode 0 , funct code 0
Addu opcode 0 , funct code 33
Lw opcode 35
Bne opcode 5
Addiu opcode 8
J opcode 2
Registers
$t1 9
$s3 19
$s5 21
$s6 22

## Slide 21: Converting C to MIPS Machine code $t0 (reg 8), &A in $t1 (reg 9), h=$s2 (reg 18)
lw $t0,1200($t1)
addu $t0,$s2,$t0
sw $t0,1200($t1)
op
rs
rt
rd
shamt
funct
R-type
op
rs
rt
address or constant
I-type
address
op
J-type
Format?
_
_
_
Instruction | Format | op | rs | rt | rd | shamt | funct | address
addu | R | 0 | reg | reg | reg | 0 | 33ten | n.a.
lw (load word) | I | 35ten | reg | reg | n.a. | n.a. | n.a. | address
sw (store word) | I | 43ten | reg | reg | n.a. | n.a. | n.a. | address
A[300] = h + A[300];
35
1200
9
8
0
8
18
8
0 33
43
9
8
1200
Notes: First ask types of each instruciton format for each instruction
Then break into fields for each one instrution type
Then fill in fields
Write opcodes and formats on blackboard
Sll opcode 0 , funct code 0
Addu opcode 0 , funct code 33
Lw opcode 35
Bne opcode 5
Addiu opcode 8
J opcode 2
Registers
$t1 9
$s3 19
$s5 21
$s6 22

## Slide 22: Agenda
Review
Floating Point Numbers
Administrivia
Instructions as Numbers
And in Conclusion, …

## Slide 23: CS61c in the News
iPhone 5, 9/12/12
  ARM Cortex A-15 core
  Claimed 2x Performance of iPhone 4’s A5 Chip (fabricated by Samsung!)
  Still dual core

## Slide 24: CS 61c in the News
1-1.5 Ghz, dual core
Level 1 caches: 32KB instruction and 32KB data, with cache coherence
“out-of-order superscalar pipeline with a tightly-coupled low-latency level-2 cache up to 4MB in size”
  15 stage integer / 17-25 stage floating point pipeline, with out-of-order speculative issue 3-way superscalar execution pipeline
“full hardware virtualization, Large Physical Address Extensions (LPAE) addressing (40 bit) to 1TB, error correction capability for fault-tolerance and soft-fault recovery”
“hw support for data management and arbitration, enabling multiple software environments and apps to simultaneously access the system capabilities”

## Slide 25: Agenda
Review
Instructions as Numbers
Administrivia
Floating Point Numbers
And in Conclusion, …

## Slide 26: Goals for Floating Point
Standard arithmetic for reals for all computers
  Like two’s complement
Keep as much precision as possible in formats
Help programmer with errors in real arithmetic
  +∞, -∞, Not-A-Number (NaN), exponent overflow, exponent underflow
Keep encoding that is somewhat compatible with two’s complement
  E.g., 0 in Fl. Pt. is 0 in two’s complement
  Make it possible to sort without needing to do floating point comparison

## Slide 27: Scientific Notation (e.g., Base 10)
Normalized scientific notation (aka standard form or exponential notation):
  r x Ei, E is exponent (usually 10), i is a positive or negative integer, r is a real number ≥ 1.0, < 10
  Normalized => No leading 0s
  61 is 6.10 x 102, 0.000061 is 6.10 x10-5

## Slide 28: Scientific Notation (e.g., Base 10)
(r x ei) x (s x ej) = (r x s) x ei+j
(1.999 x 102) x (5.5 x 103) = (1.999 x 5.5) x 105
= 10.9945 x 105
= 1.09945 x 106
(r x ei) / (s x ej) = (r / s) x ei-j
(1.999 x 102) / (5.5 x 103) = 0.3634545… x 10-1
= 3.634545… x 10-2
For addition/subtraction, you first must align:
(1.999 x 102) + (5.5 x 103) = (.1999 x 103) + (5.5 x 103) = 5.6999 x 103

## Slide 29: Which is Less? (i.e., closer to -∞)
0 vs. 1 x 10-127?
1 x 10-126 vs. 1 x 10-127?
-1 x 10-127 vs. 0?
-1 x 10-126 vs. -1 x 10-127?
Student Roulette?

## Slide 30: Which is Less? (i.e., closer to -∞)
0 vs. 1 x 10-127?
1 x 10-126 vs. 1 x 10-127?
-1 x 10-127 vs. 0?
-1 x 10-126 vs. -1 x 10-127?

## Slide 31: Floating Point: Representing Very Small Numbers
Zero: Bit pattern of all 0s is encoding for 0.000
  But 0 in exponent should mean most negative exponent (want 0 to be next to smallest real)
  Can’t use two’s complement (1000 0000two)
Bias notation: subtract bias from exponent
  Single precision uses bias of 127; DP uses 1023
0 uses 0000 0000two => 0-127 = -127; ∞, NaN uses 1111 1111two => 255-127 = +128
  Smallest SP real can represent: 1.00…00 x 2-126
  Largest SP real can represent: 1.11…11 x 2+127

## Slide 32: Bias Notation (+127)
∞, NaN
Zero
Getting closer to zero
How it is encoded
How it is interpreted

## Slide 33: What If Operation Result Doesn’t Fit in 32 Bits?
Overflow: calculate too big a number to represent within a word
Unsigned numbers: 1 + 4,294,967,295 (232-1)
Signed numbers: 1 + 2,147,483,647 (231-1)

## Slide 34: Depends on the Programming Language
C unsigned number arithmetic ignores overflow (arithmetic modulo 232)
  1 + 4,294,967,295 =
Student Roulette?
Notes: =0

## Slide 35: Depends on the Programming Language
C unsigned number arithmetic ignores overflow (arithmetic modulo 232)
  1 + 4,294,967,295 = FFFFhex + 1 = 0
Notes: =0

## Slide 36: Depends on the Programming Language
C signed number arithmetic also ignores overflow
  1 + 2,147,483,647 (231-1) =
Student Roulette?
Notes: -2, 147, …

## Slide 37: Depends on the Programming Language
C signed number arithmetic also ignores overflow
  1 + 2,147,483,647 (231-1) = 1 + EFFFhex = FFFFhex = -1
Notes: -2, 147, …

## Slide 38: Depends on the Programming Language
Other languages want overflow signal on signed numbers (e.g., Fortran)
What’s a computer architect to do?

## Slide 39: MIPS Solution: Offer Both
Instructions that can trigger overflow:
  add, sub, mult, div, addi, multi, divi
Instructions that don’t overflow are called “unsigned” (really means “no overflow”):
  addu, subu, multu, divu, addiu, multiu, diviu
Given semantics of C, always use unsigned versions
Note: slt and slti do signed comparisons, while sltu and sltiu do unsigned comparisons
  Nothing to do with overflow
  When would get different answer for slt vs. sltu?
Student Roulette?

## Slide 40: MIPS Solution: Offer Both
Instructions that can trigger overflow:
  add, sub, mult, div, addi, multi, divi
Instructions that don’t overflow are called “unsigned” (really means “no overflow”):
  addu, subu, multu, divu, addiu, multiu, diviu
Given semantics of C, always use unsigned versions
Note: slt and slti do signed comparisons, while sltu and sltiu do unsigned comparisons
  Nothing to do with overflow
  When would get different answer for slt vs. sltu?
  -1 < 0 signed, but FFFFhex > 0 unsigned!

## Slide 41: What About Real Numbers in Base 2?
r x Ei, E where exponent is (2), i is a positive or negative integer, r is a real number ≥ 1.0, < 2
Computers version of normalized scientific notation called Floating Point notation

## Slide 42: Floating Point Numbers
32-bit word has 232 patterns, so must be approximation of real numbers ≥ 1.0, < 2
IEEE 754 Floating Point Standard:
  1 bit for sign (s) of floating point number
  8 bits for exponent (E)
  23 bits for fraction (F) (get 1 extra bit of precision if leading 1 is implicit)
(-1)s x (1 + F) x 2E
Can represent from 2.0 x 10-38 to 2.0 x 1038

## Slide 43: Floating Point Numbers
What about bigger or smaller numbers?
IEEE 754 Floating Point Standard: Double Precision (64 bits)
  1 bit for sign (s) of floating point number
  11 bits for exponent (E)
  52 bits for fraction (F) (get 1 extra bit of precision if leading 1 is implicit)
(-1)s x (1 + F) x 2E
Can represent from 2.0 x 10-308 to 2.0 x 10308
32 bit format called Single Precision

## Slide 44: More Floating Point
What about 0?
  Bit pattern all 0s means 0, so no implicit leading 1
What if divide 1 by 0?
  Can get infinity symbols +∞, -∞
  Sign bit 0 or 1, largest exponent, 0 in fraction
What if do something stupid? (∞ – ∞, 0 ÷ 0)
  Can get special symbols NaN for Not-a-Number
  Sign bit 0 or 1, largest exponent, not zero in fraction
What if result is too big? (2x10308 x 2x102)
  Get overflow in exponent, alert programmer!
What if result is too small? (2x10-308 ÷ 2x102)
  Get underflow in exponent, alert programmer!

## Slide 45: Floating Point Add Associativity?
A = (1000000.0 + 0.000001) - 1000000.0
B = (1000000.0 - 1000000.0) + 0.000001
In single precision floating point arithmetic, A does not equal B
    A = 0.000000, B = 0.000001
Floating Point Addition is not Associative!
  Integer addition is associative
When does this matter?

## Slide 46: MIPS Floating Point Instructions
C, Java has single precision (float) and double precision (double) types
MIPS instructions: .s for single, .d for double
  Fl. Pt. Addition single precision: Fl. Pt. Addition double precision:
  Fl. Pt. Subtraction single precision: Fl. Pt. Subtraction double precision:
  Fl. Pt. Multiplication single precision: Fl. Pt. Multiplication double precision:
  Fl. Pt. Divide single precision: Fl. Pt. Divide double precision:
Student Roulette?

## Slide 47: MIPS Floating Point Instructions
C, Java has single precision (float) and double precision (double) types
MIPS instructions: .s for single, .d for double
  Fl. Pt. Addition single precision: add.s Fl. Pt. Addition double precision: add.d
  Fl. Pt. Subtraction single precision: sub.s Fl. Pt. Subtraction double precision: sub.d
  Fl. Pt. Multiplication single precision: mul.s Fl. Pt. Multiplication double precision: mul.d
  Fl. Pt. Divide single precision: div.s Fl. Pt. Divide double precision: div.d

## Slide 48: MIPS Floating Point Instructions
C, Java have single precision (float) and double precision (double) types
MIPS instructions: .s for single, .d for double
  Fl. Pt. Comparison single precision: Fl. Pt. Comparison double precision:
  Fl. Pt. branch:
Since rarely mix integers and Floating Point, MIPS has separate registers for floating-point operations: $f0, $f1, …, $f31
  Double precision uses adjacent even-odd pairs of registers:
  $f0 and $f1, $f2 and $f3, $f4 and $f5, …, $f30 and $f31
Need data transfer instructions for these new registers
  lwc1 (load word), swc1 (store word)
  Double precision uses two lwc1 instructions, two swc1 instructions
Notes: Floating-point comparison, single (c.x.s) and comparison, double (c.x.d),
where x may be equal (eq), not equal (neq), less than (lt), less than or equal (le), greater than (gt), or greater than or equal (ge)
Floating-point branch, true (bc1t) and branch, false (bc1f)

## Slide 49: Peer Instruction Question
Suppose Big, Tiny, and BigNegative are floats in C, with Big initialized to a big number (e.g., age of universe in seconds or 4.32 x 1017), Tiny to a small number (e.g., seconds/femtosecond or 1.0 x 10-15), BigNegative = - Big. Here are two conditionals:
(Big * Tiny) * BigNegative == (Big * BigNegative) * Tiny
(Big + Tiny) + BigNegative == (Big + BigNegative) + Tiny
Which statement about these is correct?
Orange. I. is false and II. is false
Green. I. is false and II. is true
Pink. I. is true and II. is false
Yellow. I. is true and II. is true

## Slide 50: Peer Instruction Answer
Suppose Big, Tiny, and BigNegative are floats in C, with Big initialized to a big number (e.g., age of universe in seconds or 4.32 x 1017), Tiny to a small number (e.g., seconds/femtosecond or 1.0 x 10-15), BigNegative = - Big. Here are two conditionals:
(Big * Tiny) * BigNegative == (Big * BigNegative) * Tiny
(Big + Tiny) + BigNegative == (Big + BigNegative) + Tiny
Which statement about these is correct?
Yellow. I. is true and II. is false (if we don’t consider overflow)—but there are cases where one side overflows while the other does not!
I. Works ok if no overflow, but because exponents add, if Big * BigNeg overflows, then result is overflow, not -1
II. Left hand side is 0, right hand side is tiny

## Slide 51: Pitfalls
Floating point addition is NOT associative
Some optimizations can change order of floating point computations, which can change results
Need to ensure that floating point algorithm is correct even with optimizations

## Slide 52: “And in Conclusion, …”
Program can interpret binary number as unsigned integer, two’s complement signed integer, floating point number, ASCII characters, Unicode characters, … even instructions!
Integers have largest positive and largest negative numbers, but represent all in between
  Two’s comp. weirdness is one extra negative numInteger and floating point operations can lead to results too big to store within their representations: overflow/underflow
Floating point is an approximation of reals