## Slide 1: CS 61C: Great Ideas in Computer Architecture Datapath Building Blocks
Instructors:
Krste Asanovic, Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa12

## Slide 2: You are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today

## Slide 3: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 4: Review
Truth table can be mapped to gates for combinational logic design
Boolean algebra allows minimization of gates
Sequential vs. Combinational Logic
Unique configurations of a digital system: State and State Machines

## Slide 5: Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks

## Slide 6: Type of Circuits
Synchronous Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL) circuits
    Output is a function of the inputs only, not the history of its execution
    E.g., circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    aka “State Elements”
    E.g., memories and registers (Registers)

## Slide 7: Conceptual MIPS Datapath

## Slide 8: Agenda
Multiplexer
ALU Design
And in Conclusion, …

## Slide 9: Agenda
Multiplexer
ALU Design
And in Conclusion, …

## Slide 10: Data Multiplexer (e.g., 2-to-1 x n-bit-wide)
“mux”
Notes: Go to Logisim and do design from mux

## Slide 11: N Instances of 1-bit-Wide Mux
How many rows in TT?

## Slide 12: How Do We Build a 1-bit-Wide Mux (in Logisim)?
s
Notes: Draw on Board, Build in Logisim, create as subcircuit my mux
Make s north facing

## Slide 13: 4-to-1 Multiplexer
How many rows in TT?

## Slide 14: Alternative Hierarchical Approach (in Logisim)

## Slide 15: Logisim

## Slide 16: Subcircuits
Subcircuit: Logisim equivalent of procedure or method
  Every project is a hierarchy of subcircuits

## Slide 17: N-bit-wide Data Multiplexer (in Logisim + tunnel)
“mux”
Notes: Go to Logisim and do design from mux

## Slide 18: Administrivia

## Slide 19: Agenda
Multiplexer
ALU Design
And, in Conclusion, …

## Slide 20: Arithmetic and Logic Unit
Most processors contain a special logic block called “Arithmetic and Logic Unit” (ALU)
We’ll show you an easy one that does ADD, SUB, bitwise AND, bitwise OR

## Slide 21: Simple ALU

## Slide 22: Adder/Subtractor: One-bit adder Least Significant Bit

## Slide 23: Adder/Subtractor: One-bit adder (1/2) …

## Slide 24: Adder/Subtractor: One-bit Adder (2/2) …

## Slide 25: N x 1-bit Adders  1 N-bit Adder
+
+
+
b0
Connect Carry Out i-1 to Carry in i:

## Slide 26: Twos Complement Adder/Subtractor

## Slide 27: Critical Path
When setting clock period in synchronous systems, must allow for worst case
Path through combinational logic that is worst case called “critical path”
  Can be estimated by number of “gate delays”: Number of gates must go through in worst case
Idea: Doesn’t matter if speedup other paths if don’t improve the critical path
What might critical path of ALU?

## Slide 28: And, in Conclusion, …
Use muxes to select among input
  S input bits selects 2S inputs
  Each input can be n-bits wide, indep of S
Can implement muxes hierarchically
Arithmetic circuits are a kind of combinational logic