## Slide 1: If the Internet is the answer, then what was the question?
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 2: Administrivia
Participation: administrivia questions don’t count
  And don’t send your email during class (duh!)
  Math: 340 students/ 27 lectures ~ 12.5 comments/lecture
Sections start this week
  If you asked about a switch, should have heard from me
Instructional account forms sent by email
  Should have them by now
Midterm clash:
  Is Oct 11th ok?

## Slide 3: Outline for today’s class
The telephone network
Taxonomy of networks
Some basics of packet switching
Statistical multiplexing
  This is something you should know deep in your soul…

## Slide 4: Review of Telephone Network

## Slide 5: Telephones
Alexander Graham Bell
  1876: Demonstrates the telephone at US Centenary Exhibition in Philadelphia

## Slide 6: Telephone was an app, not a network!
The big technological breakthrough was to turn voice into electrical signals and vice versa.
  Great achievement
  One of the nastiest patent battles in history
The demonstration of this new device involved two phones connected by a single dedicated wire.

## Slide 7: What about the phone “network”?
You can’t have a dedicated wire between every two telephones
  Doesn’t scale
  Most wires will go unused….
You need a “shared network” of wires
  Much like the highway is shared by cars going to different destinations
The telephone network grew into the first large-scale electronic network

## Slide 8: Telephone network uses circuit switching
Establish: source creates circuit to destination
  Nodes along the path store connection info
  And reserve resources for the connection
  If circuit not available: “Busy signal”
Transfer: source sends data over the circuit
  No destination address in msg, since nodes know path
  Continual stream of data
Teardown: source tears down circuit when done

## Slide 9: The switch in “circuit switching”
incoming links
outgoing links
Node
How does the node connect the incoming link to the outgoing link?

## Slide 10: Circuit Switching With Human Operator

## Slide 11: “Modern” switches
Almon Brown Strowger (1839 - 1902)
  1889: Invents the “girl-less, cuss-less” telephone system -- the mechanical switching system

## Slide 12: Timing in Circuit Switching
Host 1
Host 2
Switch 1
Switch 2
time

## Slide 13: Timing in Circuit Switching
Circuit Establishment
Host 1
Host 2
Switch 1
Switch 2
propagation delay
between Host 1
and Switch1
time

## Slide 14: Timing in Circuit Switching
Circuit Establishment
Host 1
Host 2
Switch 1
Switch 2
propagation delay
between Host 1
and Switch1
Transmission delay
time

## Slide 15: Timing in Circuit Switching
Circuit Establishment
Host 1
Host 2
Switch 1
Switch 2
propagation delay
between Host 1
and Switch1
Transmission delay
time

## Slide 16: Timing in Circuit Switching
Circuit Establishment
Host 1
Host 2
Switch 1
Switch 2
propagation delay
between Host 1
and Switch1
propagation delay
between Host 1
and Host 2
Transmission delay
time

## Slide 17: Timing in Circuit Switching
Information
Circuit Establishment
Transfer
Host 1
Host 2
Switch 1
Switch 2
propagation delay
between Host 1
and Switch1
propagation delay
between Host 1
and Host 2
Transmission delay
time

## Slide 18: Timing in Circuit Switching
Information
Circuit Establishment
Transfer
Circuit Teardown
Host 1
Host 2
Switch 1
Switch 2
propagation delay
between Host 1
and Switch1
propagation delay
between Host 1
and Host 2
Transmission delay
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 19: Sharing a link
incoming links
outgoing links
Node
How do the black and orange circuits share the outgoing link?

## Slide 20: Circuit Switching: Multiplexing a Link
Time-division
  Each circuit allocated certain time slots
Frequency-division
  Each circuit allocated certain frequencies
time
frequency
time

## Slide 21: Time-Division Multiplexing/Demultiplexing
Time divided into frames; frames into slots
Relative slot position inside a frame determines to which conversation data belongs
  E.g., slot 0 belongs to orange conversation
Requires synchronization between sender and receiver
  Need to dynamically bind a slot to a conversation
If a conversation does not use its circuit capacity is lost!
Frames
0
1
2
3
4
5
0
1
2
3
4
5
Slots =

## Slide 22: Strengths of phone system
Predictable performance
  Known delays
  No drops
Easy to control
  Centralized management of how calls are routed
Easy to reason about
Supports a crucial service
What about weaknesses?

## Slide 23: Weakness #1: Not resilient to failure
Any failure along the path prevents transmission
Entire transmission has to be restarted
  “All or nothing” delivery model

## Slide 24: All-or-Nothing Delivery
Information
Host 1
Host 2
Switch 1
Switch 2
Must restart from beginning after failure

## Slide 25: Weakness #2: Wastes bandwidth
Consider a network application with:
  Peak bandwidth P
  Average bandwidth A
How much does the network have to reserve for the application to work?
  The peak bandwidth
What is the resulting level of utilization?
  Ratio of A/P

## Slide 26: Smooth vs Bursty Applications
Some applications have relatively small P/A ratios
  Voice might have a ratio of 3:1 or so
Data applications tend to be rather bursty
  Ratios of 100 or greater are common
Circuit switching too inefficient for bursty apps
Generally:
  Don’t care about factors of two in performance
  But when it gets to several orders of magnitude….

## Slide 27: Statistical Multiplexing
Will delve into this in more detail later
But this is what drives the use of a shared network
And it is how we could avoid wasting bandwidth

## Slide 28: Weakness #3: Designed Tied to App
Design revolves around the requirements of voice
Not general feature of circuit switching
  But definitely part of the telephone network design
  Switches are where functionality was implemented

## Slide 29: Weakness #4: Setup Time
Every connection requires round-trip time to set up
  Slows down short transfers
In actuality, may not be a big issue
  TCP requires round-trip time for handshake
  No one seems to mind….
This was a big issue in the ATM vs IP battle
  But I think it is overemphasized as a key factor

## Slide 30: How to overcome these weaknesses?
There were two independent threads that led to a different networking paradigm….

## Slide 31: What if we wanted a resilient network?
How would we design it?
This is the question Paul Baran asked….

## Slide 32: Paul Baran
Baran investigated survivable networks for USAF
  Network should withstand almost any degree of destruction to individual components without loss of end-to-end communications.
“On Distributed Communications” (1964)
  Distributed control
  Message blocks (packets)
  Store-and-forward delivery

## Slide 33: What about a less wasteful network?
How would we design it?
This is the question Len Kleinrock asked…..
  Analyzed packet switching and statistical multiplexing

## Slide 34: Returning to title of lecture
If the Internet is the answer, then what was the question?
There were two questions:
  How can we build a more reliable network?
  How can we build a more efficient network?
Before considering nature of Internet, let’s consider the broader design space for networks
  Term “network” already implies we are sharing a communications infrastructure (i.e. not dedicated links)

## Slide 35: Taxonomy of Networks

## Slide 36: Taxonomy of Communication Networks
Communication networks can be classified based on the way in which the nodes exchange information:
Communication Network

## Slide 37: Taxonomy of Communication Networks
Communication networks can be classified based on the way in which the nodes exchange information:
Communication Network
Broadcast Communication Network

## Slide 38: Broadcast Communication Networks
Information transmitted by any node is received by every other node in the network
  Usually only in LANs (Local Area Networks)
    E.g., WiFi, Ethernet (classical, but not current)
    E.g., lecture!
What problems does this raise?
Problem #1: limited range
Problem #2: coordinating access to the shared communication medium
  Multiple Access Problem
Problem #3: privacy of communication
Notes: Do Multiaccess problem for: smoke signals, radio, ethernet
When can I tell there is a collision?
Does everyone know there is a collision? [if not, I might get screwed]

## Slide 39: Taxonomy of Communication Networks
Communication networks can be classified based on the way in which the nodes exchange information:
Communication Network
Switched Communication Network
Broadcast Communication Network

## Slide 40: Taxonomy of Communication Networks
Communication networks can be classified based on the way in which the nodes exchange information:
Communication Network
Switched Communication Network
Broadcast Communication Network
The term “switched” means that communication is directed to specific destinations
The question is how that “switching” is done

## Slide 41: Taxonomy of Communication Networks
Communication networks can be classified based on the way in which the nodes exchange information:
Communication Network
Switched Communication Network
Broadcast Communication Network
Circuit-Switched Communication Network

## Slide 42: Taxonomy of Communication Networks
Communication networks can be classified based on the way in which the nodes exchange information:
Communication Network
Switched Communication Network
Broadcast Communication Network
Circuit-Switched Communication Network
Packet-Switched Communication Network

## Slide 43: Packet Switching
Data sent as chunks of formatted bit-sequences (Packets)
Packets have following structure:
    Header and Trailer carry control information (e.g., destination address, checksum)
Each packet traverses the network from node to node along some path (Routing) based on header info.
Usually, once a node receives the entire packet, it stores it (hopefully briefly) and then forwards it to the next node (Store-and-Forward Networks)
Header
Data
Trailer (sometimes)

## Slide 44: Packet Switching
Node in a packet switching network
incoming links
outgoing links
Node
Memory

## Slide 45: Packet Switching: Multiplexing/Demultiplexing
How to tell packets apart?
  Use meta-data (header) to describe data
No reserved resources; dynamic sharing
  Single flow can use the entire link capacity if it is alone
  This leads to increased efficiency

## Slide 46: Taxonomy of Communication Networks
Communication networks can be classified based on the way in which the nodes exchange information:
Communication Network
Switched Communication Network
Broadcast Communication Network
Circuit-Switched Communication Network
Packet-Switched Communication Network
Datagram Network

## Slide 47: Datagram Packet Switching
Each packet is independently switched
  Each packet header contains full destination address
  Routers/switches make independent routing decisions
No resources are pre-allocated (reserved) in advance
Leverages “statistical multiplexing”
  Gambling that packets from different conversations won’t all arrive at the same time, so we don’t need enough capacity for all of them at their peak transmission rate
  Assuming independence of traffic sources, can compute probability that there is enough capacity

## Slide 48: Datagram Packet Switching
Host A
Host B
Host E
Host D
Host C
Node 1
Node 2
Node 3
Node 4
Node 5
Node 6
Node 7

## Slide 49: Datagram Packet Switching
Host A
Host B
Host E
Host D
Host C
Node 1
Node 2
Node 3
Node 4
Node 5
Node 6
Node 7

## Slide 50: Datagram Packet Switching
Host A
Host B
Host E
Host D
Host C
Node 1
Node 2
Node 3
Node 4
Node 5
Node 6
Node 7

## Slide 51: Taxonomy of Communication Networks
Communication networks can be classified based on the way in which the nodes exchange information:
Communication Network
Switched Communication Network
Broadcast Communication Network
Circuit-Switched Communication Network
Packet-Switched Communication Network
Datagram Network
Virtual Circuit Network
A hybrid of circuits and packets; headers include a “circuit identifier” established during a setup phase

## Slide 52: 5 Minute Break
Questions Before We Proceed?

## Slide 53: Basics of Datagram Networks

## Slide 54: Nodes and Links
Link: transmission technology
  Twisted pair, optical, radio, whatever
Node: computational devices on end of links
  Host: general-purpose computer
  Network node: switch or router
Node
Node
Link

## Slide 55: Properties of Links
Latency (delay)
  Propagation time for data sent along the link
  Corresponds to the “length” of the link
Bandwidth (capacity)
  Amount of data sent (or received) per unit time
  Corresponds to the “width” of the link
Bandwidth-delay product: (BDP)
  Amount of data that can be “in flight” at any time
  Propagation delay × bits/time = total bits in link
bandwidth
latency
delay x bandwidth

## Slide 56: Examples of Bandwidth-Delay
Same city over slow link:
  B~100mbps
  L~.1msec
  BDP ~ 10000bits ~ 1.25MBytes
Cross-country over fast link:
  B~10Gbps
  L~10msec
  BDP ~ 108bits ~ 12.5GBytes

## Slide 57: Examples of Transmission Times
1500 byte packet over 14.4k modem: ~1 sec
1500 byte packet over 10Gbps link: ~10-6sec

## Slide 58: Utilization
Fraction of time link is busy transmitting
  Often denoted by ρ
Ratio of arrival rate to bandwidth
  Arrival: A bits/sec on average
  Utilization = A/B = Arrival/Bandwidth

## Slide 59: Packets
Payload (Body)
  Data being transferred
Header
  Instructions to the network for how to handle packet
  Think of the header as an interface!

## Slide 60: The Lifecycle of Packets
Excess Packets
Stored in Buffer
Packet Arriving
at Switch
Packet
Being
Transmitted
Packet Buffer
Link
Packet Currently
Being Transmitted

## Slide 61: The Delays of Their Lives
Queueing
Delay
Transmission
Delay
Propagation Delay is how long it takes
to reach the next switch after transmission
Round-Trip Time (RTT) is the time it takes
a packet to reach the destination and
the response to return to the sender

## Slide 62: Timing of Datagram Packet Switching
Packet 1
Host 1
Host 2
Node 1
Node 2
propagation
delay between
Host 1 and
Node 1

## Slide 63: Timing of Datagram Packet Switching
Packet 1
Host 1
Host 2
Node 1
Node 2
propagation
delay between
Host 1 and
Node 1
transmission
time of Packet 1
at Host 1

## Slide 64: Timing of Datagram Packet Switching
Packet 1
Packet 1
Packet 1
processing delay of Packet 1 at Node 2
Host 1
Host 2
Node 1
Node 2
propagation
delay between
Host 1 and
Node 1
transmission
time of Packet 1
at Host 1

## Slide 65: Timing of Datagram Packet Switching
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
processing delay of Packet 1 at Node 2
Host 1
Host 2
Node 1
Node 2
propagation
delay between
Host 1 and
Node 1
transmission
time of Packet 1
at Host 1

## Slide 66: Review of Networking Delays
Propagation delay: latency
  Time spent in traversing the link
  “speed of propagation” delay
Transmission delay:
  Time spent being transmitted
  Ratio of packet size to bandwidth
Queueing delay:
  Time spent waiting in queue
  Ratio of total packet bits ahead in queue to bandwidth
Roundtrip delay (RTT)
  Total time for a packet to reach destination and a response to return to the sender

## Slide 67: Trends
Propagation delay?
  No change
Transmission delay?
  Getting smaller!
Queueing delay?
  Usually smaller
How does this affect applications?
  CDNs work very hard to move data near clients
  Reduces backbone bandwidth requirements
  But also decreases latency
  Google: time is money!

## Slide 68: Queueing Delay
Does not happen if packets are evenly spaced
  And arrival rate is less than service rate

## Slide 69: Smooth Arrivals = No Queueing Delays

## Slide 70: Queueing Delay
Does not happen if packets are evenly spaced
  And arrival rate is less than service rate
Queueing delay caused by “packet interference”
  Burstiness of arrival schedule
  Variations in packet lengths

## Slide 71: Bursty Arrivals = Queueing Delays
There is substantial queueing delay even though link is underutilized

## Slide 72: Queueing Delay Review
Does not happen if packets are evenly spaced
  And arrival rate is less than service rate
Queueing delay caused by “packet interference”
  Burstiness of arrival schedule
  Variations in packet lengths
Made worse at high load
  Less “idle time” to absorb bursts
  Think about traffic jams in rush hour….

## Slide 73: Jitter
Difference between minimum and maximal delay
Latency plays no role in jitter
  Nor does transmission delay for same sized packets
Jitter typically just differences in queueing delay
Why might an application care about jitter?

## Slide 74: Packet Losses: Buffers Full

## Slide 75: Packet Losses: Corruption

## Slide 76: Basic Queueing Theory Terminology
Arrival process: how packets arrive
  Average rate A
  Peak rate P
Service process: transmission times
  Average transmission time
  For networks, function of packet size
W: average time packets wait in the queue
  W for “waiting time”
L: average number of packets waiting in the queue
  L for “length of queue”
Two different quantities

## Slide 77: Little’s Law (1961)
L = A x W
Compute L: count packets in queue every second
  How often does a single packet get counted? W times
Could compute L differently
  On average, every packet will be counted W times
  The average arrival rate determines how frequently this total queue occupancy should be added to the total
Why do you care?
  Easy to compute L, harder to compute W
Notes: Row vs column

## Slide 78: Statistical Multiplexing

## Slide 79: Three Flows with Bursty Arrivals
Chart: 
Series 3 | 0 | 0 | 0 | 0 | 0 | 0 | 25 | 25
Chart: 
Series 1 | 25 | 25 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
Series 2 | 0 | 0 | 0 | 25 | 25 | 0 | 0 | 0
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Capacity

## Slide 80: When Each Flow Gets 1/3rd of Capacity
Chart: 
Series 3 | 0 | 0 | 0 | 0 | 0 | 0 | 25 | 25
Chart: 
Series 1 | 25 | 25 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
Series 2 | 0 | 0 | 0 | 25 | 25 | 0 | 0 | 0
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Frequent Overloading

## Slide 81: When Flows Share Total Capacity
Chart: 
Series 2 | 0 | 0 | 0 | 25 | 25 | 0 | 0 | 0
Chart: 
Series 3 | 0 | 0 | 0 | 0 | 0 | 0 | 25 | 25
Time
Time
Time
Chart: 
Series 1 | 25 | 25 | 0 | 0 | 0 | 0 | 0 | 0
No Overloading
Statistical multiplexing relies on the assumption
that not all flows burst at the same time.
Very similar to insurance, and has same failure case

## Slide 82: Classroom Demonstration of Stat Mux

## Slide 83: I need 8 volunteers!
One group of 4:
  Each generates either 0, 1, or 2 packets per cycle
  But your link only handles 1 packet per cycle
  How much of your link do you use (on average)?
Other group of 4:
  Each generates either 0, 1, or 2 packets per cycle
  You share your links, so you can handle 4 packets/cycle
  How much of your combined link do you use (average)?
Which team will win?

## Slide 84: Another Take on “Stat Mux”
Assume time divided into frames
  Frames divided into slots
Flows generate packets during each frame
  Peak number of packets/frame P
  Average number of packets/frame A
Single flow: must allocate P slots to avoid drops
  But P might be much bigger than A
  Very wasteful!
Use the “Law of Large Numbers”….
Frame
Slots

## Slide 85: Law of Large Numbers (~1713)
Consider any probability distribution
  Can be highly variable, such as varying from 0 to P
Take N samples from probability distribution
  In this case, one set of packets from each flow
Thm: the sum of the samples is very close to N×A
  And gets percentage-wise closer as N increases
Sharing between many flows (high aggregation), means that you only need to allocate slightly more than average A slots per frame.
  Sharing smooths out variations

## Slide 86: Simple Example: M/M/1 Queue
Consider n flows sharing a single queue
Flow: random (Poisson) arrivals at rate l
Random (Exponential) service with average 1/m
Utilization factor: r = nl/m
  If r >1, system is unstable
Case 1: Flows share bandwidth
  Delay = 1/( - n)
Case 2: Flows each have 1/nth share of bandwidth
  No sharing
  Delay = n/( - n) Not sharing increases delay by n

## Slide 87: If you still don’t understand stat mux
Will cover in section….

## Slide 88: Recurrent theme in computer science
Greater efficiency through “sharing”
  Statistical multiplexing
Phone network rather than dedicated lines
  Ancient history
Packet switching rather than circuits
  Today’s lecture
Cloud computing
  Shared datacenters, rather than single PCs

## Slide 89: General Lesson: scaling involves
How you share resources
How you deal with failures
…..

## Slide 90: Thursday’s lecture….
Layering, principles, the “good stuff”
Read K&R 1.4-1.8 (mostly for context)