## Slide 1: Internet History
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 2: Administrivia
Keep those questions coming!
  But will take a while for me to calibrate length of lectures
Questions about switching sections?
  Email Kay keo@eecs.berkeley.edu, cc me.
Check your bspace email address!
  Make sure it is an account you check
  If you miss a future bspace message, it is your fault
Everyone should be on Piazza now
  Again, we now view Piazza communications as reliable

## Slide 3: Outline for Today
Finishing up queueing
Statistical Multiplexing
Why did we choose packet-switching?
Internet history
Internet design goals
Protocols, Clients and Servers,….

## Slide 4: Finishing Up Queueing Delays

## Slide 5: Smooth Arrivals = No Queueing Delays

## Slide 6: Bursty Arrivals = Queueing Delays
There is substantial queueing delay even though link is underutilized

## Slide 7: Queueing Delay Review
Does not happen if packets are evenly spaced
  And arrival rate is less than service rate
Queueing delay caused by “packet interference”
  Burstiness of arrival schedule
  Variations in packet lengths
Made worse at high load
  Less “idle time” to absorb bursts
  Think about traffic jams in rush hour….

## Slide 8: Jitter
Difference between minimum and maximal delay
Latency (propagation delay) plays no role in jitter
  Nor does transmission delay for same sized packets
Jitter typically just differences in queueing delay
Why might an application care about jitter?

## Slide 9: Packet Losses
Packets can be “dropped” or lost
How?

## Slide 10: Packet Losses: Buffers Full

## Slide 11: Packet Losses: Corruption

## Slide 12: Packet Losses
Where should packet corruption be detected?
  In network?
  At host?
Other ways packets can be lost?
  TTL!

## Slide 13: Basic Queueing Theory Terminology
Arrival process: how packets arrive
  Average rate A
  Peak rate P
Service process: transmission times
  Average transmission time
  For networks, function of packet size
W: average time packets wait in the queue
  W for “waiting time”
L: average number of packets waiting in the queue
  L for “length of queue”
Two different quantities

## Slide 14: Little’s Law (1961)
L = A x W
Compute L: count packets in queue every second
  This is the straightforward approach, easy to compute
How often does a packet get counted? W times
  The average arrival rate determines how frequently this total queue occupancy should be added to the total
Why do you care?
  Easy to compute L, harder to compute W
  But W is what applications notice, so that’s what we want
Notes: Row vs column

## Slide 15: Statistical Multiplexing

## Slide 16: Three Flows with Bursty Arrivals
Chart: 
Series 3 | 0 | 0 | 0 | 0 | 0 | 0 | 25 | 25
Chart: 
Series 1 | 25 | 25 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
Series 2 | 0 | 0 | 0 | 25 | 25 | 0 | 0 | 0
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Capacity

## Slide 17: When Each Flow Gets 1/3rd of Capacity
Chart: 
Series 3 | 0 | 0 | 0 | 0 | 0 | 0 | 25 | 25
Chart: 
Series 1 | 25 | 25 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
Series 2 | 0 | 0 | 0 | 25 | 25 | 0 | 0 | 0
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Frequent Overloading

## Slide 18: When Flows Share Total Capacity
Chart: 
Series 2 | 0 | 0 | 0 | 25 | 25 | 0 | 0 | 0
Chart: 
Series 3 | 0 | 0 | 0 | 0 | 0 | 0 | 25 | 25
Time
Time
Time
Chart: 
Series 1 | 25 | 25 | 0 | 0 | 0 | 0 | 0 | 0
No Overloading
Statistical multiplexing relies on the assumption
that not all flows burst at the same time.
Very similar to insurance, and has same failure case

## Slide 19: Improved Delays: M/M/1 Queue
Consider n flows sharing a single queue
Flow: random (Poisson) arrivals at rate l
Random (Exponential) service with average 1/m
Utilization factor: r = nl/m
  If r >1, system is unstable
Case 1: Flows share bandwidth
  Delay = 1/( - n)
Case 2: Flows each have 1/nth share of bandwidth
  No sharing
  Delay = n/( - n) Not sharing increases delay by n

## Slide 20: If you still don’t understand stat mux
Will cover in section….
Will not be tested on M/M/1 content
  This is just for “fun”

## Slide 21: Recurrent theme in computer science
Greater efficiency through “sharing”
  Statistical multiplexing
Phone network rather than dedicated lines
  Ancient history
Packet switching rather than circuits
  Last lecture
Cloud computing
  Shared datacenters, rather than single PCs

## Slide 22: Choosing a Network Design

## Slide 23: If you were building a network….
Which would you choose?
  Circuit switched?
  Packet-switched (Datagram)?
Let’s review the strengths and weaknesses

## Slide 24: Advantages of Circuit Switching
Guaranteed bandwidth
  Predictable communication performance
Simple abstraction
  Reliable communication channel between hosts
  No worries about lost or out-of-order packets
Simple forwarding
  Forwarding based on time slot or frequency
  No need to inspect a packet header

## Slide 25: Disadvantages of Circuit-Switching
Wasted bandwidth
  Bursty traffic leads to idle connection during silent period
Blocked connections
  Connection refused when resources are not sufficient
  Unable to offer “okay” service to everybody
Network state
  Network nodes must store per-connection information
  This makes failures more disruptive!

## Slide 26: Disadvantages of Datagram
Worse service for flows
  No promises made about delays, just “best effort”
  Packets might be dropped or delivered out of order
  End hosts must cope with out-of-order packets
Must deal with congestion
  Without reserved resources, must cope with overloads
  Overloads can result in bad service for flows
More complicated forwarding
  Per-packet lookups, etc.

## Slide 27: Advantages of Datagram
Recovery from failures
  Routers don’t know about individual flows, so it is easy to fail over to a different path
Efficiency
  Exploits of statistical multiplexing
Deployability
  Easier for different parties to link their networks together because they are not promising to reserve resources for one another

## Slide 28: Choosing a Design for the Internet
Which would you choose? And why?

## Slide 29: The paradox of the Internet’s design
As we will discuss later, one of the main design goals is to support a wide range of apps
These applications have different requirements
Shouldn’t the Internet support them all?

## Slide 30: Diversity of application requirements
Size of transfers
Bidirectionality (or not)
Delay sensitive (or not)
Tolerance of jitter (or not)
Tolerance of packet drop (or not)
Need for reliability (or not)
Multipoint (or not)
…..

## Slide 31: Diversity of application requirements
Size of transfers
Bidirectionality (or not)
Delay sensitive (or not)
Tolerance of jitter (or not)
Tolerance of packet drop (or not)
Need for reliability (or not)
Multipoint (or not)
…..

## Slide 32: What service should Internet support?
Strict delay bounds?
  Some applications require them
Guaranteed delivery?
  Some applications are sensitive to packet drops
No applications mind getting good service
  Why not require Internet support these guarantees?

## Slide 33: Important life lessons
People (applications) don’t always need what they think they need
People (applications) don’t always need what we think they need
Flexibility often more important than performance
  But typically only in hindsight!
  Example: cell phones vs landlines
Architect for flexibility, engineer for performance

## Slide 34: Applying lessons to Internet
Requiring performance guarantees would limit variety of networks that could attach to Internet
Many applications don’t need these guarantees
And those that do?
  Well, they don’t either (usually)
  Tremendous ability to mask drops, delays
And ISPs can work hard to deliver good service without changing the architecture (engineering)
If the Internet had focused on voice applications early, it might have made different choices

## Slide 35: Bottom Line
The choice of datagram service is not as obvious as it might seem today
Great vision on the part of the Internet designers
And lucky that they were focused on applications that did not need great service

## Slide 36: 5 Minute Break
Questions Before We Proceed?

## Slide 37: Internet History

## Slide 38: Timeline
1961 Baran and Kleinrock advocate packet switching
1962 Licklider’s vision of Galactic Network
1965 Roberts connects two computers via phone
1967 Roberts publishes vision of ARPANET
BBN installs first IMP at UCLA
  IMP: Interface Message Processor
1971 Network Control Program (protocol)
1972 Public demonstration of ARPANET

## Slide 39: The beginning of the Internet revolution
Kleinrock’s group at UCLA tried to log on to Stanford computer: His recollection of the event…
We typed the L…
  “Do you see the L?”
  “Yes, we see the L.”
We typed the O…
  “Do you see the O?”
  “Yes, we see the O.”
Then we typed the G…
  …and the system crashed!

## Slide 40: Timeline continued…
Email invented
1972 Telnet introduced
1972 Kahn advocates Open Architecture networking

## Slide 41: The Problem
Many different packet-switching networks
Only nodes on the same network could communicate

## Slide 42: Kahn’s Rules for Interconnection
Each network is independent and must not be required to change (why?)
Best-effort communication (why?)
Boxes (routers) connect networks
No global control at operations level (why?)

## Slide 43: Solution
Gateways

## Slide 44: Kahn’s vision
Kahn imagined there would be only a few networks (~20) and thus only a few routers
He was wrong
  Why?
Imagined gateways would “translate” between networks
  We think of it as all routers supporting IP

## Slide 45: Timeline continued….
1973 FTP introduced
1974 Cerf and Kahn paper on TCP/IP
1980 TCP/IP adopted as defense standard
1983 Global NCP to TCP/IP flag day
198x XNS, DECbit, and other protocols
1984 Janet (British research network)
1985 NSFnet (picks TCP/IP)
198x Internet meltdowns due to congestion
1986 Van Jacobson saves the Internet (BSD TCP)

## Slide 46: Unsung hero of Internet: David D. Clark
Chief Architect 1981-1988
Great consistency of vision
Kept the Internet true to its basic design principles
Authored what became known as the End-to-end principle (next lecture)
Conceives and articulates architectural concepts
  Read his “Active Networking and End-To-End Arguments”
Perhaps the only “irreplaceable” Internet pioneer

## Slide 47: Timeline continued…
Deering and Cheriton propose multicast
Birth of the web….Tim Berners-Lee

## Slide 48: Why did it take physicist to invent web?
Physicists are the smartest people in the world?
Computer scientists were trying to invent nirvana
  Well, actually Xanadu (Ted Nelson)
  More generally, CS researchers focused on hyptertext
Again, users didn’t need what we wanted to invent
  Think about it: a paper on the web design would have been rejected by every CS conference and journal
In general, the CS research community is great at solving well-defined problems, but terrible at guessing what users will actually use
  “Academics get paid for being clever, not for being right.”
  …Don Norman

## Slide 49: Timeline continued…..
1993 Search engines invented (Excite)
199x ATM rises and falls (as internetworking layer)
199x QoS rises and falls
1994 Internet goes commercial
IPv6 specification
1998 Google reinvents search
200x The Internet boom and bust
2012 EE122 enrollment suggests boom is back!
~80 in 2010 to ~200 in 2011 to ~340 in 2012