## Slide 1: Internet Design: Goals and Principles
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 2: Administrivia
New Office Hours:
  Thursday 12:00-1:00 in 415 or 420 (come find me!)
  After class on Tuesdays: walk with me to Soda
Class going more slowly than anticipated
  Will pivot to real material, skipping some nonessentials
Lecture on September 18
  Will be returning from Moscow that day
Homework #1 released (note submission process)
  Due in two weeks….this should not be hard
  Project #1 will follow shortly
  Guesses about dates for future assignments now online

## Slide 3: Outline
Design Goals
Modularity
Layering
End-to-End Principle
Fate-Sharing

## Slide 4: Internet Design Goals

## Slide 5: David Clark
Wrote a paper in 1988 that tried to capture why the Internet turned out as it did
In particular, it described an ordered list of priorities that informed the design
We have him with us here today….Eastwood-style

## Slide 6: Internet Design Goals (Clark ‘88)
Connect existing networks
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability

## Slide 7: Connect Existing Networks
Wanted single protocol that could be used to connect any pair of (existing) networks
The Internet Protocol (IP) is that unifying protocol
  All (existing) networks must be able to implement it
This is where the need for best effort arose….

## Slide 8: Robust
As long as network is not partitioned, two hosts should be able to communicate (eventually)
Failures (excepting network partition) should not interfere with endpoint semantics
Very successful, not clear how relevant now
  Availability more important than recovering from disaster
Second notion of robustness is underappreciated
  Key to modularity of Internet

## Slide 9: Types of Delivery Services
Use of the term “delivery services” already implied an application-neutral network
Built lowest common denominator service
  Allow end-based protocols to provide better service
  For instance, turn unreliable service into reliable service
Example: recognition that TCP wasn’t needed (or wanted) by some applications
  Separated TCP from IP, and introduced UDP

## Slide 10: Variety of Networks
Incredibly successful!
  Minimal requirements on networks
  No need for reliability, in-order, fixed size packets, etc.
  A result of aiming for lowest common denominator
IP over everything
  Then: ARPANET, X.25, DARPA satellite network..
  Now: ATM, SONET, WDM…

## Slide 11: Decentralized Management
Both a curse and a blessing
  Important for easy deployment
  Makes management hard today

## Slide 12: Host Attachment
Clark observes that cost of host attachment may be higher because hosts have to be smart
But the administrative cost of adding hosts is very low, which is probably more important
  Plug-and-play kind of behavior….

## Slide 13: Cost Effective
Cheaper than circuit switching at low end
More expensive than circuit switching at high end
Not a bad compromise:
  Cheap where it counts (low-end)
  More expensive for those who can pay….

## Slide 14: Resource Accountability
Failure!

## Slide 15: Internet Motto
We reject kings, presidents, and voting. We believe in rough consensus and running code.”
David Clark

## Slide 16: Real Goals
Build something that works!
Connect existing networks
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability

## Slide 17: Questions to think about….
What priorities would a commercial design have?
What would the resulting design look like?
What goals are missing from this list?
Notes: Missing: resource sharing, other considerations of malicious users (traceback, etc.), address concerns of administrative domains visible

## Slide 18: Modularity

## Slide 19: Modularity in Computer Science
“Modularity based on abstraction is the way things get done”
--Barbara Liskov

## Slide 20: The Role of Modularity
We can’t build big systems out of spaghetti code
  Impossible to understand, debug
  Hard to update
We need to limit the scope of changes, so that we can update system without rewriting it from scratch
Modularity is how we limit the scope of changes
  And understand the system at a higher level

## Slide 21: Computer System Modularity
Partition system into modules
  Each module has well-defined interface
Interfaces give flexibility in implementation
  Changes have limited scope
Examples:
  Libraries encapsulating set of functionality
  Programming language abstracts away CPU
The trick is to find the right modularity
  The interfaces should be long-lasting
  If interfaces are changing often, modularity is wrong

## Slide 22: Finding the Right Modularity
Decompose problem into tasks or abstractions
  Task: e.g., compute a function
  Abstraction: e.g., provide reliable storage
Define a module for each task/abstraction
  Involves defining a clean interface for each module
  “Clean” means hiding unnecessary details
Implement system a few times:
  If interfaces seem to hold, you are on the right track…

## Slide 23: Network System Modularity
The need for modularity still applies
  And is even more important! (why?)
Network implementations not just distributed across many lines of code
  Normal modularity “organizes” that code
Networking is distributed across many machines
  Hosts
  Routers

## Slide 24: Network Modularity Decisions
How to break system into modules?
  Classic decomposition into tasks
Where are modules implemented?
  Hosts?
  Routers?
  Both?
Where is state stored?
  Hosts?
  Routers?
  Both?

## Slide 25: Leads to three design principles
How to break system into modules?
  Layering
Where are modules implemented?
  End-to-End Principle
Where is state stored?
  Fate-Sharing

## Slide 26: Layering

## Slide 27: Tasks in Networking
What does it take to send packets across country?
Simplistic decomposition:
  Task 1: send along a single wire
  Task 2: stitch these together to go across country
This gives idea of what I mean by decomposition
  Next slide presents a much more detailed version

## Slide 28: Tasks in Networking (bottom up)
Electrons on wire
Bits on wire
Packets on wire
Deliver packets across local network
  Local addresses
Deliver packets across country
  Global addresses
Ensure that packets get there
Do something with the data
Notes: Note thatfirst three are making unit of delivery bigger, next two go from wire to global.

## Slide 29: Resulting Modules (layers)
Electrons on wire (contained in next layer)
Bits on wire (Physical)
Packets on wire (contained in next layer)
Deliver packets across local network (Datalink)
  Local addresses
Deliver packets across country (Network)
  Global addresses
Ensure that packets get there (Transport)
Do something with the data (Application)

## Slide 30: Five Layers (top-down)
Application: Providing network support for apps
Transport (L4): (Reliable) end-to-end delivery
Network (L3): Global best-effort delivery
Datalink (L2): Local best-effort delivery
Physical: Bits on wire
Interactions between these components?
  Do all components talk to each other?
  Or are the components limited in their interactions?
Answer: they are strictly layered!

## Slide 31: Strictly Layered Dependencies
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits

## Slide 32: Three Observations
Each layer:
  Depends on layer below
  Supports layer above
  Independent of others
Multiple versions in layer
  Interfaces differ somewhat
  Components pick which lower-level protocol to use
But only one IP layer
  Unifying protocol

## Slide 33: Layering Crucial to Internet’s Success
Innovation at most levels
  Applications (lots)
  Transport (few)
  Datalink (few)
  Physical (lots)
Innovation proceeded largely in parallel
Pursued by very different communities
  Like PL and chip designs

## Slide 34: Distributing Layers Across Network
Layers are simple if only on a single machine
  Just stack of modules interacting with those above/below
But we need to implement layers across machines
  Hosts
  Routers (switches)
What gets implemented where?

## Slide 35: What Gets Implemented on Host?
Bits arrive on wire, must make it up to application
Therefore, all layers must exist at host!

## Slide 36: What Gets Implemented on Router?
Bits arrive on wire
  Physical layer necessary
Packets must be delivered to next-hop
  Datalink layer necessary
Routers participate in global delivery
  Network layer necessary
Routers don’t support reliable delivery
  Transport layer (and above) not supported

## Slide 37: What Gets Implemented on Switches?
Switches do what routers do, except they don’t participate in global delivery, just local delivery
They only need to support Physical and Datalink
  Don’t need to support Network layer
Won’t focus on the router/switch distinction
  When I say switch, I almost always mean router
  Almost all boxes support network layer these days

## Slide 38: Complicated Diagram
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 39: Simple Diagram
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
Notes: Why go up? Why not stay down in the lower levels?

## Slide 40: Logical Communication
Layers interacts with peer’s corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 41: Physical Communication
Communication goes down to physical network
Then from network peer to peer
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 42: Layer Encapsulation
Trans: Connection ID
Net: Source/Dest
Link: Src/Dest
Appl: Get index.html
User A
User B
Common case: 20 bytes TCP header + 20 bytes IP header + 14 bytes Ethernet header = 54 bytes overhead
Notes: Deepest level most header

## Slide 43: Example of Layering in the Real World
Dear John,
Your days are numbered.
--Pat
CEO A writes letter to CEO B
  Folds letter and hands it to administrative aide
Aide:
  Puts letter in envelope with CEO B’s full name
  Takes to FedEx
FedEx Office
  Puts letter in larger envelope
  Puts name and street address on FedEx envelope
  Puts package on FedEx delivery truck
FedEx delivers to other company

## Slide 44: The Path of the Letter
CEO
Aide
FedEx
CEO
Aide
FedEx
Location
Fedex Envelope (FE)
Letter
Envelope
Semantic Content
Identity
“Peers” on each side understand the same things
No one else needs to
Lowest level has most packaging

## Slide 45: The Path Through FedEx
Truck
Sorting
Office
Airport
FE
Sorting
Office
Airport
Truck
Sorting
Office
Airport
Crate
Crate
FE
New
Crate
Crate
FE
Higher “Stack”
at Ends
Partial “Stack”
During Transit
Deepest Packaging (Envelope+FE+Crate)
at the Lowest Level of Transport
Highest Level of
“Transit Stack”
is Routing

## Slide 46: Back to Networking Picture
Communication goes down to physical network
Then from network peer to peer
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 47: Back to Encapsulation (Headers)
Trans: Connection ID
Net: Source/Dest
Link: Src/Dest
Appl: Get index.html
User A
User B
Common case: 20 bytes TCP header + 20 bytes IP header + 14 bytes Ethernet header = 54 bytes overhead
Notes: Deepest level most header

## Slide 48: Five Minute Break….

## Slide 49: Three Internet Design Principles
How to break system into modules?
  Layering
Where are modules implemented?
  End-to-End Principle
Where is state stored?
  Fate-Sharing

## Slide 50: The End-to-End Principle
Everyone believes it, but no one knows what it means…..

## Slide 51: Placing Network Functionality
Influential paper: “End-to-End Arguments in System Design” by Saltzer, Reed, and Clark (‘84)
  End-to-end principle
Basic observation: some types of network functionality can only be correctly implemented end-to-end
In these cases, end hosts:
  Can satisfy the requirement without network’s help
  Must do so, since can’t rely on network’s help
Thus, don’t need to implement them in network
  Debate about what the network does and doesn’t do…
Notes: Contrary to wisdom of the day!
Talmud

## Slide 52: Example: Reliable File Transfer
Solution 1: make each step reliable, and string them together to make reliable end-to-end process
Solution 2: allow steps to be unreliable, but do end-to-end check and try again if necessary
OS
Appl.
OS
Appl.
Host A
Host B
OK

## Slide 53: Discussion
Solution 1 cannot be made perfectly reliable
  What happens if a network element misbehaves?
  Receiver has to do the check anyway!
Solution 2 can also fail, but only if the end system itself fails (i.e., doesn’t follow its own protocol)
Solution 2 only relies on what it can control
  The endpoint behavior
Solution 1 requires endpoints trust other elements
  That’s not what reliable means!

## Slide 54: Robust (From Clark’s Paper)
As long as the network is not partitioned, two endpoints should be able to communicate
Failures (excepting network partition) should not interfere with endpoint semantics

## Slide 55: Question?
Should you ever implement reliability in network?
Perhaps, if needed for reasonable efficiency
  Don’t aim for perfect reliability, but ok to reduce error rate
If individual links fail 10% of the time, and are traversing 10 links, then E2E error rate is 65%
Implementing one retransmission on links
  Link error rate reduced to 1%, E2E error rate is 9.5%

## Slide 56: Back to the End-to-End Principle
Implementing such functionality in the network:
Doesn’t reduce host implementation complexity
Does increase network complexity
Often imposes delay/overhead on all applications, even if they don’t need functionality
However, implementing in network can enhance performance in some cases
  E.g., very lossy link
Three interpretations of the end-to-end principle

## Slide 57: “Only-if-Sufficient” Interpretation
Don’t implement a function at the lower levels of the system unless it can be completely implemented at this level
Unless you can relieve the burden from hosts, don’t bother

## Slide 58: “Only-if-Necessary” Interpretation
Don’t implement anything in the network that can be implemented correctly by the hosts
  E.g., multicast
Make network layer absolutely minimal
  This E2E interpretation trumps performance issues
  Increases flexibility, since lower layers stay simple
Notes: One make hosts as simple as possible. The other makes the network as simple as possible. Which do you prefer?

## Slide 59: “Only-if-Useful” Interpretation
If hosts can implement functionality correctly, implement it in a lower layer only as a performance enhancement
But do so only if it does not impose burden on applications that do not require that functionality

## Slide 60: What Does E2E Principle Ignore?
There are other stakeholders besides users
  ISP might care about the good operation of their network
  Various commercial entities
  Money-chain might require insertion into the network
The need for middlebox functionality
  Some functions that, for management reasons, are more easily done in the network.

## Slide 61: Three Internet Design Principles
How to break system into modules?
  Layering
Where are modules implemented?
  End-to-End Principle
Where is state stored?
  Fate-Sharing

## Slide 62: Fate-Sharing

## Slide 63: Fate-Sharing
Note that E2E principles relied on “fate-sharing”
  Invariants break only when endpoints themselves break
  Minimize dependence on other network elements
This should dictate placement of storage

## Slide 64: General Principle: Fate-Sharing
When storing state in a distributed system, co-locate it with entities that rely on that state
Only way failure can cause loss of the critical state is if the entity that cares about it also fails ...
  … in which case it doesn’t matter
Often argues for keeping network state at end hosts rather than inside routers
  In keeping with End-to-End principle
  E.g., packet-switching rather than circuit-switching
  E.g., NFS file handles, HTTP “cookies”

## Slide 65: A Cynical View of Distributed Systems
“A distributed system is one in which the failure of a computer you didn't even know existed can render your own computer unusable”
  ---Leslie Lamport

## Slide 66: Decisions and Their Principles
How to break system into modules
  Dictated by Layering
Where modules are implemented
  Dictated by End-to-End Principle
Where state is stored
  Dictated by Fate-Sharing

## Slide 67: Question
If reliability is implemented by the ends, how is it done?
That’s the subject of the next lecture!