## Slide 1: More Routing
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 2: Let’s focus on clarifying questions
I love the degree of interaction in this year’s class
But there are many people who are confused
I’d like to give them the chance to ask about basics
So today, let’s give priority to questions of the form
  “I don’t understand X” or “how does that work?”
Ask speculative questions during or after break

## Slide 3: Warning….
This lecture contains detailed calculations
Prolonged exposure may induce drowsiness
To keep you awake I will be tossing beanbags
  Do not misplace them
  Do not read the sheet of paper attached
  If you’ve already participated, hand to nbr who hasn’t

## Slide 4: Logic Refresher
A if B means B  A
  if B is true, then A is true
A only if B means A  B
  if A is true, then B is true
A if and only if B means: A  B
  If A is true, then B is true
  If B is true, then A is true
To make the statement that A if and only if B, you must prove statements 1 and 2.

## Slide 5: Short Summary of Course
Architecture, layering, E2E principle, blah, blah,…
  How functionality is organized
There are only two important design challenges:
  Reliable Transport and Routing
Reliable Transport:
A transport mechanism is “reliable” if and only if it resends all dropped or corrupted packets
Routing:
  Global routing state is valid if and only if there are no dead ends (easy) and there are no loops (hard)

## Slide 6: 10 Years from Now….
If you remember nothing else from this course except this single slide, I’ll be very happy
If you don’t remember this slide, you have wasted your time…

## Slide 7: Previous Routing Lecture
We assume destination-based forwarding
The key challenge is to compute loop-free routes
This is easy when the topology is a tree
  Loops are impossible without reversing a packet
  Flooding always will find the destination
  Can use “learning” to reduce need for flooding
But this approach has serious disadvantages
  Can’t use entire network, must restrict to tree
  Does not react well to failures or host movement
  Universally hated by operators….

## Slide 8: Other Ways to Avoid Loops?
If I gave you a network graph, could you define loop-free paths to a given destination?
Simple algorithm:
  For given source, pick an arbitrary path that doesn’t loop
  For any node not on path, draw a path that does not contradict earlier path
  Continue until all nodes are covered
Can pick any spanning tree rooted at destination

## Slide 9: Example

## Slide 10: Loops are easy to avoid…
..if you have the whole graph
Centralized or pseudo-centralized computation
  Requirement: routes computed knowing global view
  One node can do calculation for everyone
  Or each node can do calculation for themselves
But question is: how do you construct global view?

## Slide 11: Link-State
Details in Section

## Slide 12: Link-State Routing Is Conceptually Simple
Each router keeps track of its incident links
Each router broadcasts the link state
  To give every router a complete view of the graph
Each router computes paths using same algorithm
Example protocols
  Open Shortest Path First (OSPF)
  Intermediate System – Intermediate System (IS-IS)
Challenges: scaling, transient disruptions

## Slide 13: Link State Routing
Each node floods its local information
Each node then knows entire network topology
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6

## Slide 14: Link State: Each Node Has Global View
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C

## Slide 15: How to Compute Routes
Each node should have same global view
They each compute their own routing tables
Using exactly the same algorithm
Can use any algorithm that avoids loops
Computing shortest paths is one such algorithm
  Associate “cost” with links, don’t worry what it means….
  Dijkstra’s algorithm is one way to compute shortest paths
We will review Dijkstra’s algorithm briefly
  But that’s just because it is expected from such courses
    Snore….

## Slide 16: “Least Cost” Routes
No sensible cost metric will be minimized by traversing a loop
“Least cost” routes an easy way to avoid loops
Least cost routes are also “destination-based”
  i.e., do not depend on the source
  Why is this?
Therefore, least-cost paths form a spanning tree

## Slide 17: Example
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 18: Dijkstra’s Shortest Path Algorithm
INPUT:
  Network topology (graph), with link costs
OUTPUT:
  Least cost paths from one node to all other nodes
  Produces “tree” of routes
    Different from what we talked about before
    Previous tree was rooted at destination
    This is rooted at source
    But shortest paths are reversible!
Warnings:
  There is a typo, but I don’t remember where (prize!)
  Most claim to know Dijkstra, but in practice they don’t
Notes: How many people know this algorithm?
Well, last year….

## Slide 19: Notation
c(i,j): link cost from node i to j; cost infinite if not direct neighbors; ≥ 0
D(v): current value of cost of path from source to destination v
p(v): predecessor node along path from source to v, that is next to v
S: set of nodes whose least cost path definitively known
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Source

## Slide 20: Dijkstra’s Algorithm
1 Initialization:
2 S = {A};
3 for all nodes v
4 if v adjacent to A
5 then D(v) = c(A,v);
6 else D(v) = ;
7
8 Loop
9 find w not in S such that D(w) is a minimum;
10 add w to S;
11 update D(v) for all v adjacent to w and not in S:
12 if D(w) + c(w,v) < D(v) then
// w gives us a shorter path to v than we’ve found so far
13 D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;
c(i,j): link cost from node i to j
D(v): current cost source  v
p(v): predecessor node along path from source to v, that is next to v
S: set of nodes whose least cost path definitively known

## Slide 21: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
start S
A
D(B),p(B)
2,A
D(C),p(C)
5,A
D(D),p(D)
1,A
D(E),p(E)
D(F),p(F)
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
1 Initialization:
2 S = {A};
3 for all nodes v
4 if v adjacent to A
5 then D(v) = c(A,v);
6 else D(v) = ;
…

## Slide 22: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
start S
A
D(B),p(B)
2,A
D(C),p(C)
5,A
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
D(D),p(D)
1,A
D(E),p(E)
D(F),p(F)

## Slide 23: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
start S
A
AD
D(B),p(B)
2,A
D(C),p(C)
5,A
D(D),p(D)
1,A
D(E),p(E)
D(F),p(F)
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 24: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
start S
A
AD
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 25: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
start S
A
AD
ADE
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 26: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
start S
A
AD
ADE
ADEB
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 27: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
start S
A
AD
ADE
ADEB
ADEBC
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 28: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
start S
A
AD
ADE
ADEB
ADEBC
ADEBCF
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 29: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
start S
A
AD
ADE
ADEB
ADEBC
ADEBCF
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
To determine path A  C (say), work backward from C via p(v)

## Slide 30: The Forwarding Table
Running Dijkstra at node A gives the shortest path from A to all destinations
We then construct the forwarding table
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Destination | Link
B | (A,B)
C | (A,D)
D | (A,D)
E | (A,D)
F | (A,D)
Notes: Separate routing and forwarding tables - not always the case. For efficiency, hardware implementation

## Slide 31: Complexity
How much processing does running the Dijkstra algorithm take?
Assume a network consisting of N nodes
  Each iteration: check all nodes w not in S
  N(N+1)/2 comparisons: O(N2)
  More efficient implementations: O(N log(N))

## Slide 32: Flooding the Topology Information
Each router sends information out its ports
The next node sends it out through all of its ports
  Except the one where the information arrived
  Need to remember previous msgs, suppress duplicates!
X
A
C
B
D
(a)
X
A
C
B
D
(b)
X
A
C
B
D
(c)
X
A
C
B
D
(d)

## Slide 33: Making Flooding Reliable
Reliable flooding
  Ensure all nodes receive link-state information
  Ensure all nodes use the latest version
Challenges
  Packet loss
  Out-of-order arrival
Solutions
  Acknowledgments and retransmissions
  Sequence numbers
How can it still fail?
Notes: When node goes down, it might take an update with it…..and then come back up and not remember it.

## Slide 34: When to Initiate Flood?
Topology change
  Link or node failure
  Link or node recovery
Configuration change
  Link cost change
  Potential problems with making cost dynamic!
Periodically
  Refresh the link-state information
  Typically (say) 30 minutes
  Corrects for possible corruption of the data

## Slide 35: Convergence
Getting consistent routing information to all nodes
  E.g., all nodes having the same link-state database
Forwarding is consistent after convergence
  All nodes have the same link-state database
  All nodes forward packets on same paths

## Slide 36: Convergence Delay
Time elapsed before every router has a consistent picture of the network
Sources of convergence delay
  Detection latency
  Flooding of link-state information
  Recomputation of forwarding tables
  Storing forwarding tables
Performance during convergence period
  Lost packets due to blackholes and TTL expiry
  Looping packets consuming resources
  Out-of-order packets reaching the destination
Very bad for VoIP, online gaming, and video

## Slide 37: Transient Disruptions
Inconsistent link-state database
  Some routers know about failure before others
  The shortest paths are no longer consistent
  Can cause transient forwarding loops
A
E
D
C
B
F
A
E
D
C
B
F
A and D think that this is the path to C
E thinks that this is the path to C
Loop!

## Slide 38: Reducing Convergence Delay
Faster detection
  Smaller “hello” timers
  Link-layer technologies that can detect failures
Faster flooding
  Flooding immediately
  Sending link-state packets with high-priority
Faster computation
  Faster processors on the routers
  Incremental Dijkstra algorithm
Faster forwarding-table update
  Data structures supporting incremental updates

## Slide 39: Scaling Link-State Routing
Overhead of link-state routing
  Flooding link-state packets throughout the network
  Running Dijkstra’s shortest-path algorithm
  Becomes unscalable when 100s of routers
Introducing hierarchy through “areas”
Area 0
Area 1
Area 2
Area 3
Area 4
area
border
router

## Slide 40: What about other approaches?
Link-state is essentially a centralized computation:
  Global state, local computation
What about a more distributed approach?
  Local state, global computation

## Slide 41: Learn-By-Doing
I need 40 volunteers
If you haven’t participated, this is your chance!

## Slide 42: The Task
Remove sheet of paper from beanbag, but do not look at sheet of paper until I say so
You will have five minutes to complete this task
Each sheet says:
You are node X You are connected to nodes Y,Z
Your job: find route from source (node 1) to destination (node 40) in five minutes

## Slide 43: Ground Rules
You may not:
  Leave your seat (but you can stand)
  Pass your sheet of paper
  Let anyone copy your sheet of paper
You may:
  Ask nearby friends for advice
  Shout to other participants (anything you want)
  Curse your instructor (sotto voce)
You must: Try

## Slide 44: Go!

## Slide 45
1
16
36
7
25
10
19
5
34
38
29
33
15
39
23
14
9
2
35
11
22
32
26
21
37
3
28
12
30
4
27
20
31
18
24
40
8
17
6
13

## Slide 46: Distance-Vector
Details in Section

## Slide 47: Distributed Computation of Routes
More scalable than Link-State
  No global flooding
Each node computing the outgoing port based on:
  Local information (who it is connected to)
  Paths advertised by neighbors
Algorithms differ in what these exchanges contain
  Distance-vector: just the distance to each destination
  Path-vector: the entire path to each destination
We will focus on distance-vector for now

## Slide 48: Example of Distributed Computation
I am one hop away
I am one hop away
I am one hop away
I am two hops away
I am two hops away
I am two hops away
I am two hops away
I am three hops away
I am three hops away
Destination
I am three hops away

## Slide 49: This is what you could have done
Destination stands up
Announces neighbors
  They stand up
They announce their neighbors
  They stand up (if they haven’t already done so)
  They remember who called them to stand
…..and so on, until source stands
Key point: don’t stand up twice!
Notes: Let’s try this again!!!

## Slide 50: Step 1
Destination stands up

## Slide 51: Step 1

## Slide 52: Step 2
Destination stands up
Announces neighbors
  They stand up

## Slide 53: Step 2
I am one hop away
I am one hop away
I am one hop away

## Slide 54: Step 3
Destination stands up
Announces neighbors
  They stand up
They announce their neighbors
  They stand up

## Slide 55: Step 3
I am two hops away
I am two hops away
I am two hops away
I am two hops away

## Slide 56: Why Not Stand Up Twice?
Being called a second time means that there is a second (and longer) path to you
  You already contacted your neighbors the first time
  Your distance to destination is based on shorter path

## Slide 57: Congratulations!
You have “implemented” Distance-Vector routing
  For a single destination
  With the slowest code possible
OK, so now let’s consider this more generally….

## Slide 58: Routing “Metrics”
Algorithm finds path with smallest hop-count
  More complicated if you route with a different metric
Other routing goals (besides hop-count)
  Path with highest capacity
  Path with lowest latency
  Path with most reliable links
  ….
Generally, assume every link has “cost” or weight associated with it, and you want to minimize cost

## Slide 59: Distance Vector Routing
Each router knows the links to its neighbors
  Does not flood this information to the whole network
Each router has provisional “shortest path”
  E.g.: Router A: “I can get to router B with cost 11 via next hop router D”
Routers exchange this Distance-Vector information with their neighboring routers
  Vector because one entry per destination
Routers update their idea of the best path using info from neighbors
Iterative process converges to set of shortest paths

## Slide 60: Information Flow in Distance Vector
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6

## Slide 61: Information Flow in Distance Vector
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6

## Slide 62: Information Flow in Distance Vector
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6
Why is this different from flooding?