## Slide 1: Even More Routing
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 2: Questions about Project 1
Colin goes into cone of silence for next 30 hours
So ask your questions now!

## Slide 3: Today’s Lecture: A little of everything
Finishing up distance vector routing
  Last time we covered the good
  This time we cover the bad and the ugly
Covering some “missing pieces”
  Maybe networking isn’t as simple as I said….
Lots of details today…
  So I will go slowly and ask you to do the computations
  Will have you ask your neighbors if you can’t figure it out
    If they can’t figure it out, sit next to smarter people next time!

## Slide 4: Two Ways to Avoid Loops
Global state, local computation
  Link-state
  Broadcast local information, construct network map
Local state, global computation
  Distance-Vector
  Minimizing “cost” will produce loop-free routes
  Iterative computation: no one knows the topology

## Slide 5: Distance Vector Routing
Each router knows the links to its neighbors
  Does not flood this information to the whole network
Each router has provisional “shortest path”
  E.g.: Router A: “I can get to router B with cost 11”
Routers exchange this Distance-Vector information with their neighboring routers
  Vector because one entry per destination
  Why only advertise “best” path? Why not two best?
    Loops and lies….
Routers look over the set of options offered by their neighbors and select the best one
Iterative process converges to set of shortest paths

## Slide 6: Information Flow in Distance Vector
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6

## Slide 7: Bellman-Ford Algorithm
INPUT:
  Link costs to each neighbor
  Not full topology
OUTPUT:
  Next hop to each destination and the corresponding cost
  Does not give the complete path to the destination
My neighbors tell me how far they are from dest’n
  Compute: (cost to nhbr) plus (nhbr’s cost to destination)
  Pick minimum as my choice
  Advertise that cost to my neighbors

## Slide 8: Bellman-Ford Overview
Each router maintains a table
  Best known distance from X to Y,
  via Z as next hop = DZ(X,Y)
Each local iteration caused by:
  Local link cost change
  Message from neighbor
Notify neighbors only if least cost path to any destination changes
  Neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute distance table
if least cost path to any dest has changed, notify neighbors
Each node:
Notes: Note: for simplicity in this lecture examples we show only the shortest distances to each destination

## Slide 9: Bellman-Ford Overview
Each router maintains a table
  Row for each possible destination
  Column for each directly-attached neighbor to node
  Entry in row Y and column Z of node X  best known distance from X to Y, via Z as next hop = DZ(X,Y)
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 4 | 8
Node A
Neighbor
(next-hop)
Destinations
DC(A, D)
Notes: Note: for simplicity in this lecture examples we show only the shortest distances to each destination

## Slide 10: Bellman-Ford Overview
Each router maintains a table
  Row for each possible destination
  Column for each directly-attached neighbor to node
  Entry in row Y and column Z of node X  best known distance from X to Y, via Z as next hop = DZ(X,Y)
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 4 | 8
Node A
Smallest distance in row Y = shortest
Distance of A to Y, D(A, Y)
Notes: Note: for simplicity in this lecture examples we show only the shortest distances to each destination

## Slide 11: Distance Vector Algorithm (cont’d)
1 Initialization:
2 for all neighbors V do
3 if V adjacent to A
4 D(A, V) = c(A,V);
else
D(A, V) = ∞;
send D(A, Y) to all neighbors
loop:
8 wait (until A sees a link cost change to neighbor V /* case 1 */
9 or until A receives update from neighbor V) /* case 2 */
10 if (c(A,V) changes by ±d) /*  case 1 */
11 for all destinations Y that go through V do
12 DV(A,Y) = DV(A,Y) ± d
13 else if (update D(V, Y) received from V) /*  case 2 */
/* shortest path from V to some Y has changed */
14 DV(A,Y) = DV(A,V) + D(V, Y); /* may also change D(A,Y) */
15 if (there is a new minimum for destination Y)
16 send D(A, Y) to all neighbors
17 forever
c(i,j): link cost from node i to j
DZ(A,V): cost from A to V via Z
D(A,V): cost of A’s best path to V

## Slide 12: Distance Vector Algorithm (cont’d)
wait for (change in local link cost or msg from neighbor)
recompute distance table
if least cost path to any dest has changed, notify neighbors
Each node: initialize, then

## Slide 13: Distance Vector Algorithm (cont’d)
1 Initialization:
2 for all neighbors V do
3 if V adjacent to A
4 D(A, V) = c(A,V);
else
D(A, V) = ∞;
send D(A, Y) to all neighbors
loop:
8 wait (until A sees a link cost change to neighbor V /* case 1 */
9 or until A receives update from neighbor V) /* case 2 */
10 if (c(A,V) changes by ±d) /*  case 1 */
11 for all destinations Y that go through V do
12 DV(A,Y) = DV(A,Y) ± d
13 else if (update D(V, Y) received from V) /*  case 2 */
/* shortest path from V to some Y has changed */
14 DV(A,Y) = DV(A,V) + D(V, Y); /* may also change D(A,Y) */
15 if (there is a new minimum for destination Y)
16 send D(A, Y) to all neighbors
17 forever
c(i,j): link cost from node i to j
DZ(A,V): cost from A to V via Z
D(A,V): cost of A’s best path to V

## Slide 14: Example: Initialization
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | ∞
C | ∞ | 7
D | ∞ | ∞
Node A
 | A | C | D
A | 2 | ∞ | ∞
C | ∞ | 1 | ∞
D | ∞ | ∞ | 3
Node B
Node C
 | A | B | D
A | 7 | ∞ | ∞
B | ∞ | 1 | ∞
D | ∞ | ∞ | 1
 | B | C
A | ∞ | ∞
B | 3 | ∞
C | ∞ | 1
Node D
1 Initialization:
2 for all neighbors V do
3 if V adjacent to A
4 D(A, V) = c(A,V);
else
D(A, V) = ∞;
send D(A, Y) to all neighbors

## Slide 15: Example: C sends update to A
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | ∞ | 7
D | ∞ | 8
Node A
 | A | C | D
A | 2 | ∞ | ∞
C | ∞ | 1 | ∞
D | ∞ | ∞ | 3
Node B
Node C
 | A | B | D
A | 7 | ∞ | ∞
B | ∞ | 1 | ∞
D | ∞ | ∞ | 1
 | B | C
A | ∞ | ∞
B | 3 | ∞
C | ∞ | 1
Node D
loop:
…
13 else if (update D(A, Y) from C)
14 DC(A,Y) = DC(A,C) + D(C, Y);
15 if (new min. for destination Y)
16 send D(A, Y) to all neighbors
17 forever
DC(A, B) = DC(A,C) + D(C, B) = 7 + 1 = 8
DC(A, D) = DC(A,C) + D(C, D) = 7 + 1 = 8

## Slide 16: Example: Now B sends update to A
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 5 | 8
Node A
 | A | C | D
A | 2 | ∞ | ∞
C | ∞ | 1 | ∞
D | ∞ | ∞ | 3
Node B
Node C
 | A | B | D
A | 7 | ∞ | ∞
B | ∞ | 1 | 
D | ∞ | ∞ | 1
Node D
loop:
…
13 else if (update D(A, Y) from B)
14 DB(A,Y) = DB(A,B) + D(B, Y);
15 if (new min. for destination Y)
16 send D(A, Y) to all neighbors
17 forever
DB(A, C) = DB(A,B) + D(B, C) = 2 + 1 = 3
DB(A, D) = DB(A,B) + D(B, D) = 2 + 3 = 5
 | B | C
A | ∞ | ∞
B | 3 | ∞
C | ∞ | 1
Make sure you know why this is 5, not 4!

## Slide 17: Example: After 1st Full Exchange
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 5 | 8
Node A
Node B
Node C
 | A | B | D
A | 7 | 3 | ∞
B | 9 | 1 | 4
D | ∞ | 4 | 1
Node D
 | B | C
A | 5 | 8
B | 3 | 2
C | 4 | 1
End of 1st Iteration All nodes knows the best two-hop paths
 | A | C | D
A | 2 | 8 | ∞
C | 9 | 1 | 4
D | ∞ | 2 | 3
Make sure you know why this is 3
Assume all send messages at same time

## Slide 18: Example: Now A sends update to B
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 5 | 8
Node A
Node B
Node C
 | A | B | D
A | 7 | 3 | ∞
B | 9 | 1 | 4
D | ∞ | 4 | 1
Node D
 | B | C
A | 5 | 8
B | 3 | 2
C | 4 | 1
 | A | C | D
A | 2 | 8 | ∞
C | 5 | 1 | 4
D | 7 | 2 | 3
loop:
…
13 else if (update D(B, Y) from A)
14 DA(B,Y) = DA(B,A) + D(A, Y);
15 if (new min. for destination Y)
16 send D(B, Y) to all neighbors
17 forever
DA(B, C) = DA(B,A) + D(A, C) = 2 + 3 = 5
DA(B, D) = DA(B,A) + D(A, D) = 2 + 5 = 7
Where does this 5 come from?
Where does this 7 come from?
What harm does this cause?
How could we fix this?
Notes: Talk about where the 5 and 7 come from!

## Slide 19: Example: End of 2nd Full Exchange
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 4 | 8
Node A
 | A | C | D
A | 2 | 4 | 8
C | 5 | 1 | 4
D | 7 | 2 | 3
Node B
Node C
 | A | B | D
A | 7 | 3 | 6
B | 9 | 1 | 3
D | 12 | 3 | 1
Node D
 | B | C
A | 5 | 4
B | 3 | 2
C | 4 | 1
End of 2nd Iteration All nodes knows the best three-hop paths
Assume all send messages at same time

## Slide 20: Example: End of 3rd Full Exchange
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 4 | 8
Node A
 | A | C | D
A | 2 | 4 | 7
C | 5 | 1 | 4
D | 6 | 2 | 3
Node B
Node C
 | A | B | D
A | 7 | 3 | 5
B | 9 | 1 | 3
D | 11 | 3 | 1
Node D
 | B | C
A | 5 | 4
B | 3 | 2
C | 4 | 1
End of 3rd Iteration: Algorithm Converges!
What route does this 11 represent?
Assume all send messages at same time
If you can’t figure it out after three minutes, ask your neighbor

## Slide 21: Intuition
Initial state: best one-hop paths
One simultaneous round: best two-hop paths
Two simultaneous rounds: best three-hop paths
…
Kth simultaneous round: best (k+1) hop paths
Must eventually converge
  as soon as it reaches longest best path
…..but how does it respond to changes in cost?
The key here is that the starting point is
not the initialization, but some other set of
entries. Convergence could be different!

## Slide 22: DV: Link Cost Changes
 | A | C
A | 4 | 6
C | 9 | 1
Node B
 | A | B
A | 50 | 5
B | 54 | 1
Node C
Link cost changes here
 | A | C
A | 1 | 6
C | 6 | 1
 | A | B
A | 50 | 5
B | 54 | 1
 | A | C
A | 1 | 6
C | 3 | 1
 | A | B
A | 50 | 5
B | 51 | 1
 | A | C
A | 1 | 6
C | 3 | 1
 | A | B
A | 50 | 2
B | 51 | 1
 | B | C
B | 4 | 51
C | 5 | 50
Node A
 | B | C
B | 1 | 51
C | 2 | 50
 | B | C
B | 1 | 51
C | 2 | 50
 | B | C
B | 1 | 51
C | 2 | 50
 | A | C
A | 1 | 3
C | 3 | 1
 | A | B
A | 50 | 2
B | 51 | 1
 | B | C
B | 1 | 51
C | 2 | 50
Stable state
A-B changed
A sends tables to B, C
B sends tables to C
C sends tables to B
A
C
1
4
50
B
1
“good news travels fast”

## Slide 23: DV: Count to Infinity Problem
 | A | C
A | 4 | 6
C | 9 | 1
Node B
 | A | B
A | 50 | 5
B | 54 | 1
Node C
Link cost changes here
 | A | C
A | 60 | 6
C | 65 | 1
 | A | B
A | 50 | 5
B | 54 | 1
 | A | C
A | 60 | 6
C | 110 | 1
 | A | B
A | 50 | 5
B | 101 | 1
 | A | C
A | 60 | 6
C | 110 | 1
 | A | B
A | 50 | 7
B | 101 | 1
 | B | C
B | 4 | 51
C | 5 | 50
Node A
 | B | C
B | 60 | 51
C | 61 | 50
 | B | C
B | 60 | 51
C | 61 | 50
 | B | C
B | 60 | 51
C | 61 | 50
 | A | C
A | 60 | 8
C | 110 | 1
 | A | B
A | 50 | 7
B | 101 | 1
 | B | C
B | 60 | 51
C | 61 | 50
Stable state
A-B changed
A sends tables to B, C
B sends tables to C
C sends tables to B
A
C
1
4
50
B
60
“bad news travels slowly”
(not yet converged)

## Slide 24: DV: Poisoned Reverse
 | A | C
A | 4 | ∞
C | ∞ | 1
Node B
 | A | B
A | 50 | 5
B | 54 | 1
Node C
Link cost changes here
 | A | C
A | 60 | ∞
C | ∞ | 1
 | A | B
A | 50 | 5
B | 54 | 1
 | A | C
A | 60 | ∞
C | 110 | 1
 | A | B
A | 50 | 5
B | ∞ | 1
 | A | C
A | 60 | ∞
C | 110 | 1
 | A | B
A | 50 | 61
B | ∞ | 1
 | B | C
B | 4 | 51
C | 5 | 50
Node A
 | B | C
B | 60 | 51
C | 61 | 50
 | B | C
B | 60 | 51
C | 61 | 50
 | B | C
B | 60 | 51
C | 61 | 50
 | A | C
A | 60 | 51
C | 110 | 1
 | A | B
A | 50 | 61
B | ∞ | 1
 | B | C
B | 60 | 51
C | 61 | 50
Stable state
A-B changed
A sends tables to B, C
B sends tables to C
C sends tables to B
A
C
1
4
50
B
60
If B routes through C to get to A:
  B tells C its (B’s) distance to A is infinite (so C won’t route to A via B)
Note: this converges after C receives another update from B
Notes: Explain full table version of DV in section from the other set of slides.

## Slide 25: Will PR Solve C2I Problem Completely?
A
C
1
B
D
1
1
1
1
1
2
2
∞
∞
∞
100
100
100
3
∞
4
∞
4
5
6
Notes: Finish by replacing 100s with infinity on one side, 5 on the other, and then updating C

## Slide 26: A few other inconvenient aspects
What if we use a non-additive metric?
  E.g., maximal capacity
What if routers don’t use the same metric?
  I want low delay, you want low loss rate?
What happens if nodes lie?

## Slide 27: Can You Use Any Metric?
We said that we can pick any metric. Really?
What about maximizing capacity?

## Slide 28: What Happens Here?
All nodes want to maximize capacity
A high capacity link gets reduced to low capacity
Problem:“cost” does not change around loop
How could you fix this (without changing metric)?

## Slide 29: No agreement on metrics?
If the nodes choose their paths according to different criteria, then bad things might happen
Example
  Node A is minimizing latency
  Node B is minimizing loss rate
  Node C is minimizing price
Any of those goals are fine, if globally adopted
  Only a problem when nodes use different criteria
Consider a routing algorithm where paths are described by delay, cost, loss

## Slide 30: What Happens Here?
Low price link
Low loss link
Low delay link
Low loss link
Low delay link
Low price link
Cares about price,
then loss
Cares about delay,
then price
Cares about loss,
then delay
Go figure this out in groups!
Would path-vector fix this?
Notes: Figure this out. Break into groups….

## Slide 31: Must agree on loop-avoiding metric
When all nodes minimize same metric
And that metric increases around loops
Then process is guaranteed to converge

## Slide 32: What happens when routers lie?
What if router claims a 1-hop path to everywhere?
All traffic from nearby routers gets sent there
How can you tell if they are lying?
Can this happen in real life?
  It has, several times….

## Slide 33: Routing: Just the Beginning
Link state and distance-vector (and path vector) are the deployed routing paradigms
But we know how to do much, much better…
Stay tuned for a later lecture where we:
  Reduce convergence time to zero
  Deal with “policy oscillations”
  Enable multipath routing