## Slide 1: Missing Pieces, and Designing IP
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 2: Questions about Project 1

## Slide 3: Announcements
HW formatting: don’t screw it up.
  You have been warned!
HW2 out later tonight
Midterm review???

## Slide 4: Today’s Lecture: Two Topics
Covering some “missing pieces”
  Maybe networking isn’t as simple as I said….
Designing IP
  What should it be doing?
  What needs to be included in the packet header?

## Slide 5: Missing Pieces

## Slide 6: Where are we?
We have covered the “fundamentals”
  How to deliver packets (routing)
  How to build reliable delivery on an unreliable network
With this, we could build a decent network
But couldn’t actually do anything with the network
  Too many missing pieces
We now want to identify those pieces
  Will guide what we cover rest of semester

## Slide 7: Scenario: Joan Wants Her Music
Joan is sitting in her dorm room, with a laptop
Has overwhelming urge to listen to John Cage
  In particular, his piece 4′33″
  Let’s listen to the opening movement…(quiet!!)
What needs to happen to make this possible?
  Not in terms of today’s protocols…
  ……but in terms of basic tasks

## Slide 8: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Addressing general security concerns
  Verifying that this is the right content
  And that no one can tell what she’s downloading
Before I answer, jot down a few steps.
This portion of the lecture won’t mean
much if you don’t try to figure it out.
Talk to your neighbors about it,
talk to yourself about it,
don’t just sit there and read your mail….
Did I miss anything?
Notes: Stop for input!

## Slide 9: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Addressing general security concerns
  Verifying that this is the right content
  And that no one can tell what she’s downloading
Notes: Stop for input!

## Slide 10: Access Networks
If access network is “switched”, we understand it
  Just like any other packet-switched network
If the access network is shared medium, then we need to figure out how to share the medium
  Wireless
  Classical ethernet

## Slide 11: Media Access Control (MAC)
Carrier sense: (CSMA)
  Don’t send if someone else is sending
Collision detection: (CD)
  Stop if you detect someone else was also sending
Collision avoidance: (CA)
  How to arrange transmissions so that they don’t collide
This is the subject of my first CS paper.
And you know how old people like me
like to relive their youth…..

## Slide 12: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (need to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Addressing general security concerns
  Verifying that this is the right content
  And that no one can tell what she’s downloading
Notes: Stop for input!

## Slide 13: Network Management
Control how network interconnects to Internet
  Interdomain routing
Keep unwanted traffic off network
  Firewalls and access control
Share limited number of public addresses
  NAT
Keep links from overloading
  Traffic engineering
Most undeveloped part of Internet architecture

## Slide 14: Current Network Management
No abstractions, no layers
Just complicated distributed algorithms
  Such as routing algorithms
Or manual configuration
  Such as Access Control Lists and Firewalls

## Slide 15: Future Network Management
Clean abstractions
No complicated distributed algorithms
Treat networks like systems…
Two lectures later in semester!
Find out why stick shifts are the root of all evil in networking!

## Slide 16: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Addressing general security concerns
  Verifying that this is the right content
  And that no one can tell what she’s downloading
Notes: Stop for input!

## Slide 17: “Real World Name” to “Network Name”
Joan knows what music she wants
Doesn’t know how to tell network what she wants
Needs to map “real world name” (John Cage)….
…..to a name that the infrastructure understands
  We will call this the “network name” but this isn’t a name at the IP level, but another portion of the infrastructure
Search engine!
  Maps keywords to URL
How can we do this?

## Slide 18: What is a “Network Name”?
HTTP://www.youtube.com/watch?v=hUJagb7hL0E
HTTP is host-to-host protocol
www.youtube.com is a “host name”
  Widely replicated, but still represents a host
watch?v=hUJagb7hL0E is meaningful to host

## Slide 19: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Addressing general security concerns
  Verifying that this is the right content
  And that no one can tell what she’s downloading
Notes: Stop for input!

## Slide 20: Map Network Name to Location
“Name resolution” converts name to location
  Location is IP address of host
We would like location to be nearby copy
  Speeds up download
  Reduce load on backbone and access networks
Notes: Draw picture of access network and backbone network

## Slide 21: How is this done today?
Name resolution: Domain Name System (DNS)
  Hand in a hostname, get back an IP address
Nearby copy of the data?
  CDNs: content distribution networks (like Akamai)
P2P systems can also point you to nearby content

## Slide 22: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Addressing general security concerns
  Verifying that this is the right content
  And that no one can tell what she’s downloading
Notes: Stop for input!

## Slide 23: Download Data from Location
Need a reliable transfer protocol: TCP
  Must share network with others: congestion control
But must be able to use URL to retreive content
  Need higher-level protocol like HTTP to coordinate

## Slide 24: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Addressing general security concerns
  Verifying that this is the right content
  And that no one can tell what she’s downloading
Notes: Stop for input!

## Slide 25: Ensuring Security
Privacy: prevent sniffers from knowing what she downloaded (“it was for EE122, I promise!”)
Integrity: ensure data wasn’t tampered with during its trip through network
Provenance: ensure that music actually came from the music company (and not some imposter)

## Slide 26: How do we do this today?
Cryptographic measures enable us to do all three
Public Key cryptography is crucial
  No need to share secrets beforehand

## Slide 27: Scenario Requires
Media Access Control
Network management
Naming and name resolution
Content distribution networks
And perhaps P2P
Congestion control
HTTP
Cryptographic measures to secure content

## Slide 28: Rest of Course
Details of IP and TCP
  Bringing reality to general concepts
Filling in pieces of name resolution and HTTP
Congestion control
Advanced routing
Security
Ethernet and Wireless
Network Management
What if we were to redesign Internet from scratch

## Slide 29: Break

## Slide 30: The Design of IP

## Slide 31: We are about to make a transition!
From heady principles…
...to packet headers
From essentials…
…to esoterica
From fundamentals…
…to no-fun-at-all

## Slide 32: What I’ll try to get through….
Design-it-yourself packet header
IP header (maybe)
Comparison with IPv6 (not a chance)

## Slide 33: What is “designing” a protocol?
Specifying the syntax of its messages
  Format
Specifying their semantics
  Meaning
  Responses

## Slide 34: What is Designing IP?
Syntax: format of packet
  Nontrivial part: packet “header”
  Rest is opaque payload (why opaque?)
Semantics: meaning of header fields
  Required processing
Header
Opaque Payload

## Slide 35: Packet Header as Interface
Think of packet header as interface
  Only way of passing information from packet to switch
Designing interfaces:
  What task are you trying to perform?
  What information do you need to accomplish it?
Header reflects information needed for basic tasks

## Slide 36: In-Class Exercise
Five minutes to design the IPv7 packet header
  Do not look at book, or otherwise copy IPv4 or IPv6
  Do work in groups
Goal not to get right answer, but to think about:
  What tasks are involved?
  How can a packet header accomplish it?
Note: IPv4 is not a great model
  Try to do better!

## Slide 37: I’ll Take Two or Three Answers
You tell me your:
  Task list
  Corresponding information in header
  And any deep insights about architecture? (Optional!)
Example:
  Task 1: get packet to destination
  Header information: destination address

## Slide 38: Answer #1:
Destination address
TTL

## Slide 39: What Tasks Do We Need to Do?
Read packet correctly
Get packet to the destination
Get responses to the packet back to source
  Not really, but humor me….
Carry data
Tell host what to do with packet once arrived
Specify any special network handling of the packet
Deal with problems that arise along the path

## Slide 40: Reading Packet Correctly
Where does header end?
Where does packet end?
What version of IP?
  Why is this so important?

## Slide 41: Getting to the Destination
Provide destination address (duh!)
Should this be location or identifier?
  And what’s the difference?
If a host moves, should its address change?
  If not, how can you build scalable Internet?
  If so, then what good is an address for identification?

## Slide 42: Getting Response Back to Source
Source address (duh!)
You’ve already heard my rant on this….

## Slide 43: Carry Data
Payload (duh!)

## Slide 44: Telling Dest’n How to Process Packet
Indicate which protocols should handle packet
What layer should this protocol be in?
What are some options for this today?
How does the source know what to enter here?

## Slide 45: Special Handling
Type-of-service: Priority, etc.
Options: discuss later

## Slide 46: Dealing with Problems
Is packet caught in loop?
  TTL
Header Corrupted:
  Detect with Checksum
  What about payload checksum?
Packet too large?
  Deal with fragmentation
  Split packet apart
  Keep track of how to put together

## Slide 47: Are We Missing Anything?
Read packet correctly
Get packet to the destination
Get responses to the packet back to source
Carry data
Tell host what to do with packet once arrived
Specify any special network handling of the packet
Deal with problems that arise along the path

## Slide 48: From Semantics to Syntax
The past few slides discussed the kinds of information the header must provide
Will now show the syntax (layout) of IPv4 header, and discuss the semantics in more detail

## Slide 49: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 50: 20 Bytes of Standard Header, then Options
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 51: Go Through Tasks One-by-One
Read packet correctly
Get packet to the destination
Get responses to the packet back to source
Carry data
Tell host what to do with packet once arrived
Specify any special network handling of the packet
Deal with problems that arise along the path

## Slide 52: Reading Packet Correctly
Version number (4 bits)
  Indicates the version of the IP protocol
  Necessary to know what other fields to expect
  Typically “4” (for IPv4), and sometimes “6” (for IPv6)
Header length (4 bits)
  Number of 32-bit words in the header
  Typically “5” (for a 20-byte IPv4 header)
  Can be more when IP options are used
Total length (16 bits)
  Number of bytes in the packet
  Maximum size is 65,535 bytes (216 -1)
  … though underlying links may impose smaller limits

## Slide 53: Fields for Reading Packet Correctly
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 54: Getting Packet to Destination and Back
Two IP addresses
  Source IP address (32 bits)
  Destination IP address (32 bits)
Destination address
  Unique identifier/locator for the receiving host
  Allows each node to make forwarding decisions
Source address
  Unique identifier/locator for the sending host
  Recipient can decide whether to accept packet
  Enables recipient to send a reply back to source

## Slide 55: Fields for Packet Reaching Destination
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 56: Telling Host How to Handle Packet
Protocol (8 bits)
  Identifies the higher-level protocol
  Important for demultiplexing at receiving host
Most common examples
  E.g., “6” for the Transmission Control Protocol (TCP)
  E.g., “17” for the User Datagram Protocol (UDP)
IP header
IP header
TCP header
UDP header
protocol=6
protocol=17

## Slide 57: Field for Next Protocol
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 58: Special Handling
Type-of-Service (8 bits)
  Allow packets to be treated differently based on needs
  E.g., low delay for audio, high bandwidth for bulk transfer
  Has been redefined several times, will cover late in QoS
Options

## Slide 59: Fields for Special Handling
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 60: Potential Problems
Header Corrupted: Checksum
Loop: TTL
Packet too large: Fragmentation

## Slide 61: Header Corruption
Checksum (16 bits)
  Particular form of checksum over packet header
If not correct, router discards packets
  So it doesn’t act on bogus information
Checksum recalculated at every router
  Why?
  Why include TTL?
  Why only header?

## Slide 62: Checksum Field
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 63: Preventing Loops
Forwarding loops cause packets to cycle forever
  As these accumulate, eventually consume all capacity
Time-to-Live (TTL) Field (8 bits)
  Decremented at each hop, packet discarded if reaches 0
  …and “time exceeded” message is sent to the source
    Using “ICMP” control message; basis for traceroute

## Slide 64: TTL Field
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 65: Fragmentation
Fragmentation: when forwarding a packet, an Internet router can split it into multiple pieces (“fragments”) if too big for next hop link
Must reassemble to recover original packet
  Need fragmentation information (32 bits)
  Packet identifier, flags, and fragment offset

## Slide 66: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 67: Option Field Layout
Field | Size (bits) | Description
Copied | 1 | Set if field copied to all fragments
Class | 2 | 0=control, 2=debugging/measurement
Number | 5 | Specifies option
Length | 8 | Size of entire option
Data | Variable | Option-specific data

## Slide 68: Examples of Options
End of Options List
No Operation (padding between options)
Record Route
Strict Source Route
Loose Source Route
Timestamp
Traceroute
Router Alert
…..

## Slide 69: IPv6

## Slide 70: IPv6
Motivated (prematurely) by address exhaustion
  Addresses four times as big
Steve Deering focused on simplifying IP
  Got rid of all fields that were not absolutely necessary
  “Spring Cleaning” for IP
Result is an elegant, if unambitious, protocol

## Slide 71: IPv4 and IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 72: Summary of Changes
Eliminated fragmentation (why?)
Eliminated header length (why?)
Eliminated checksum (why?)
New options mechanism (next header) (why?)
Expanded addresses (why?)
Added Flow Label (why?)

## Slide 73: IPv4 and IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 74: Philosophy of Changes
Don’t deal with problems: leave to ends
  Eliminated fragmentation
  Eliminated checksum
  Why retain TTL?
Simplify handling:
  New options mechanism (uses next header approach)
  Eliminated header length
    Why couldn’t IPv4 do this?
Provide general flow label for packet
  Not tied to semantics
  Provides great flexibility

## Slide 75: Comparison of Design Philosophy
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
To Destination and Back (expanded)
Deal with Problems (greatly reduced)
Read Correctly (reduced)
Special Handling (similar)

## Slide 76: Improving on IPv4 and IPv6?
Why include unverifiable source address?
  Would like accountability and anonymity (now neither)
  Return address can be communicated at higher layer
Why packet header used at edge same as core?
  Edge: host tells network what service it wants
  Core: packet tells switch how to handle it
    One is local to host, one is global to network
Some kind of payment/responsibility field?
  Who is responsible for paying for packet delivery?
  Source, destination, other?
Other ideas?
Survey results