## Slide 1: Advanced Topics in Routing
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 2: Announcements

## Slide 3: Holy Trinity of Routing: LS, DV, PV
Normally presented as the complete story
But we know how to do much better
That is what we will talk about today…..
Notes: To complete analogy, Learning Switch is the Old Testament, before we saw the light….

## Slide 4: Major Routing Challenges:
Policy Oscillations
Resilience
Traffic Engineering

## Slide 5: Another Purpose for Today
EE122 (CS version) is algorithmically vacuous
  AIMD is the high point of intellectual depth (ugh)
The algorithms described today are nontrivial
  Algorithms simple, but their properties are nonobvious
You will prove two results as a class exercise
  5 minutes, in groups, try to come up with reasoning
  I’ll help shape it into a proof
Notes: Usually, material is boring ,and my lecture style doesn’t help matters.
Today, material is interesting (if you like networks), so get your head into it.
If you don’t want to think about this, feel free to leave. I want the rest of you alert, and if you don’t understand something then ASK!!!

## Slide 6: Policy Dispute Resolution

## Slide 7: Policy Oscillations
Last time we discussed how BGP might never converge due to “policy oscillations”
We now discuss how we might solve this problem

## Slide 8: Policy Oscillations (cont’d)
Policy autonomy vs network stability
  Oscillations possible with small degree of autonomy
  Focus of much recent research
Not an easy problem
  PSPACE-complete to decide whether given policies will eventually converge!
However, if policies follow normal business practices, stability is guaranteed
  “Gao-Rexford conditions”
  Essentially the provider/peer/customer policy categories

## Slide 9: Theoretical Results (in more detail)
If preferences obey Gao-Rexford, BGP is safe
  Safe = guaranteed to converge
If there is no “dispute wheel”, BGP is safe
  But converse is not true
If there are two “stable states”, BGP is unsafe
  But converse is not true
If domains can’t lie about routes, and there is no dispute wheel, BGP is incentive compatible

## Slide 10: Objectives for New Policy Approach
Do not reveal any ISP policies
Distributed, online dispute detection and resolution
Pick “normal” path (according to policies) if no oscillation exists
  Get something reasonable if oscillation would exist
Account for transient oscillations, don’t permanently blacklist routes

## Slide 11: Example of Policy Oscillation
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
“1” prefers “1 3 0”
over “1 0” to reach “0”

## Slide 12: Step-by-Step of Policy Oscillation
Initially: nodes 1, 2, 3 know only shortest path to 0
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0

## Slide 13
1 advertises its path 1 0 to 2
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 1 0
Step-by-Step of Policy Oscillation

## Slide 14
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 15
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 3 0
3 advertises its path 3 0 to 1
Step-by-Step of Policy Oscillation

## Slide 16
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 17
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 1 0
1 withdraws its path 1 0 from 2
Step-by-Step of Policy Oscillation

## Slide 18
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 19
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 2 0
2 advertises its path 2 0 to 3
Step-by-Step of Policy Oscillation

## Slide 20
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 21
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 3 0
3 withdraws its path 3 0 from 1
Step-by-Step of Policy Oscillation

## Slide 22
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 23
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
1 advertises its path 1 0 to 2
Step-by-Step of Policy Oscillation
advertise: 1 0

## Slide 24
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 25
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 2 0
2 withdraws its path 2 0 from 3
Step-by-Step of Policy Oscillation

## Slide 26
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
We are back to where we started!
Step-by-Step of Policy Oscillation

## Slide 27: Nodes See Signs of Trouble
Route choices oscillation
  Node 1:
    1 0 , 1 3 0 , 1 0 , 1 3 0 , …..
  Node 2:
    2 0 , 2 1 0 , 2 0 , 2 1 0 , …..
  Node 3:
    3 0 , 3 2 0 , 3 0 , 3 2 0 , …..
Choices alternate between more preferred and less preferred routes

## Slide 28: Basic Idea
If node notices that it is constantly selectng routes that are more / less preferred than previous route
  Node thinks it may be involved in oscillation
Computes local “precedence” figure
  Higher precedence value for less preferred routes
  In example, 1 0 gets higher value than 1 3 0
Route advertisements carry this precedence
  Two precedence values:
    Incoming (carried by packet)
    Local (determined by own past history)

## Slide 29: Precedence Calculation
Routes are first ranked by “incoming precedence”
  Pick most preferred route among those with lowest incoming precedence value
Outgoing precedence is sum of incoming and local precedence

## Slide 30: Use of Precedence Values
  Maintain history of routes encountered during oscillations
    In table below, prefer P0 to P1 to P2
  Pick path P2, mark with precedence 1

## Slide 31: Example of Policy Oscillation
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0

## Slide 32
1 advertises its path 1 0 to 2
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 1 0
Precedence 0
Step-by-Step of Policy Oscillation

## Slide 33
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 34
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 3 0
Precedence 0
3 advertises its path 3 0 to 1
Step-by-Step of Policy Oscillation

## Slide 35
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 36
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 1 0
1 withdraws its path 1 0 from 2
Step-by-Step of Policy Oscillation

## Slide 37
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 38
Routes stabilize at this point
3 cannot choose 2 0 route from 2, because of higher precedence value
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 2 0
Precedence 1
2 advertises its path 2 0 to 3
Step-by-Step of Policy Oscillation

## Slide 39: “Proof” of why it works
Assume that policy oscillation exists within scheme
Some router A must prefer a path offered by a router B that does not prefer that path
  If everyone is getting first choice, no oscillation!
  So A’s first choice is B’s second choice for some A,B
But router A cannot choose that path because it will have a lower precedence

## Slide 40: Properties of Solution
If no policy oscillation exists, get usual routes
If policy oscillation would have existed, approach short-circuits oscillation
If, after convergence, non-zero global precedence values exist,  dispute(s) exist
Only precedence values advertised, no other routes or policies revealed
Why isn’t this deployed?

## Slide 41: Routing Resilience

## Slide 42: Resilience
Basic routing algorithms rely on timely consistency or global convergence to achieve ensure delivery
  LS: routers need to have same picture of network
  DV: if algorithm hasn’t converged, might loop
As nets grow, this gets harder and takes longer
  Need both consistency/convergence and timeliness!
Creates lag between failure detection and recovery
  Lag is biggest barrier to achieving 99.999% reliability

## Slide 43: Hacks Used Today
Preconfigured backup paths
  When link fails, router has a backup route to use
  Very helpful against single failures
  Only limited protection against multiple failures
  No systematic paradigm
ECMP: Equal-Cost Multipath
  Similar to backups, but narrower applicability
  Choose among several “shortest-paths”

## Slide 44: Solutions Presented Today
Multipath (one slide)
Failure-carrying packets
Routing-along-DAGs

## Slide 45: Multipath Routing
Multipath:
  Providing more than one path for each S-D pair
  Allow endpoints to choose among them
    This can be implemented by having a “path” field in packet
Good: if one path goes down, can use another
Bad: Delay while endpoints detect failure (RTT)
Absolutely necessary because of E2E arguments
  But not a fundamental paradigm shift
Part of solution, but still need more reliable routing

## Slide 46: Fundamental Question
Can we completely eliminate the need to “reconverge” after link failures?
i.e., can we tolerate failures without losses?

## Slide 47: Failure-Carrying Packets (FCP)

## Slide 48: FCP Approach: Step 1
Ensure all routers have consistent view of network
  But this view can be out-of-date
  Consistency is easy if timeliness not required
Use reliable flooding
  Each map has sequence number
Routers write this number in packet headers, so packets are routing according to the same “map”
  Routers can decrement this counter, not increment it
  Eventually all routers use the same graph to route packet
This achieves consistency, but not timeliness….

## Slide 49: FCP Approach: Step 2
Carry failure information in the packets!
  Use this information to “fix” the local maps
When a packet arrives and the next-hop link for the path computed with the consistent state is down, insert failure information into packet header
  Then compute new paths assuming that link is down
If failure persists, it will be included in next consistent picture of network
  Then not needed in packet header

## Slide 50: Example: FCP routing
B
D
C
E
A
F
IP packet
source
destination

## Slide 51: Example: FCP routing
F
B
D
C
E
A
source
destination
IP packet
(C,E)
IP packet
(D,F)
(C,E)
IP packet

## Slide 52: Class Exercise: Prove This Works
Develop line of argument about why this guarantees connectivity
Under what circumstances does guarantee hold?

## Slide 53: Keys to Proof
Deadend: as long as map plus failures has connectivity, no dead ends
Loops: Assume loop. The nodes on the loop all share the same “consistent” map plus a set of failures in the packet header. Therefore, they compute the same path. Contradiction.

## Slide 54: Condition for Correctness
Consider a set of changes to network from the last consistent map before packet is sent until TTL of packet would expire.
If intersection of all network states during change process is connected, then FCP will deliver packet

## Slide 55: Properties of FCP
Guarantees packet delivery
  As long as a path exists during failure process
Major conceptual change
  Don’t rely solely on protocols to keep state consistent
  Information carried in packets ensures eventual consistency of route computation
  This theme will recur in next design….
  Ion’s Stoica’s thesis!

## Slide 56: Results: OSPF vs. FCP
Unlike FCP, OSPF cannot simultaneously provide low churn and high availability
Overhead [msgs/sec per link]
OSPF-overhead
FCP-lossrate
OSPF-lossrate

## Slide 57: Results: Backup-paths vs. FCP
Unlike FCP, Backup-paths cannot simultaneously provide low state and lossrate
Bkup-state
FCP-state
FCP-lossrate
Bkup-lossrate

## Slide 58: Problems with FCP
Requires changes to packet header
  And packet headers could get long
Requires fast recomputation of routes
  Can precompute common cases, but worst case is bad
Does not address traffic engineering
  What is that?

## Slide 59: Traffic Engineering (TE)
Connectivity is necessary but not sufficient
Need to also provide decent service
Requires that links on the path not be overloaded
  Congestion control lowers drop rate, but need to provide reasonable bandwidth to connections by spreading load
TE is a way of distributing load on the network
  i.e., not all packets travel the “shortest path”

## Slide 60: Routing Along DAGs (RAD)

## Slide 61: Avoiding Recomputation: Take II
Recover from failures without global recomputation
Support locally adaptive traffic engineering
Without any change in packet headers, etc.
Or requiring major on-the-fly route recomputation

## Slide 62: Background
Focus only on routing table for single destination
  Could be a prefix, or a single address
  Routing to each destination is independent, so this is fine
Today we compute paths to particular destination
  From each source to this destination there is a path
When path breaks, need to recompute path
  The source of all our troubles!

## Slide 63: Our Approach: Shift the Paradigm
Move from path to DAG (Directed Acyclic Graph)
Routing compute paths from source to destination
If a link fails, all affected paths must be recomputed
Path
DAG
X
X
  Packets can be sent on any of the DAG’s outgoing links
  No need for global recomputation after each failure

## Slide 64: DAG Properties
Guaranteed loop-free
Local decision for failure recovery
Adaptive load balancing
X
X
0.7
0.3

## Slide 65: Load Balancing
Use local decisions:
  Choose which outgoing links to use
  Decide how to spead the load across these links
  Push back when all outgoing links are congested
    Send congestion signal on incoming links to upstream nodes
Theorem:
  When all traffic goes to a single destination, local load balancing leads to optimal throughput
Simulations:
  In general settings, local load balancing close to optimal

## Slide 66: DAG-based Routing
Essentially a principled paradigm for backup paths
  Can tolerate many failures
  Scalable
  Easy to understand and manage
Notes: MPLS: 100,000s of labels….

## Slide 67: Computing DAG
Use each link in a single direction
DAG iff link directions follow global order
Computing a DAG for destination v is simple:
  Essentially a shortest-path computation
  With consistent method of breaking ties

## Slide 68: What about Connectivity?
Multiple outgoing links improve connectivity
  But can RAD give “perfect” connectivity?
If all outbound links fail that node is disconnected
  Even if underlying graph is still connected
How can we fix this?

## Slide 69: Link Reversal
If all outgoing links fail, reverse incoming links to outgoing
X
X
X
X
Notes: pre compute paths doesn’t have guarantee
but link reversal can

## Slide 70: RAD Algorithm
When packet arrives, send out any outgoing link
When an outgoing link fails (or is reversed)
  If other outgoing links exist, do nothing
  If no other outgoing links exist, reverse all incoming links
    i.e., change them to outgoing

## Slide 71: Link Reversal Properties
Connectivity guaranteed!
  If graph is connected, link reversal process will restore connectivity in DAG
This has been known in wireless literature
  Now being applied to wired networks
If you don’t think this is neat, then you are asleep.
  Local rule to produce ideal connectivity!

## Slide 72: Class Exercise: Prove This Works
Develop line of argument about why this guarantees connectivity

## Slide 73: Keys to Proof
Deadend: algorithm never results in dead-ends
  At least one link will be outbound, if you have a link
Loops:
  Assume network does not have loop at beginning
    (i.e., we have a DAG)
  Link reversal cannot create a loop
    Because reversed node cannot be part of a loop
  Therefore, topology never in a state where a loop exists
Are we done with proof?

## Slide 74: No, link reversals might not terminate
Must prove topology reaches fixed point
  If underlying graph is connected
Not reaching a fixed point means process of node reversals continues forever
Since network is of finite size, this process must repeat in a cycle of node reversals
How can we prove this is impossible?

## Slide 75: Fact #1
If a node has a path to the destination, then it will never reverse itself.
Conclusion: the set of nodes with a path to the destination is nondecreasing

## Slide 76: Fact #2
For a node to do a second link reversal, all of its neighbors must have also reversed its links.
Therefore, the set of nodes doing a link reversal is an expanding set
Can only re-reverse all reversing nodes if the process reaches the “edge” of network
But once this process touches a node which is connected to the source, it stops. QED.

## Slide 77: Summary of RAD
Local responses lead to:
  Guaranteed connectivity
  Close-to-optimal load balancing
Can be used for L2 and/or L3
  No change in packet headers

## Slide 78: Why Isn’t RAD Enough?
The link reversals are on the “control plane”
They take time to compute
Packets can be lost in the meantime…
Exactly the problem with FCP route recomputation
  Works on control-plane speeds, not data speeds
Any suggestions?

## Slide 79: Data-Driven Connectivity (DDC)
Define link reversal properties in terms of actions that can occur at data speeds
Events: packet arriving in “reverse” direction
Action: remove that link from outgoing set
Goal: define simple algorithms that can be supported in HW
  Ask Panda for more details

## Slide 80: Review
Major Routing Challenges:
  Resilience
  Traffic Engineering
  Policy Oscillations
We have solutions for all of them!
  FCP, RAD, and Policy Dispute Resolution
Are they deployed? No…..
  Will they be deployed? Maybe…..
..