## Slide 1: Link-Layer and ICMP
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 3: Project 1
Distribution of grades:
  50% perfect score of 240
  90% above 140
Giving people a second chance:
  Fix your project, get it running
  We’ll figure out the penalties later
Constraints:
  Fix must cause multiple test cases to go from fail to pass
  Regrades get maximum score of 200
  Contact Anand/Colin for details……

## Slide 4: Midterm
Average score 104 (out of 119)
Standard deviation 11
50th percentile 107
90th percentile 115

## Slide 5: Question-by-question….
True/False: about 10% got full credit
  Peak about 18 out of 20
Multiple choice: about 8% got full credit
  Peak about 18 out of 20
  IP checksum only looks at header
  UDP header does not include addresses
TCP Basics: about 50% got full credit
Seq. of Messages: about 80% got full credit
The Real World: about 90% got full credit

## Slide 6: Question-by-question….
Timer values: about 50% got full credit
Addressing: about 70% got full credit
Learning switch: about 60% got full credit
DNS: about 70% got full credit
Sliding window: about 70% got full credit

## Slide 7: Humorous answers….
Who is the unsung hero?
  “me”
  “Al Gore” (surprisingly popular answer)
What letter caused the first demo to fail?
  “love letter”
  “S for shenker”
In what year?
  “1776”,
  “122 BCE”
  “12000 BC (there was time travel involved)”

## Slide 8: Suggested Bonus Questions…
What is Scott Shenker’s brother’s profession?
How many citations does Shenker have?
Draw a giraffe

## Slide 9: The Bet….
8 people with a score of 119 on questions 1-10
  I geared the review to the test way too closely
  But I felt like I had not sufficiently covered the “putting it all together” questions in lecture/sections
5 of the 119 scores got three bonus questions right
  The fact you knew the answers to the bonus questions is a very bad sign….
0 of the 119 scores got four bonus questions

## Slide 10: Victory is Mine!

## Slide 11: But in the spirit of fair play….
I won’t collect on the bet
I will donate my stake of $220 to the EE122 review sessions refreshment fund
I’m taking bets for the final….(10:1 odds again)
I was accused (in writing) for “cheating” on the bet
  I won’t forget who you are…….
  P. S. My TAs agree with you
  P. P. S. None of them will ever graduate

## Slide 12: Where Are We?

## Slide 13: What Do We Know?
How to route
  L2 (learning switches)
  L3 (DV, LS)
How to get an IP address (DHCP)
How to resolve names to IP addresses (DNS)
How to forward packets (LPM)
How to deliver packet reliably (TCP)
How to access content (HTTP)
……

## Slide 14: Missing Pieces (covered today)
Basics of link-layer (L2) networks
  Will do details of ethernet later
Using link-layer networks to reach destination
  L2 involved at first/last hops (and in between)
How do I find out about network problems?
  Loops, MTU limitations, etc.

## Slide 15: Background on Link-Layer

## Slide 16: Message, Segment, Packet, and Frame
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Ethernet frame
Ethernet frame
SONET frame

## Slide 17: Focus on Link-Layer
Ethernet
interface
Ethernet
interface
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
Ethernet frame
Ethernet frame
SONET frame

## Slide 18: Adapter-to-Adapter Communication
Link layer implemented in adapter (network interface card; NIC)
  Ethernet card, 802.11 card
Sending side:
  Encapsulates datagram in a frame
  Determines local addressing, adds error checking, controls transmission
Receiving side
  Recognizes arrival, looks for errors, possibly acknowledges
  Extracts datagram and passes to receiving node
sending
node
frame
receiving
node
datagram
frame
adapter
adapter
link layer protocol

## Slide 19: Link-Layer Services
Encoding
  Representing the 0s and 1s
Framing
  Encapsulating packet into frame, adding header, trailer
  Using MAC addresses rather than IP addresses
Error detection
  Errors caused by signal attenuation, noise
  Receiver detects presence, may ask for repeat
Resolving contention
  Deciding who gets to transmit when multiple senders want to use a shared media
Flow control (pacing between sender & receiver)
Notes: Each link layer technology uses its own solution for these services.
And they support different subsets. Some do error detection, some do flow control, etc.

## Slide 20: MAC Address vs. IP Address
MAC addresses (used in link-layer)
  Hard-coded in read-only memory when adapter is built
  Like a social security number
  Flat name space of 48 bits (e.g., 00-0E-9B-6E-49-76)
  Portable, and can stay the same as the host moves
  Used to get packet between interfaces on same network
IP addresses
  Configured, or learned dynamically
  Like a postal mailing address
  Hierarchical name space of 32 bits (e.g., 12.178.66.9)
  Not portable, and depends on where the host is attached
  Used to get a packet to destination IP subnet

## Slide 21: Broadcast at Link-Level
Use broadcast address: ff:ff:ff:ff:ff:ff
If have return MAC address, use that in response
Unless want everyone to know result

## Slide 22: Broadcast at IP Level
Can't broadcast to all IP hosts
But application might want to send “local” broadcast
Uses IP broadcast address 255.255.255.255
Link-layer then uses link-layer broadcast

## Slide 23: Sending Packets Over Link-Layer
Adapters only understand MAC addresses
  Translate the destination IP address to MAC address
  Encapsulate the IP packet inside a link-level frame
host
host
DNS
...
1.2.3.156
router
1.2.3.53
1.2.3.53
1.2.3.156
IP packet
Mask: 255.255.255.0

## Slide 24: Steps in Sending a Packet
What do hosts need to know?
And how do they find out?

## Slide 25: What Does a Host Need to Know?
What IP address the host should use?
What local DNS server to use?
How to tell which destinations are local?
How do we send packets to local destinations?
How to send packets to remote destinations?
host
host
DNS
...
host
host
DNS
...
router
router
1.2.3.0/23
5.6.7.0/24
1.2.3.7
1.2.3.156
???
1.2.3.19
router

## Slide 26: Steps in reaching a Host
First look up IP address
Need to know where local DNS server is
  DHCP
Also needs to know its own IP address
  DHCP

## Slide 27: Sending a Packet
On same subnet:
  Use MAC address of destination.
  How do hosts know?
On some other subnet:
  Use MAC address of first-hop router.
  How do they know?
And how can a host tell whether destination is on same or other subnet?
  Use the netmask
  DHCP

## Slide 28: DHCP Refresher
Dynamic Host Configuration Protocol (DHCP)
  End host learns how to send packets
  Learn IP address, DNS servers, “gateway”, what’s local
Have already described DHCP operation
  Sequence of broadcasts, no configuration needed
host
host
DNS
...
host
host
DNS
...
router
router
1.2.3.0/24
255.255.255.0
5.6.7.0/24
1.2.3.7
1.2.3.156
1.2.3.48
1.2.3.19
router
1A-2F-BB-76-09-AD

## Slide 29: DHCP Supplies Basic Information
IP address
Mask
Gateway router
DNS server
Now what?

## Slide 30: Sending A Packet: Which Destination?
If destination is on the local network
  Need to address it directly (MAC address)
If destination is not local (“remote”)
  Need to figure out the first “hop” on the local network
  Need MAC address of first hop router
host
host
DNS
...
host
host
DNS
...
router
router
1.2.3.0/24
255.255.255.0
5.6.7.0/24
1.2.3.7
1.2.3.156
1.2.3.48
1.2.3.19
router
1A-2F-BB-76-09-AD

## Slide 31: Determining if Address is Local
Use the netmask
  E.g., mask destination IP address w/ 255.255.255.0
Is it same value as our own masked address?
    Yes = local
    No = remote
host
host
DNS
...
host
host
DNS
...
router
router
1.2.3.0/24
255.255.255.0
5.6.7.0/24
1.2.3.7
1.2.3.156
1.2.3.48
1.2.3.19
router
1A-2F-BB-76-09-AD

## Slide 32: In Both Cases, Need to Send Locally
If it’s remote, look up first hop in (very small) local routing table (in case there are multiple first hops)
  E.g., by default, route via 1.2.3.19
  Now do the local case but for 1.2.3.19 rather than ultimate destination IP address
For the local case, need to determine the destination’s MAC address
host
host
DNS
...
host
host
DNS
...
router
router
1.2.3.0/24
255.255.255.0
5.6.7.0/24
1.2.3.7
1.2.3.156
1.2.3.48
1.2.3.19
router
1A-2F-BB-76-09-AD

## Slide 33: Address Resolution Protocol
Every node maintains an ARP table
  <IP address, MAC address> pair
Consult the table when sending a packet
  Map destination IP address to destination MAC address
  Encapsulate and transmit the data packet
But: what if IP address not in the table?
  Sender broadcasts: “Who has IP address 1.2.3.156?”
  Receiver responds: “MAC address 58-23-D7-FA-20-B0”
  Sender caches result in its ARP table

## Slide 34: Example: A Sending a Packet to B
How does host A send an IP packet to host B?
A
R
B
Take a few minutes, break into groups, figure out how this would work…..

## Slide 35: Example: A Sending a Packet to B
How does host A send an IP packet to host B?
A
R
B
1. A sends packet to R. 2. R sends packet to B.

## Slide 36: Host A Decides to Send Through R
A
R
B
Host A constructs an IP packet to send to B
  Source 111.111.111.111, destination 222.222.222.222
Host A has a gateway router R
  Used to reach destinations outside of 111.111.111.0/24
  Address 111.111.111.110 for R learned via DHCP

## Slide 37: Host A Sends Packet Through R
Host A learns the MAC address of R’s interface
  ARP request: broadcast request for 111.111.111.110
  ARP response: R responds with E6-E9-00-17-BB-4B
Host A encapsulates the packet and sends to R
A
R
B

## Slide 38: R Decides how to Forward Packet
Router R’s adapter receives the packet
  R extracts the IP packet from the Ethernet frame
  R sees the IP packet is destined to 222.222.222.222
Router R consults its forwarding table
  Packet matches 222.222.222.0/24 via other adapter
A
R
B
Two points:
  Routing table points to this port
  Destination address is within mask of port’s address (i.e., local)

## Slide 39: R Sends Packet to B
Router R’s learns the MAC address of host B
  ARP request: broadcast request for 222.222.222.222
  ARP response: B responds with 49-BD-D2-C7-56-2A
Router R encapsulates the packet and sends to B
A
R
B

## Slide 40: Security Analysis of ARP
Impersonation
  Any node that hears request can answer …
  … and can say whatever they want
Actual legit receiver never sees a problem
  Because even though later packets carry its IP address, its NIC doesn’t capture them since not its MAC address

## Slide 41: Key Ideas in Both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
  Remember your own address & other host’s addresses
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 42: Why Not Use DNS-Like Tables?
When host arrives:
  Assign it an IP address that will last as long it is present
  Add an entry into a table in DNS-server that maps MAC to IP addresses (i.e., no need for ARP!)
Think about it for a few minutes, talk in groups
Notes: Two key points

## Slide 43: Two Different Issues
Setting up the database:
  Names: explicit creation, tied to “static” addresses
    DNS need only handle occasional updates
  Hosts: come and go without explicitly informing network
    Must do MAC-IP mapping on demand
  But could leverage DHCP
    DHCP knows when a host arrives
    And DHCP messages already contain MAC addresses
Using the MAC address:
  So if I get MAC address when I look up address in DNS, how can I use that information?
  The database must live in each router and host for it to save any time….but it does cut down on broadcasting

## Slide 44: 5 Minute Break

## Slide 45: Network Control Messages (and how to use them for discovery)

## Slide 46: What Errors Might A Router See?
Dead-end: No route to destination
Sign of a loop: TTL expires
Can’t physically forward: packet too big
  And has DF flag set
Can’t keep up with traffic: buffer overflowing
Header corruption or ill-formed packets
….

## Slide 47: Which should network tell host about?
No route to destination?
  Host can’t detect or fix routing failure.
TTL expires?
  Host can’t detect or fix routing loop.
Packet too big (with DF set)?
  Host can adjust packet size, but can’t tell difference between congestion drops and MTU drops
Buffer overflowing?
  Transport congestion control can detect/deal with this
Header corruption or ill-formed packets?
  Host can’t fix corruption, but can fix formatting errors
This assumes we want to bind the
meaning of packet drops to congestion

## Slide 48: Router Response to Problems?
Router doesn’t really need to respond
  Best effort means never having to say you’re sorry
  So, IP could conceivably just silently drop packets
Network is already trying its best
  Routing is already trying to avoid loops/dead-ends
  Network can’t reduce packet size (in DF packets)
  Network can’t reduce load, nor fix format problems
What more can/should it do?

## Slide 49: Error Reporting Helps Diagnosis
Silent failures are really hard to diagnose
IP includes feedback mechanism for network problems, so they don’t go undetected
Internet Control Message Protocol (ICMP)
The Internet “print” statement
Runs on IP, but viewed as integral part of IP

## Slide 50: Internet Control Message Protocol
Triggered when IP packet encounters a problem
  E.g., Time Exceeded or Destination Unreachable
ICMP packet sent back to the source IP address
  Includes the error information (e.g., type and code)
  IP header plus 8+ byte excerpt from original packet
Source host receives the ICMP packet
  Inspects excerpt (e.g., protocol/ports) to identify socket
Exception: not sent if problem packet is ICMP
  And just for fragment 0 of a group of fragments

## Slide 51: Types of Control Messages
Need Fragmentation
  IP packet too large for link layer, DF set
TTL Expired
  Decremented at each hop; generated if  0
Unreachable
  Subtypes: network / host / port
    (who generates Port Unreachable?)
Source Quench
  Old-style signal asking sender to slow down
Redirect
  Tells source to use a different local router

## Slide 52: Using ICMP
ICMP intended to tell host about network problems
  Diagnosis
  Won’t say more about this….
Can exploit ICMP to elicit network information
  Discovery
  Will focus on this….

## Slide 53: Discovering Network Path Properties
PMTU Discovery: What is largest packet that go through the network w/o needing fragmentation?
  Most efficient size to use
  (Plus fragmentation can amplify loss)
Traceroute:
  What is the series of routers that a packet traverses as it travels through the network?
Ping:
  Simple RTT measurements

## Slide 54: Ping: Echo and Reply
ICMP includes simple “echo” functionality
  Sending node sends an ICMP Echo Request message
  Receiving node sends an ICMP Echo Reply
Ping tool
  Tests connectivity with a remote host
  … by sending regularly spaced Echo Request
  … and measuring delay until receiving replies
If you have never used ping, do it tonight!
  One of the few ways you actually “see” the network

## Slide 55: Path MTU Discovery
MTU = Maximum Transmission Unit
  Largest IP packet that a link supports
Path MTU (PMTU) = minimum end-to-end MTU
  Must keep datagrams no larger to avoid fragmentation
How does the sender know the PMTU is?
Strategy (RFC 1191):
  Try a desired value
  Set DF to prevent fragmentation
  Upon receiving Need Fragmentation ICMP …
    … oops, that didn’t work, try a smaller value

## Slide 56: Issues with Path MTU Discovery
What set of values should the sender try?
  Usual strategy: work through “likely suspects”
  E.g., 4352 (FDDI), 1500 (Ethernet), 1480 (IP-in-IP over Ethernet), 296 (some modems)
What if the PMTU changes? (how could it?)
  Sender will immediately see reductions in PMTU (how?)
  Sender can periodically try larger values
What if Needs Fragmentation ICMP is lost?
  Retransmission will elicit another one
How can The Whole Thing Fail?
  “PMTU Black Holes”: routers that don’t send the ICMP

## Slide 57: Discovering Routing via Time Exceeded
host
DNS
...
host
host
DNS
...
router
router
router
host
1.2.3.7
8.9.10.11
5.6.7.156
Host sends an IP packet
  Each router decrements the time-to-live field
If TTL reaches 0
  Router sends Time Exceeded ICMP back to the source
  Message identifies router sending it
    Since ICMP is sent using IP, it’s just the IP source address
    And can use PTR record to find name of router
Time exceeded

## Slide 58: Traceroute: Exploiting Time Exceeded
Time-To-Live field in IP packet header
  Source sends a packet with TTL ranging from 1 to n
  Each router along the path decrements the TTL
  “TTL exceeded” sent when TTL reaches 0
Traceroute tool exploits this TTL behavior
source
destination
TTL=1
Time
exceeded
TTL=2
Send packets with TTL=1, 2, …
and record source of Time Exceeded message

## Slide 59
traceroute to www.whitehouse.gov (204.102.114.49),
30 hops max, 40 byte packets

## Slide 60
traceroute to www.whitehouse.gov (204.102.114.49),
30 hops max, 40 byte packets
1 cory115-1-gw.EECS.Berkeley.EDU (128.32.48.1)
0.829 ms 0.660 ms 0.565 ms

## Slide 61
traceroute to www.whitehouse.gov (204.102.114.49),
30 hops max, 40 byte packets
1 cory115-1-gw.EECS.Berkeley.EDU (128.32.48.1)
0.829 ms 0.660 ms 0.565 ms
2 cory-cr-1-1-soda-cr-1-2.EECS.Berkeley.EDU (169.229.59.233)
0.953 ms 0.857 ms 0.727 ms

## Slide 62
traceroute to www.whitehouse.gov (204.102.114.49),
30 hops max, 40 byte packets
1 cory115-1-gw.EECS.Berkeley.EDU (128.32.48.1)
0.829 ms 0.660 ms 0.565 ms
2 cory-cr-1-1-soda-cr-1-2.EECS.Berkeley.EDU (169.229.59.233)
0.953 ms 0.857 ms 0.727 ms
3 soda-cr-1-1-soda-br-6-2.EECS.Berkeley.EDU (169.229.59.225)
1.461 ms 1.260 ms 1.137 ms
4 g3-8.inr-202-reccev.Berkeley.EDU (128.32.255.169)
1.402 ms 1.298 ms *
5 ge-1-3-0.inr-002-reccev.Berkeley.EDU (128.32.0.38)
1.428 ms 1.889 ms 1.378 ms
6 oak-dc2--ucb-ge.cenic.net (137.164.23.29)
1.731 ms 1.643 ms 1.680 ms
7 dc-oak-dc1--oak-dc2-p2p-2.cenic.net (137.164.22.194)
3.045 ms 1.640 ms 1.630 ms
8 * * *
9 dc-lax-dc1--sac-dc1-pos.cenic.net (137.164.22.126)
13.104 ms 13.163 ms 12.988 ms
10 137.164.22.21 (137.164.22.21)
13.328 ms 42.981 ms 13.548 ms
11 dc-tus-dc1--lax-dc2-pos.cenic.net (137.164.22.43)
18.775 ms 17.469 ms 21.652 ms
12 a204-102-114-49.deploy.akamaitechnologies.com (204.102.114.49)
18.137 ms 14.905 ms 19.730 ms
Lost Reply
Router doesn't send ICMPs
Final Hop
No PTR record for address