## Slide 1: Miscellaneous Topics
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 2: Q/A on Project 3

## Slide 3: Today’s Lecture: Dim Sum of Design
Quality-of-Service
Multicast
Announcements…
Wireless addendum
Advanced CC addendum

## Slide 4: Extending the Internet Service Model

## Slide 5: Internet Service Model
Best-Effort: everyone gets the same service
  No guarantees
Unicast: each packet goes to single destination

## Slide 6: Extending the service model
Better than best-effort: Quality of Service (QoS)
More than one receiver: Multicast

## Slide 7: Quality of Service (QoS)

## Slide 8: Summary of Current QoS Mechanisms
Blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, priority scheduling, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah, blah….

## Slide 9: Multicast

## Slide 10: Motivating Example: Internet Radio
Internet concert
  More than 100,000 simultaneous online listeners
  Could we do this with parallel unicast streams?
Bandwidth usage
  If each stream was 1Mbps, concert requires > 100Gbps
Coordination
  Hard to keep track of each listener as they come and go
Multicast addresses both problems….

## Slide 11: Unicast approach does not scale…
Backbone
ISP
Broadcast
Center

## Slide 12: Instead build data replication trees
Backbone
ISP
Broadcast
Center
Copy data at routers
At most one copy of a data packet per link
LANs implement link layer multicast by broadcasting
Routers keep track of groups in real-time
Routers compute trees and forward packets along them

## Slide 13: Multicast Service Model
Receivers join multicast group with address G
Sender(s) send data to address G
Network routes data to each of the receivers
Multicast both delivery and rendezvous mechanism
  Senders don’t know list of receivers
  The latter is often more important than the former
R0 joins G
R1 joins G
Rn joins G
S
R0
R1
.
.
.
[G, data]
[G, data]
[G, data]
[G, data]
Rn
Net
Notes: Stay on this slide a bit…..

## Slide 14: Multicast and Layering
Multicast can be implemented at different layers
  Link layer
    e.g. Ethernet multicast
  Network layer
    e.g. IP multicast
  Application layer
    e.g. End system multicast
Each layer has advantages and disadvantages
  Link: easy to implement, limited scope
  IP: global scope, efficient, but hard to deploy
  Application: less efficient, easier to deploy [not covered]
Notes: Bandwidth plentiful in link; don’t worry about wasting

## Slide 15: Multicast Implementation Issues
How is join implemented?
How is send implemented?
How much state is kept and who keeps it?

## Slide 16: Link Layer Multicast
Join group at multicast address G
  NIC normally only listens for packets sent to unicast address A and broadcast address B
  After being instructed to join group G, NIC also listens for packets sent to multicast address G
Send to group G
  Packet is flooded on all LAN segments, like broadcast
Scalability:
  State: Only host NICs keep state about who has joined
  Bandwidth: Requires broadcast on all LAN segments
Limitation: just over single LAN

## Slide 17: Network Layer (IP) Multicast
Performs inter-network multicast routing
  Relies on link layer multicast for intra-network routing
Portion of IP address space reserved for multicast
  228 addresses for entire Internet
Open group membership
  Anyone can join (sends IGMP message)
    Internet Group Management Protocol
  Privacy preserved at application layer (encryption)
Anyone can send to group
  Even nonmembers

## Slide 18: How Would YOU Design this?
5 Minutes….

## Slide 19: IP Multicast Routing
Intra-domain (know the basics here)
  Source Specific Tree: Distance Vector Multicast Routing Protocol (DVRMP)
  Shared Tree: Core Based Tree (CBT)
Inter-domain [not covered]

## Slide 20: Distance Vector Multicast Routing Protocol
Elegant extension to DV routing
  Using reverse paths!
Use shortest path DV routes to determine if link is on the source-rooted spanning tree
Three steps in developing DVRMP
  Reverse Path Flooding
  Reverse Path Broadcasting
  Truncated Reverse Path Broadcasting (pruning)

## Slide 21: Reverse Path Flooding (RPF)
If incoming link is shortest path to source
Send on all links except incoming
Otherwise, drop
Issues: (fixed with RPB)
Some links (LANs) may receive multiple copies
Every link receives each multicast packet
s:2
s
s:1
s:3
s:2
s:3
r

## Slide 22: Other Problems
Flooding can cause a given packet to be sent multiple times over the same link
Solution: Reverse Path Broadcasting
x
y
z
S
a
b
duplicate packet

## Slide 23: Reverse Path Broadcasting (RPB)
x
y
z
S
a
b
5
6
child link of x
for S
forward only
to child link
Parent of z on
reverse path
Choose single parent for each link along reverse shortest path to source
Only parent forwards to child link
Identifying parent links
  Distance
  Lower address as tie-breaker

## Slide 24: Even after fixing this, not done
This is still a broadcast algorithm – the traffic goes everywhere
Need to “Prune” the tree when there are subtrees with no group members
Networks know they have members based on IGMP messages
Add the notion of “leaf” nodes in tree
  They start the pruning process

## Slide 25: Pruning Details
Prune (Source,Group) at leaf if no members
  Send Non-Membership Report (NMR) up tree
If all children of router R send NMR, prune (S,G)
  Propagate prune for (S,G) to parent R
On timeout:
  Prune dropped
  Flow is reinstated
  Down stream routers re-prune
Note: a soft-state approach

## Slide 26: Distance Vector Multicast Scaling
State requirements:
  O(Sources  Groups) active state
How to get better scaling?
  Hierarchical Multicast
  Core-based Trees

## Slide 27: Core-Based Trees (CBT)
Pick “rendevouz point” for the group (called core)
Build tree from all members to that core
  Shared tree
More scalable:
  Reduces routing table state from O(S x G) to O(G)

## Slide 28: Use Shared Tree for Delivery
Group members: M1, M2, M3
M1 sends data
root
M1
M2
M3
control (join) messages
data

## Slide 29: Core-Based Tree Approach
Build tree from all members to core or root
  Spanning tree of members
Packets are broadcast on tree
  We know how to broadcast on trees
Requires knowing root per group

## Slide 30: Barriers to Multicast
Hard to change IP
  Multicast means changes to IP
  Details of multicast were very hard to get right
Not always consistent with ISP economic model
  Charging done at edge, but single packet from edge can explode into millions of packets within network

## Slide 31: Multicast vs Caching
If delivery need not be simultaneous, caching (as in CDNs) works well, and needs no change to IP

## Slide 32: Announcements

## Slide 33: Clarification on Homework 3
All links in the homework are full duplex.
  Can send full line rate in both directions simultaneously

## Slide 34: Announcements
HW4 will just be a nongraded worksheet
Review sessions (i.e., extended office hours) will be scheduled during class time of reading week
  Will ask you to send in questions beforehand….
In response to several queries, sometime after the SDN lecture I will give a short (and very informal) talk on my experience with Nicira.

## Slide 35: Wireless Review

## Slide 36: History
MACA proposal: basis for RTS/CTS in lecture
  MACA proposed as replacement for carrier sense
  Contention is at receiver, but CS detects sender!
MACAW paper: extended and altered MACA
  Implications of data ACKing
  Introducing DS in exchange: RTS-CTS-DS-Data-ACK
    Shut up when hear DS or CTS (DS sort of like carrier sense)
  Other clever but unused extensions for fairness, etc.
802.11: uses carrier sense and RTS/CTS
  RTS/CTS often turned off, just use carrier sense
  When RTS/CTS turned on, shut up when hear either
  RTS/CTS augments carrier sense

## Slide 37: Why Isn’t MACA Enough?
That’s what we now discuss, by repeating a few slides from previous lecture
In what follows, we assume that basic reception is symmetric (if no interference):
  If A is in range of B, then B is in range of A
Any asymmetries in reception reflect interference from other senders

## Slide 38: Hidden Terminals: Why MACA is Needed
38
A, C can both send to B but can’t hear each other
  A is a hidden terminal for C and vice versa
Carrier Sense by itself will be ineffective
  If A is already sending to B, C won’t know to defer…
A
B
C
transmit range
Notes: 38

## Slide 39: Exposed Terminals: Alleged Flaw in CS
39
Exposed node: using carrier sense
  B sends a packet to A
  C hears this and decides not to send a packet to D
  Despite the fact that this will not cause interference!
Carrier sense prevents successful transmission!
A
B
C
D
Notes: 39

## Slide 40: Key Points in MACA Rationale
No concept of a global collision
  Different receivers hear different signals
  Different senders reach different receivers
Collisions are at receiver, not sender
  Only care if receiver can hear the sender clearly
  It does not matter if sender can hear someone else
  As long as that signal does not interfere with receiver
Goal of protocol:
  Detect if receiver can hear sender
  Tell senders who might interfere with receiver to shut up

## Slide 41: What Does This Analysis Ignore?
Data should be ACKed!
  In wireless settings, data can be easily lost
  Need to give sender signal that data was received
How does that change story?
Connection is now two-way!
  Congestion is at both sender and receiver
  Carrier-sense is good for detecting the former
  MACA is good for detecting the latter

## Slide 42: Exposed Terminals Revisited
42
Exposed node: with only MACA, both B and C send
But when A or D send ACKs, they won’t be heard!
Carrier-sense prevents B, C sending at same time
A
B
C
D
Notes: 42

## Slide 43: 802.11 Overview (oversimplified)
Uses carrier sense and RTS/CTS
  RTS/CTS often turned off, just use carrier sense
If RTS/CTS turned on, shut up when hear either
  CTS
  Or current transmission (carrier sense)
What if hear only RTS, no CTS or transmission?
  You can send (after waiting small period)
    CTS probably wasn’t sent

## Slide 44: What Will Be on the Final?
General awareness of wireless (lecture, section)
Reasoning about a given protocol
  If we used the following algorithm, what would happen?
You are not expected to know which algorithm to use; we will tell you explicitly:
  RTS/CTS
  Carrier Sense
  Both

## Slide 45: Back to Congestion Control

## Slide 46: Quick Review of Advanced CC
Full queues: RED
Non-congestion losses: ECN
High-speeds: Alter constants: HSTCP
Fairness: Need isolation
Min. flow completion time: Need better adjustment
Router-Assisted CC: Isolation: WFQ, AFD Adjustment: RCP

## Slide 47: Why is Scott a Moron?
Or why does Bob Briscoe think so?

## Slide 48: Giving equal shares to “flows” is silly
What if you have 8 flows (to different destinations), and I have 4…
  Why should you get twice the bandwidth?
What if your flow goes over 4 congested hops, and mine only goes over 1?
  Why not penalize you for using more scarce bandwidth?
And what is a flow anyway?
  TCP connection
  Source-Destination pair?
  Source?

## Slide 49: flow rate fairness dismantling a religion <draft-briscoe-tsvarea-fair-01.pdf>
Bob Briscoe
Chief Researcher, BT Group
IETF-68 tsvwg Mar 2007
status: individual draft
final intent: informational
intent next: tsvwg WG item after (or at) next draft

## Slide 50: Charge people for congestion!
Use ECN as congestion markers
Whenever I get ECN bit set, I have to pay $$$
No debate over what a flow is, or what fair is…
  Just send your packets and pay your bill
Can avoid charges by sending when no congestion
Idea started by Frank Kelly, backed by much math
  Great idea: simple, elegant, effective

## Slide 51: Why isn’t this the obvious thing to do?
Do you really want to sell links to highest bidder?
  Will you ever bandwidth when Bill Gates is sending?
  He just sends as fast as he can, and pays the bill
Can we embed economics at such a low level?
  Charging mechanisms usually at higher levels
Is this the main problem with congestion control?
  Is this a problem worth solving? Bandwidth caps work…
This approach is fundamentally right…
  …but perhaps not practically relevant

## Slide 52: Datacenter Networks

## Slide 53: What makes them special?
Huge scale:
  100,000s of servers in one location
Limited geographic scope:
  High bandwidth (10Gbps)
  Very low RTT
Extreme latency requirements (especially the tail)
  With real money on the line
Single administrative domain
  No need to follow standards, or play nice with others
Often “green field” deployment
  So can “start from scratch”…

## Slide 54: This means….
Can design “from scratch”
Can assume very low latencies
Need to ensure very low queuing delays
  Both the average, and the tail….
  TCP terrible at this, even with RED
Can assume plentiful bandwidth internally
As usual, flows can be elephants or mice
  Most flows small, most bytes in large flows…

## Slide 55: Deconstructing Datacenter Packet Transport
Mohammad Alizadeh, Shuang Yang, Sachin Katti,
Nick McKeown, Balaji Prabhakar, Scott Shenker
Stanford University U.C. Berkeley/ICSI

## Slide 56: Transport in Datacenters
Latency is King
  Web app response time depends on completion of 100s of small RPCs
  Tail of distribution is particularly important
But, traffic also diverse
  Mice AND Elephants
  Often, elephants are the root cause of latency
Large-scale Web Application
Fabric
Data Tier
App Tier
App
Logic
App
Logic
App
Logic
App
Logic
App
Logic
App
Logic
App
Logic
App
Logic
App
Logic
App
Logic
Alice
Who does she know?
What has she done?
Minnie
Eric
Pics
Videos
Apps

## Slide 57: Transport in Datacenters
Two fundamental requirements
  High fabric utilization
    Good for all traffic, esp. the large flows
  Low fabric latency (propagation + switching)
    Critical for latency-sensitive traffic
Active area of research
  DCTCP[SIGCOMM’10], D3[SIGCOMM’11]
  HULL[NSDI’11], D2TCP[SIGCOMM’12]
  PDQ[SIGCOMM’12], DeTail[SIGCOMM’12]
vastly improve performance,
but very complex

## Slide 58: Goal of pFabric
Subtract complexity, not add to it
Start from scratch and ask:
  What components do we need for DC CC?
  How little mechanism can we get away with?
None of what we say here applies to general CC, it is limited to DC setting

## Slide 59: pFabric in 1 Slide
Packets carry a single priority #
e.g., prio = remaining flow size
pFabric Switches
Very small buffers (e.g., 10-20KB)
Send highest priority / drop lowest priority pkts
  Give priority to packets with least remaining in flow
pFabric Hosts
Send/retransmit aggressively
Minimal rate control: just prevent congestion collapse

## Slide 60: DC Fabric: Just a Giant Switch!
H1
H2
H3
H4
H5
H6
H7
H8
H9

## Slide 61: DC Fabric: Just a Giant Switch!
H1
H2
H3
H4
H5
H6
H7
H8
H9

## Slide 62: DC Fabric: Just a Giant Switch!
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
TX
RX

## Slide 63: DC Fabric: Just a Giant Switch!
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
TX
RX

## Slide 64
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
Objective?
Minimize avg FCT
DC transport = Flow scheduling on giant switch
ingress & egress
capacity constraints
TX
RX

## Slide 65: Min. FCT with Simple Queue
Just use shortest-job first…..
But here we have many inputs and many outputs with capacity constraints at both

## Slide 66: “Ideal” Flow Scheduling
Problem is NP-hard  [Bar-Noy et al.]
  Simple greedy algorithm: 2-approximation
1
2
3
1
2
3

## Slide 67
pFabric Design

## Slide 68: pFabric Switch
Switch Port
7
1
9
4
3
Priority Scheduling send higher priority packets first
Priority Dropping drop low priority packets first
6
3
2
5
small “bag” of packets per-port
prio = remaining flow size

## Slide 69: Near-Zero Buffers
Easiest way to keep delays small?
  Have small buffers!
Buffers are very small (~1 BDP)
  e.g., C=10Gbps, RTT=15µs → BDP = 18.75KB
  Today’s switch buffers are 10-30x larger

## Slide 70: pFabric Rate Control
Priority scheduling & dropping in fabric also simplifies rate control
  Queue backlog doesn’t matter
  Priority packets get through
H1
H2
H3
H4
H5
H6
H7
H8
H9
50% Loss
One task:
Prevent congestion collapse when elephants collide

## Slide 71: pFabric Rate Control
Minimal version of TCP
  Start at line-rate
    Initial window larger than BDP
  No retransmission timeout estimation
    Fix RTO near round-trip time
  No fast retransmission on 3-dupacks
    Allow packet reordering

## Slide 72: Why does this work?
Key observation:
Need the highest priority packet destined for a port available at the port at any given time.
Priority scheduling
  High priority packets traverse fabric as quickly as possible
What about dropped packets?
  Lowest priority → not needed till all other packets depart
  Buffer larger than BDP → more than RTT to retransmit

## Slide 73: Evaluation
55% of flows
3% of bytes
5% of flows
35% of bytes
54 port fat-tree: 10Gbps links, RTT = ~12µs
Realistic traffic workloads
  Web search, Data mining
* From Alizadeh et al.
[SIGCOMM 2010]
<100KB
>10MB

## Slide 74: Evaluation: Mice FCT (<100KB)
Average
99th Percentile
Near-ideal: almost no jitter

## Slide 75: Evaluation: Elephant FCT (>10MB)
Congestion collapse
at high load w/o rate control

## Slide 76: Summary
pFabric’s entire design:
Near-ideal flow scheduling across DC fabric
Switches
  Locally schedule & drop based on priority
Hosts
  Aggressively send & retransmit
  Minimal rate control to avoid congestion collapse