## Slide 1: Network Security (and related topics)
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 2: Next Week
No sections
No lecture on Thursday
On Tuesday we will talk about SDN

## Slide 3: Agenda
Project 3 Q/A (10)
Network Security (20)
Dealing with Persistent Route Failures (20) [Colin]
More network security (15)
Datacenter Congestion Control (15, if time)

## Slide 4: Project 3 Q/A
Last chance to grill Panda…..

## Slide 5: Network Security
narrowly defined….

## Slide 6: My definition of “network security”
“network security” ≠ “security in a connected world”
  For the latter, take CS 161 (spectacular course!)
If network magically transfers data between known parties, there is no “network security” problem
There are many other security problems
  Distributed system (if A lies to B, does system crash?)
  Operating system (Can A’s system be compromised?)
  …
But these may not require network solutions

## Slide 7: Examples: Non-network security issues
Browser “drive-by” exploits
Server vulnerabilities
Spam
Phishing
Account theft
….

## Slide 8: Two Kinds of Network Security Goals
Core concern: accomplishing communication
  Getting the data from A to B intact
  Knowing it was from intended party, to intended party
Also: Keeping bystanders as ignorant as possible
  Making sure C, D, etc. don’t know what A and B did

## Slide 9: Core Security Requirements
Availability: Will the network deliver data?
Authentication: Who is sending me data?
Integrity: Do messages arrive in original form?
Provenance: Who is responsible for this data?
  Not who sent the data, but who created it
  Important because communication may not be directly between actors, but through intermediaries

## Slide 10: Keeping Bystanders Ignorant
Privacy: can others read data I send?
Anonymity: can I avoid revealing my identity?
Freedom from traffic analysis: can someone tell when I am sending and to whom?
Today, will ignore latter two and focus on privacy
But first, how would you achieve these two goals?
  Assume all the crypto you want….

## Slide 11: Back to other goals
Availability
Authentication
Integrity
Provenance
Privacy

## Slide 12: Public Key Crypto Provides
Way to authenticate yourself: signature
Way to ensure privacy: encryption
  with rcvr’s public key
Way to verify integrity: hash function (or MAC)
Way to verify provenance: signature
In short, crypto provides all but availability!
  Will return to availability later, focus on crypto for now

## Slide 13: On Cryptography and Identities

## Slide 14: Crypto is about algorithms…..
…algorithms that enable or prevent certain actions
  Enable authentication and provenance
  Prevent eavesdropping and undetectable tampering
But security also requires tying actions to identities
  Who is contacting me?
And identities are not purely algorithmic

## Slide 15: Three Aspects of Identities
Real-world identities (RWI)
  This is who you are in the real world
  RWI established by social interactions
    Direct experience
    Referrals from friends
    ….
Names
  Used in network protocols (e.g., DNS, URLs)
Keys
  Used by crypto

## Slide 16: Security requires binding all three…
Protocols: to ensure that they are interacting with appropriate entity, name must be bound to key
  When accessing CNN.com, I need to know CNN’s key in order to make sure that I’m not being spoofed
Humans: to ensure that they are interacting with appropriate entity, name must be bound to RWI
  I need to know that CNN.com is the news organization based in Atlanta, not the Canadian Numismatic Network
Once names are bound to both keys and RWI
  Then keys and RWI are indirectly bound together

## Slide 17: Current Approach
Google, human interactions: bind RWI to names
  Works pretty well when you start with RWI and find name
  Works less well when presented with name…
    …and you are left to guess the RWI (phishing!)
Certificate authorities bind names to keys
  Binding is done via digital certificates
  This does not work well…

## Slide 18: The evolution of a cynic….
“Commercial certificate authorities protect you from anyone from whom they are unwilling to take money.”
  Matt Blaze 2001
“A decade ago, I observed that commercial certificate authorities protect you from whom they are unwilling to take money. That turns out to be wrong; they don’t even do that much.”
  Matt Blaze 2010

## Slide 19: Deeper problem with this approach
Network: needs binding between names and key
  Fetches data based on name
  Authenticates based on keys
Human: needs binding between RWI and name
  Human makes decisions based on RWI
  Humans must be involved in anything concerning RWI
Current approach requires external authority to make the binding the network needs
  Ties network infrastructure to external authorities

## Slide 20: An Alternative Approach
Use self-certifying names
  Make your name the hash of your public key
  Then the binding between names and keys is inherent
  The network need not turn to external authorities
Binding between RWI and names is flexible
  Requires human-level interactions and judgements
    How do I decide a name represents my brother?
    Does same mechanism give name representing Barack Obama?
  Already done reasonably well by Google, etc.
  But is independent of low-level network mechanisms
    So it can evolve!
    Different people can use different mechanisms

## Slide 21: Trust vs Identity
Knowing who you are dealing with is different than trusting them
Trust is a completely different concept, that should lie outside the architecture
We often refer to mechanisms that bind names to keys or RWIs as “trust” mechanisms
  Terrible terminology

## Slide 22: Back to security goals
Availability
Authentication
Integrity
Provenance
Privacy

## Slide 23: Protecting Availability

## Slide 24: How can availability be harmed?
Problems in basic protocols
  Persistent outages due to natural events (Colin)
External vulnerabilities in basic protocols
  Attackers can prevent protocols from functioning
Internal vulnerabilities in basic protocols
  If attackers compromise routers, can prevent network from functioning
Denial-of-service attacks
  Overwhelming the data plane with traffic

## Slide 25: Colin will present recent research…

## Slide 26: How can availability be harmed?
Problems in basic protocols
  Persistent outages due to natural failures (Colin)
External vulnerabilities in basic protocols
  Attackers can prevent protocols from functioning
Internal vulnerabilities in basic protocols
  If attackers compromise routers, can prevent network from functioning
Denial-of-service attacks
  Overwhelming the data plane with traffic

## Slide 27: Examples of external vulnerabilities
TCP:
  Spoofing RST: requires knowing port/seq. no
  Spoofing data: requires knowing port/seq. no
  Cheating CC: reducing available bandwidth
DHCP:
  Spoof DHCP: can set host’s DNS server and gateway
    See all a host’s traffic
    Redirect connections to site’s of your choosing
DNS:
  Cache poisoning

## Slide 28: Note: semantics can be guarded
If crypto is used everywhere (which it isn’t), then you can always prevent hosts from being fooled
But you can’t prevent them from wasting time with incorrect accesses, etc., and thereby not getting the data they want in a timely fashion….

## Slide 29: How can availability be harmed?
Problems in basic protocols
  Persistent outages due to natural failures (Colin)
External vulnerabilities in basic protocols
  Attackers can prevent protocols from functioning
Internal vulnerabilities in basic protocols
  If attackers compromise routers, can prevent network from functioning
Denial-of-service attacks
  Overwhelming the data plane with traffic

## Slide 30: Example of internal vulnerability: BGP
Why Google Went Offline Today and a Bit about How the Internet Works (November 6, 2012)
“Someone at Moratel likely "fat fingered" an Internet route. PCCW, who was Moratel's upstream provider, trusted the routes Moratel was sending to them. And, quickly, the bad routes spread. It is unlikely this was malicious, but rather a misconfiguaration or an error evidencing some of the failings in the BGP Trust model.”

## Slide 31: BGP: Naïve Trust Model
BGP assumes routes are valid
  Even when they are clearly not!
How could we fix this?
  Based on what we have discussed today

## Slide 32: Solution to BGP Problem
Bind prefixes to ASes
  Registry of some kind
Bind keys to ASes
  Using certificate authorities
Each route announcement must have signatures for each step (including originating prefix)

## Slide 33: Easier solution
Have BGP route on AS names
Have AS names be self-certifying
No external binding needed!

## Slide 34: How can availability be harmed?
Problems in basic protocols
  Persistent outages due to natural failures (Colin)
External vulnerabilities in basic protocols
  Attackers can prevent protocols from functioning
Internal vulnerabilities in basic protocols
  If attackers compromise routers, can prevent network from functioning
Denial-of-service attacks
  Overwhelming the data plane with traffic

## Slide 35: Denial of Service (DoS)
Attacker prevents legitimate users from using something (network, server)
Motives?
  Retaliation
  Extortion (e.g., betting sites just before big matches)
  Commercial advantage (disable your competitor)
  Cripple defenses (e.g., firewall) to enable broader attack
Often done via some form of flooding
Can be done at different semantic levels
  Network: clog a link or router with a huge rate of packets
  Transport: overwhelm victim’s ability to handle connections
  Application: overwhelm victim’s ability to handle requests

## Slide 36: DoS: Network Flooding
Goal is to clog network link(s) leading to victim
  Either fill the link, or overwhelm their routers
  Users can’t access victim server due to congestion
Attacker sends traffic to victim as fast as possible
  It will often use (many) spoofed source addresses …
Using multiple hosts (slaves, or zombies) yields a Distributed Denial-of-Service attack, aka DDoS
Traffic is varied (sources, destinations, ports, length) so no simple filter matches it
If attacker has enough slaves, often doesn’t need to spoof - victim can’t shut them down anyway! :-(

## Slide 37: Distributed Denial-of-Service (DDoS)
Master
Slave 1
Slave 3
Slave 4
Slave 2
Victim
Control traffic directs slaves at victim
src = random dst = victim
Slaves send streams of traffic (perhaps spoofed) to victim

## Slide 38: Very Nasty DoS Attack: Reflectors
Reflection
  Cause one non-compromised host to help flood another
  E.g., host A sends DNS request or TCP SYN with source V to server R.
Reflector (R)
Internet
Attacker (A)
R
V
Victim (V)

## Slide 39: Very Nasty DoS Attack: Reflectors
Reflection
  Cause one non-compromised host to attack another
  E.g., host A sends DNS request or TCP SYN with source V to server R.
  R sends reply to V
Reflector (R)
Internet
Attacker (A)
V
R
Victim (V)

## Slide 40: Diffuse DDoS: Reflector Attack
Master
Slave 1
Slave 3
Slave 4
Slave 2
Victim
Control traffic directs slaves at victim & reflectors
Request: src = victim dst = reflector
Reflectors send streams of non-spoofed but unsolicited traffic to victim
Reflector 1
Reflector 9
Reflector 4
Reflector 2
Reflector 3
Reflector 5
Reflector 6
Reflector 7
Reflector 11
Reflector 8
Reflector 10
Reply: src = reflector dst = victim

## Slide 41: Defending Against Network Flooding
How do we defend against such floods?
Answer: basically, we don’t! Big problem today!
Techniques exist to trace spoofed traffic back to origins, but this isn’t useful in face of a large attack
Techniques exist to filter traffic, but a well-designed flooding stream defies stateless filtering
Best solutions to date:
  Overprovision - have enough raw capacity that it’s hard to flood your links
    Largest confirmed botnet to date: 1.5 million hosts (old!)
    Floods seen to date: 40+ Gbps (old!)
  Distribute your services - force attacker to flood many points
    E.g., the root name servers