## Slide 1: Network Management and Software-Defined Networking (SDN)
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 2: This Week
No sections
No lecture on Thursday
I’m not holding office hours tonight, or on Thursday
  I just held office hours, so you missed your chance!
Project 3 part 2 is out today
  Panda will now take questions

## Slide 3: Coming Soon: EE122 Top Gun
Who can design the best routing algorithm?
We will use routing framework from project 2
  You design a routing algorithm
  We come up with test cases
Whoever delivers the most packets wins
Prizes:
  First prize: dinner with the TAs at a fine restaurant
  Second prize: chocolate from my private collection
  No extra credit, just bragging rights

## Slide 4: You can play with the code now…
Code and rules are online….
Quick preview:
  Do not ask TAs anything, ever, period.
  Do not post on Piazza about your solution
  Submit bugs by email to Panda
After you’ve looked at the rules and code, email Panda if you want to participate (see rules)

## Slide 5: Last three lectures
Today: Introduction to SDN
  An exercise in thinking radically
Tuesday: Implications of SDN
  An exercise in thinking architecturally
Thursday: P2P and the triumph of the Internet
  An exercise in thinking egotistically

## Slide 6: Software-Defined Networking: Caveats and Context

## Slide 7: Caveats
I cofounded a startup (Nicira) that worked on SDN
  My views may be biased
  I have no financial interest in the outcome, just ego
SDN is not a revolutionary technology…
  …just a way of organizing network functionality
But that’s all the Internet architecture is….
  The Internet architecture isn’t clever, but it is deeply wise
  We know SDN isn’t clever, but we hope it is wise….

## Slide 8: Some context before we go further…
Where did SDN come from?
And what is the state of networking as a field?
Keep context in mind as you learn about SDN…

## Slide 9: Where did SDN come from?
~2004: Research on new management paradigms
  RCP, 4D [Princeton, CMU,….]
  SANE, Ethane [Stanford/Berkeley]
  Industrial efforts with similar flavor (not published)
2008: Software-Defined Networking (SDN)
  NOX Network Operating System [Nicira]
  OpenFlow switch interface [Stanford/Nicira]
2011: Open Networking Foundation (72 members)
  Board: Google, Yahoo, Verizon, DT, Msoft, F’book, NTT
  Members: Cisco, Juniper, HP, Dell, Broadcom, IBM,…..

## Slide 10: Where did SDN really come from?

## Slide 11: Martín Casado (from a Wired profile)
“Martin Casado is fucking amazing,” says Scott Shenker, the physics PhD, UC Berkeley computer science professor, and former Xerox PARC researcher who has worked closely with Casado for the past several years on the networking problems Nicira is trying to solve. “I’ve known a lot of smart people in my life, and on any dimension you care to mention, he’s off the scale.”

## Slide 12: Current Status of SDN
SDN widely accepted as “future of networking”
  ~1000 engineers at latest Open Networking Summit
  Commercialized, in production use (few places)
    E.g., controls Google’s WAN; NTT moving to deploy
  Much more acceptance in industry than in academia
An insane level of SDN hype, and backlash…
  SDN doesn’t work miracles, merely makes things easier
But the real question is: why the rapid adoption?

## Slide 13: The Field of Networking…
CS networking now largely the study of the Internet
Also interesting research in wireless, optical
  Much of it is EE research into underlying technologies
  Some wireless research (such at Katabi at MIT) broader
This Internet research effort built a great artifact
  Mostly unrelated to academic research which came later
But it has failed to create an academic discipline
  The fact that EE122 sucks is not my fault!

## Slide 14: Building an Artifact, Not a Discipline
Other fields in “systems”: OS, DB, etc.
  Teach basic principles
  Are easily managed
  Continue to evolve
Networking:
  Teach big bag of protocols
  Notoriously difficult to manage
  Evolves very slowly
Networks are much more primitive and less understood than other computer systems

## Slide 15: We are left with two key questions
Why the rapid adoption of SDN?
  What problem is it solving?
Why is networking behind other fields in CS?
  What is missing in the field?
The answers are related, but will unfold slowly

## Slide 16: Network Management

## Slide 17: What is Network Management?
Recall the two “planes”
Data plane: forwarding packets
  Based on local forwarding state
Control plane: computing that forwarding state
  Involves coordination with rest of system
Broad definition of “network management”:
  Everything having to do with the control plane

## Slide 18: Original goals for the control plane
Basic connectivity: route packets to destination
  Local state computed by routing protocols
  Globally distributed algorithms
Interdomain policy: find policy-compliant paths
  Done by fully distributed BGP
For long time, these were the only relevant goals!
  What other goals are there in running a network?

## Slide 19: Isolation
Want multiple LANs on single physical network
Packets on LAN don’t pass through routers
  But routers used to impose various controls (later)
Use VLANs (virtual LANs) tags in L2 headers
  Controls where broadcast packets go
  Gives support for logical L2 networks
  Routers connect these logical L2 networks
No universal method for setting VLAN state

## Slide 20: Access Control
Operators want to limit access to various hosts
  Don’t let laptops access backend database machines
This can be imposed by routers using ACLs
  ACL: Access control list
Example entry in ACL: <header template; drop>

## Slide 21: Traffic Engineering
Want to avoid persistent overloads on links
Choose routes to spread traffic load across links
Two main methods:
  Setting up MPLS tunnels
  Adjusting weights in OSPF
Often done with centralized computation
  Take snapshot of topology
  Compute appropriate MPLS/OSPF state
  Send to network

## Slide 22: Summarizing
Network management has many goals
Achieving these goals is job of the control plane…
…which currently involves many mechanisms

## Slide 23: Control Plane Mechanisms
Globally distributed: routing algorithms
Manual/scripted configuration: ACLs, VLANs
Centralized computation: Traffic engineering

## Slide 24: Bottom Line
Many different control plane mechanisms
Each designed from scratch for their intended goal
Encompassing a wide variety of implementations
  Distributed, manual, centralized,…
Network control plane is a complicated mess!

## Slide 25: How Did We Get Into This Mess?

## Slide 26: How Have We Managed To Survive?
Net. admins miraculously master this complexity
  Understand all aspects of networks
  Must keep myriad details in mind
This ability to master complexity is both a blessing
  …and a curse!

## Slide 27: A Simple Story About Complexity….
~1985: Don Norman visits Xerox PARC
  Talks about user interfaces and stick shifts

## Slide 28: What Was His Point?
The ability to master complexity is valuable
  But not the same as the ability to extract simplicity
Each has its role:
  When first getting systems to work, master complexity
  When making system easy to use, extract simplicity
You will never succeed in extracting simplicity
  If you don’t recognize it is a different skill set than mastering complexity

## Slide 29: What Is My Point?
Networking has never made the distinction…
  And therefore has never made the transition from mastering complexity to extracting simplicity
Still focused on mastering complexity
  Networking “experts” are those that know all the details
Extracting simplicity lays intellectual foundations
  This is why networking has weak foundation
  We are still building the artifact, not the discipline

## Slide 30: Have answered one of our questions
The reason networking is not a discipline is because it has not sought to extract simplicity
  Other fields, such as OS, DB, etc, have
  Those fields are more mature
Extracting simplicity is also how you generalize to larger, more complicated systems
  So it has practical advantages as well….

## Slide 31: Forcing people to make the transition
We are really good at mastering complexity
  And it has worked for us for decades, why change?
How do you make people change?
  Make them cry!
A personal story about algebra and complexity
  School problems:
  3x + 2y = 8 x + y = 3
  My father’s problems:
  327x + 26y = 8757 45x + 57y = 7776

## Slide 32: Making Network Operators Cry…

## Slide 33: Step 1: Large datacenters
100,000s machines; 10,000s switches
This is pushing the limits of what we can handle….

## Slide 34: Step 2: Multiple tenancy
Large datacenters can host many customers
Each customer gets their own logical network
  Customer should be able to set policies on this network
  ACLs, VLANs, etc.
If there are 1000 customers, that adds 3 oom
  Where oom = orders of magnitude
This goes way beyond what we can handle

## Slide 35: Network Operators Are Now Weeping…
They have been beaten by complexity
The era of ad hoc control mechanisms is over
We need a simpler, more systematic design
So how do you “extract simplicity”?

## Slide 36: An Example Transition: Programming
Machine languages: no abstractions
  Had to deal with low-level details
  Mastering complexity was crucial
Higher-level languages: OS and other abstractions
  File system, virtual memory, abstract data types, ...
Modern languages: even more abstractions
  Object orientation, garbage collection,...
Abstractions key to extracting simplicity

## Slide 37: “The Power of Abstraction”
“Modularity based on abstraction
is the way things get done”
− Barbara Liskov
Abstractions  Interfaces  Modularity

## Slide 38: What About Networking Abstractions?
Consider the data and control planes separately
Different tasks, so naturally different abstractions

## Slide 39: Abstractions for Data Plane: Layers
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits

## Slide 40: The Importance of Layering
Decomposed delivery into basic components
Independent, compatible innovation at each layer
  Clean “separation of concerns”
  Leaving each layer to solve a tractable problem
Responsible for the success of the Internet!
  Rich ecosystem of independent innovation

## Slide 41: Control Plane Abstractions
?

## Slide 42: (Too) Many Control Plane Mechanisms
Variety of goals, no modularity:
  Routing: distributed routing algorithms
  Isolation: ACLs, VLANs, Firewalls,…
  Traffic engineering: adjusting weights, MPLS,…
Control Plane: mechanism without abstraction
  Too many mechanisms, not enough functionality

## Slide 43: Finding Control Plane Abstractions

## Slide 44: How do you find abstractions?
You first decompose the problem….
…and define abstractions for each subproblem
So what is the control plane problem?

## Slide 45: Task: Compute forwarding state:
Consistent with low-level hardware/software
  Which might depend on particular vendor
Based on entire network topology
  Because many control decisions depend on topology
For all routers/switches in network
  Every router/switch needs forwarding state

## Slide 46: Our current approach
Design one-off mechanisms that solve all three
A sign of how much we love complexity
No other field would deal with such a problem!
They would define abstractions for each subtask
…and so should we!

## Slide 47: Separate Concerns with Abstractions
Be compatible with low-level hardware/software
  Need an abstraction for general forwarding model
Make decisions based on entire network
  Need an abstraction for network state
Compute configuration of each physical device
  Need an abstraction that simplifies configuration

## Slide 48: Abs#1: Forwarding Abstraction
Express intent independent of implementation
  Don’t want to deal with proprietary HW and SW
OpenFlow is current proposal for forwarding
  Standardized interface to switch
  Configuration in terms of flow entries: <header, action>
Design details concern exact nature of:
  Header matching
  Allowed actions

## Slide 49: Two Important Facets to OpenFlow
Switches accept external control messages
  Not closed, proprietary boxes
Standardized flow entry format
  So switches are interchangable

## Slide 50: Abs#2: Network State Abstraction
Abstract away various distributed mechanisms
Abstraction: global network view
  Annotated network graph provided through an API
Implementation: “Network Operating System”
  Runs on servers in network (“controllers”)
  Replicated for reliability
Information flows both ways
  Information from routers/switches to form “view”
  Configurations to routers/switches to control forwarding

## Slide 51: Network Operating System
Think of it as a centralized link-state algorithm
Switches send connectivity info to controller
Controller computes forwarding state
  Some control program that uses the topology as input
Controller sends forwarding state to switches
Controller is replicated for resilience
  System is only “logically centralized”

## Slide 52: Software Defined Network (SDN)
Control Program
Network OS
Global Network View
Traditional Control Mechanisms
Network of Switches and/or Routers
Distributed algorithm running between neighbors
Complicated task-specific distributed algorithm
routing, access control, etc.

## Slide 53: Major Change in Paradigm
Control program: Configuration = Function(view)
Control mechanism now program using NOS API
Not a distributed protocol, just a graph algorithm

## Slide 54: Abs#3: Specification Abstraction
Control mechanism expresses desired behavior
  Whether it be isolation, access control, or QoS
It should not be responsible for implementing that behavior on physical network infrastructure
  Requires configuring the forwarding tables in each switch
Proposed abstraction: abstract view of network
  Abstract view models only enough detail to specify goals
  Will depend on task semantics

## Slide 55: Simple Example: Access Control
Global
Network View
Abstract Network
View
A
B
A
B

## Slide 56: Software Defined Network
Network OS
Global Network View
Abstract Network View
Control Program
Virtualization Layer

## Slide 57: Clean Separation of Concerns
Control program: express goals on abstract view
  Driven by Operator Requirements
VirtualizationLayer: abstract view  global view
  Driven by Specification Abstraction for particular task
NOS: global view  physical switches
  API: driven by Network State Abstraction
  Switch interface: driven by Forwarding Abstraction

## Slide 58: SDN: Layers for the Control Plane
Network OS
Global Network View
Abstract Network View
Control Program
Network Virtualization

## Slide 59: Abstractions Don’t Remove Complexity
NOS, Virtualization are complicated pieces of code
SDN merely localizes the complexity:
  Simplifies interface for control program (user-specific)
  Pushes complexity into reusable code (SDN platform)
This is the big payoff of SDN: modularity!
  The core distribution mechanisms can be reused
  Control programs only deal with their specific function
Note that SDN separates control and data planes
  SDN platform does control plane, switches do data plane

## Slide 60: Why Does SDN Scale?
Per Packet
Per Flow
Per Network Event
No Consistency
No Consistency
Eventual Consistency
106 – 108/s
103 – 106/s
101 – 103/s
Modification of Control Program
Strong Consistency
0 - 10/s

## Slide 61: What This Really Means

## Slide 62: Routing
Look at graph of network
Compute routes
Give to SDN platform, which passes on to switches

## Slide 63: Access Control
Control program decides who can talk to who
Pass this information to SDN platform
Appropriate ACL flow entries are added to network
  In the right places (based on the topology)

## Slide 64: Common Questions about SDN

## Slide 65: Common Questions about SDN?
Is SDN less scalable, secure, resilient,…?
Is SDN incrementally deployable?
Can SDN be extended to the WAN?
Can you troubleshoot an SDN network?
Is OpenFlow the right fwding abstraction?

## Slide 66: Common Questions about SDN?
Is SDN less scalable, secure, resilient,…? No
Is SDN incrementally deployable? Yes
Can SDN be extended to the WAN? Yes
Can you troubleshoot an SDN network? Yes
Is OpenFlow the right fwding abstraction? No

## Slide 67: Next Time
Extending SDN
Thinking architecturally

## Slide 68: Have a good holiday!
Get some rest….