## Slide 1: Thinking Architecturally (80 Minutes Inside Scott’s Head)
EE122 Fall 2012
Scott Shenker
http://inst.eecs.berkeley.edu/~ee122/
Materials with thanks to Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley

## Slide 2: Announcements
Roughly 60 of you have not yet participated
  If you aren’t sure, check bspace
I will not schedule special office hours for you
  Show up at normal hours, or ask a question in class
I only have office hours tonight and Thursday
  And I will be doing some reviews next week
  Details on Thursday….

## Slide 3: Agenda
MPLS primer
Architecture vs Engineering
Review of SDN
  And its implications
Another functional decomposition
  And its implications

## Slide 4: Warning!
These are recent architectural developments
Still trying to work them through
Will present three different approaches
Not yet clear how they fit together
If you understand this lecture, you will know more about Internet architecture than 99% of networking researchers….

## Slide 5: Rules of Engagement….
If you don’t understand, ask….

## Slide 6: MPLS
Necessary background for today

## Slide 7: Multiprotocol Label Switching (MPLS)
Operators wanted more flexibility in routing traffic
  Normal routing just used destination address…
Wanted ability to route on larger aggregates
  First decide if flow belongs to aggregate, then route agg.
  Example: all traffic from LA to NY follow same path
Wanted ability to route at finer granularity
  Not all packets with same destination take same path
Solution: insert a “label” before IP header
  Route based on that label

## Slide 8: MPLS Header

## Slide 9: Using MPLS
Make a distinction between edge and core routers
Edge routers inspect IP header, insert MPLS label
Core routers route based on MPLS label
Must set up forwarding state for MPLS labels
  Done in a variety of ways, for a variety of goals
  Supporting failover paths, TE,…

## Slide 10: MPLS is widely used
Sometimes used for traffic engineering
But mostly used for VPNs
  Where all a customer’s traffic is given a single label
Extremely important practically, not intellectually
  Because it is not tightly tied to a single purpose
  Each use is ad hoc, rather than an overall paradigm
    Sort of like the IPv6 flow ID: all mechanism, no policy

## Slide 11: Architecture

## Slide 12: Net Management and the E2E Principle
The E2E principle assumes that hosts have goals
  But completely ignores network operators
There are some tasks that can’t be implemented in the host because:
  They require knowledge of the network (TE)
  The host may not share the operator’s goal (ACLs)
  The host may be poorly configured (ACLs)
  ….
Network management requires new principles
  SDN’s layering is one such principle (reviewed today)

## Slide 13: Architecture vs Engineering [Old Slide]
Architecture:
  The allocation of functionality and definition of interfaces among elements
The Internet “architecture” is the decision about what tasks get done, and where:
  In the network, or in the hosts
  Engineering is more about how tasks get done
These architectural decisions play a crucial role in scaling, heterogeneity, robustness, etc…
  This is what I spend my life worrying about

## Slide 14: Architecture in this course…
E2E principle:
  Do things in hosts when you can
Fate sharing:
  Store state where it is needed
Layering:
  Arises from functional decomposition of network delivery
  All modularity follows from decomposition, and modularity is the key to any overall design

## Slide 15: Decomposing Network Delivery
First get bits on wire locally
  No packets or packet headers, just low-level bits
Then find a way to deliver packets locally
  Requires packet headers, but only local addressing
Then find a way to deliver packets globally
  Requires packet headers with global addresses
Then find a way to deliver packets reliably
  Requires ACKing, etc.

## Slide 16: Decomposition leads to layers
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits

## Slide 17: Decomposing the Control Plane

## Slide 18: Control Plane Decomposition
Goal: what are you trying to accomplish?
  Access control: who can reach who?
  Isolation: what are the virtual networks?
Switch configurations needed to implement goal
  What forwarding state is needed to achieve goals?
Gathering information about topology
  Need topology in order to compute forwarding state
Telling switches what to do
  Switches must be given the computed forwarding state

## Slide 19: Controlling Switches
Need protocol to communicate with switches
Need standard way to specify configuration
OpenFlow does both:
  General controller-switch protocol
  Specification of < header ; action > flow entries
    What matches and actions are allowed
    How are they expressed

## Slide 20: Gathering Information About Topology
Need a “network operating system”
  NOX was the first
  Many exist now: ONIX, Floodlight, Trema, POX,….
The NOS runs on servers
Communicates with each switch
Can construct topology from switch information

## Slide 21: Determining Appropriate Configuration
Compute appropriate switch configurations
Given specified control goals (next slide)…
…and topology (previous slide)
Computation depends on details of goals:
  Access control
  Traffic engineering
  …

## Slide 22: Deciding on your goals
Operator decides what needs to be done
Expresses these desires to control program
  Through some UI
  (not standardized, specific to control program)
Which then communicates them to SDN platform
The SDN platform then implements these goals
  First computing appropriate configurations
  Then communicating those configurations to switches

## Slide 23: Interface for control program
Control program needs interface to SDN platform
  Must have some way of communicating intent
Currently, we use an “abstract network view”
  Intent is communicated by configuring simple network

## Slide 24: Abstractions for Control Plane
…built on…
…built on…
…built on…
Expression of Intent
Abstract Network View
Global Network View
Physical Topology

## Slide 25: SDN: Layers for the Control Plane
Network OS
Global Network View
Abstract Network View
Control Program
Network Virtualization

## Slide 26: Clean Separation of Concerns
Control program: express goals on abstract view
VirtualizationLayer: abstract view  global view
NOS: global view  physical switches

## Slide 27: Abstractions for Control Plane
…built on…
…built on…
…built on…
Expression of Intent (Control Program)
Abstract Network View (Virtualization Layer)
Global Network View (NOS)
Physical Topology (Real Network)

## Slide 28: This view is greatly oversimplified
But I won’t tell you in what ways…
…because it would just confuse the picture

## Slide 29: Implications of SDN

## Slide 30: Separation of Control/Data Plane
Today, routers implement both
  They forward packets
  And run the control plane software
SDN networks
  Data plane implemented by switches
    Switches act on local forwarding state
  Control plane implemented by controllers
    All forwarding state computed by SDN platform
This is a technical change, with broad implications

## Slide 31: Old Economic Model
Bought HW/SW from single vendor
  Closed control SW, proprietary forwarding HW
HW deployment needs to be all from one vendor
“Vendor lock-in”

## Slide 32: New Economic Model
Can buy HW from anyone (theoretically)
  HW becomes interchangeable, if it supports OpenFlow
Can buy SW from anyone
  Runs on controllers, so doesn’t need to run on switch
SDN platform sold separately from control pgrms?
  Would require stable and open platform interface
  Currently a debate within ONF….
Much less lock in (we hope)

## Slide 33: Role of OpenFlow
Architecturally: boring
  Just a switch specification….zzzzzz
Economically: hugely important
  Could help break HW vendor lock-in

## Slide 34: Changes the Testing Model
Unit test hardware
  The forwarding abstraction is well specified
  Completely separate from control plane
Use simulator to analyze large-scale control planes
  External events are input to simulation
  Can do regression testing
Much wider testing coverage than is possible today
  Today use physical testbeds, limited in size/scope

## Slide 35: Which Then Changes Deployment…
Before SDN, upgrades were scary and rare events
  Code was not well tested (because it was hard to test)
  And could only come from hardware vendor
With SDN, upgrades can be easy and frequent
  Much better testing
  And the software can come from anyone
Rate of innovation will be much greater!
  Old: innovation mainly to get customers to buy new HW
  SDN: innovation to make customers happier!

## Slide 36: What is SDN’s “Killer App”?
Notes: All that technical material in the past 20 slides was to convince you that SDN simplified network management. But just because SDN is a good idea doesn’t mean It would get adopted. So why is SDN on the fast track to adoption?

## Slide 37: Current Networks: Topology = Policy
Network topology determines:
  Broadcast domains
  Effectiveness of ACLs and firewalls
  Equivalence classes
  …
When moving net to cloud, want to retain policy
  But often don’t have abstract formulation of that policy

## Slide 38: SDN and Multitenant Datacenters
SDN allows users to specify virtual topology
  Each tenant can specify own topology (i.e., policy)
SDN-enabled cloud network implements policies
  SDN compiles set of policies into low-level configuration
Tenants can migrate VMs to/from own network
  Because policies driven from same topology
This is what people are paying money for….
  Enabled by SDN’s ability to virtualize the network

## Slide 39: Research Topics in SDN
Troubleshooting (now)
Scaling (later in lecture)

## Slide 40: Troubleshooting SDNs?
SDN networks introduce layers of abstraction
  Good: makes it easier to write control programs
  Bad: finding the problem when things go wrong
“Going wrong” means packet behaviors do not agree with goals set by control program
  Routing, access control, etc.
Example: control pgrm forbids A from contacting B
  But operators sees packets from A reaching B!

## Slide 41: Must Answer Two Questions
What layer of abstraction caused this error?
  Is the control program wrong?
  Did the SDN platform introduce the error?
    If so, in the NOS or the virtualization layer?
  Did the physical switches malfunction?

## Slide 42: Must Answer Two Questions
What layer of abstraction caused this error?
  Is the control program wrong? [Other work]
  Did the SDN platform introduce the error?
    If so, in the NOS or the virtualization layer?
    Or at what level of the hierarchy?
  Did the physical switches malfunction? [Other work]
What external events triggered this error?
  SDN platform is a complex distributed system
  Subtle errors in responding to controller failures, etc.
  ….

## Slide 43: Identifying the Problematic Events
Controller A
Controller B
Controller C
Switch 1
Switch 2
Switch3
Switch 4
Switch 5
Switch 6
Switch 7
Switch 8
Switch 9
?
Notes: Now this algorithm becomes really useful when you’re running a friggin’ huge datacenter…. 8 Failures/s in a large datacenter
Lots of events: internal, external, etc.

## Slide 44: Leverage Control/Data Plane Split
Replay control plane in simulator
Iteratively remove external events from log
  See if error still occurs
Can programmatically identify a minimal causal set
Focus debugging efforts on a small log of events
Lots of technical difficulties swept under the rug!

## Slide 45: Another Decomposition

## Slide 46: Thinking architecturally
Seeing how network services can be decomposed
But there are many aspects to network service
Dataplane considers how packets are handled
Our control plane discussion only considers at how operator controls network
What about another decomposition that takes hosts and forwarding into account

## Slide 47: Three Important Logical Interfaces
Host to network: destination, QoS requirements
Packet to router: lookup key into forwarding state
Operator to network: isolation, access control,…

## Slide 48: Interfaces in IP
Host-network and packet-router interfaces are conflated.
  They use same fields
  Every router must interpret host demands
Minimal operator-network interface
  Routing algorithms, ACLs
  Tacked on, not integral to overall design
Host-Network
Packet-Router
Src IP
Dst IP
L4 ...
L2

## Slide 49: Interfaces in OpenFlow
Host-network and packet-router interfaces still conflated
  Same fields still used for both (just more fields)
  All routers have fully general OF matching
But SDN provides programmatic network-operator interface.
  Huge step forward!
Host-Network
Packet-Router
Src IP
Dst IP
L4 ...
L2

## Slide 50: Interfaces in MPLS
Host-network and packet-router interfaces are distinct
  Edge router looks at IP header
  Internal switches look at MPLS label
No fully general operator-network interface
Host-Network (Edge)
Packet-Router (Core)
Src IP
Dst IP
L4 ...
MPLS
Labels
L2

## Slide 51: Need to combine SDN and MPLS
MPLS makes the important distinction between
  Host-network interface
  Packet-switch interface
SDN provides full operator-network interface
The combination of SDN and MPLS looks like this:
  Network core is a “fabric” that delivers packets e2e
  Network edge uses full IP header to make decisions
    Then uses fabric interface to forward across network

## Slide 52: SDN + MPLS = “Fabric”
Dst
Host
Src
Host
Interface for fabric
Src IP
Dst IP
L4 ...
L2
Fabric Header
Interface
for edge
and host
Edge
Switch
Edge
Switch
CE
Fabric
(Switches)
CF

## Slide 53: Fabric Interface
Fabric functions much like a distributed switch
  Delivers packets to appropriate edge ports
  “Transactional” changes for internal forwarding state
  We will call these a “logical cross-bar” (LXB)
Internal hardware is simple and future-proof:
  Fabric only requires simple label forwarding internally
  Only edge switches tied to host protocols
Normal SDN needs general matching everywhere
  This SDN approach only uses general matching at edge

## Slide 54: Core-Edge Distinction
Has far-reaching implications for SDN’s future
  Scalability
  Deployability
  Evolvability
  ….

## Slide 55: Scalability

## Slide 56: Scaling SDN
What about global networks?
  Can’t have a flat organization of replicated controllers
  Need more locality of control
Can organize network into a hierarchical structure
  Each unit of the hierarchy is a logical xbar (LXB)
Each LXB
  Given forwarding table by parent
  Gathers topology from children
  Controller implements Table on Topology

## Slide 57: Example
Level 0 LXBs: physical switches

## Slide 58: Level 1 LXBs: PoPs
Notes: Those individual LXBs are then connected together. But now we would like to control this infrastructure from a single point and present it as a single abstraction so we are going to enlarge our abstraction.

## Slide 59: Level 2 LXBs: Regional Networks
Notes: So we now instantiate yet another LXB on top of our other LXBs. But these are still seem as two disjoint elements.

## Slide 60: Level 3 LXB: Global Network
Ports attached to stub networks
LXB forwards between them
Notes: Therefore we instantiate another LXB and we do this for all levels until we reach a single gigantic LXB.

## Slide 61: What’s New Here?
Recursive application of basic “fabric” control
Can use same controller codebase for each level
  Topology state from children
  Forwarding table from parent
  Controller figures out to implement Table on Topology
Overall structure has desirable properties:
  Transactional model for network state changes
  Bounded depth of computation for state changes

## Slide 62: Deployability

## Slide 63: Fact
Most functionality can be implemented at edge
  Access control
  Isolation
  ….
This is implicit in the notion of “fabrics”
  Fabric has simple service model
  But makes sophisticated decisions at edge
    Whether to forward
    Where to forward
    …

## Slide 64: Current Networks Are Like Fabrics
They provide edge-to-edge delivery
To provide SDN-like benefits, merely add SDN-based switches at edge
Use legacy equipment in core of network
Simplifies deployment

## Slide 65: Virtualization makes this even easier…
Virtualization (VMs) is supported by hypervisors
Hypervisors use software switch to connect VMs
Make this software switch SDN-compatible
  And you’ll be able to deploy SDN without any new HW
Open vSwitch is now in Linux, Xen, and coming soon to other Oses and hypervisors
SDN now deployable without any HW deployment!

## Slide 66: Network in Regular Setting
Host
Host
Host
Host
Physical Switch

## Slide 67: Network in Virtualized Setting
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM

## Slide 68: Virtual Switches (Vswitch)
Virtual Switch
VM
VM
VM
VM
Vswitch is first-hop switch for all VMs
  Software switch (speed is not an issue)
  Should support OpenFlow
  Can be controlled by Network Operating System

## Slide 69: Physical View of Virtualized Network
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM

## Slide 70: Logical View of Virtualized Network
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
All edge switches are Vswitches

## Slide 71: Vswitches are Sufficient
Vswitches are enough to implement most functions
  Access control, QoS, mobility, migration, monitoring,…
Physical network becomes static crossbar
  Simple to implement and manage
  Components can be legacy and static

## Slide 72: Managing Physical Network
NOS
Physical Switches

## Slide 73: Managing Virtualized Network
Physical network is logical crossbar
NOS
Only Vswitches need to be controlled by NOS

## Slide 74: Vswitches as Insertion Point
Can insert new functionality into old networks with:
  Hypervisors with OpenFlow-enabled Vswitch
  Network Operating System (on servers)
No change to physical infrastructure
  Legacy hosts
  Legacy network components

## Slide 75: Evolvability

## Slide 76: Implications
Domains can be build like “fabrics”
Edge uses software forwarding
  Controlled by edge controller
Core uses hardware label-based forwarding
Only edge understands interdomain delivery
  Change in “architecture” (e.g., IPv4 to IPv6) only requires change to edge controller software
  Software-defined Internet Architecture

## Slide 77: Software-Defined Internet Architecture
Major architectural changes via edge software
Software switches are fast enough to handle load
  Single core can do ~10Gbps
No need for architectural support inside domain
  At least not initially
No need for a single global internetworking layer
  A repudiation of the core Internet belief
  Can have several such layers coexist