## Slide 1: Wireless – there is no cat!
EE 122: Intro to Communication Networks
Materials with thanks to Scott Shenker, Jennifer Rexford, Ion Stoica, Vern Paxson and other colleagues at Princeton and UC Berkeley
"You see, wire telegraph is a kind of a very, very long cat. You pull his tail in New York and his head is meowing in Los Angeles. And radio operates exactly the same way… The only difference is that there is no cat.“
Albert Einstein,
when asked to describe radio.
Yahel Ben-David
Yahel @ eecs.berkeley.edu

## Slide 2
Notes: Rapid evolution in the wireless eco-system – hard to keep up.
Both technologies and business-models

## Slide 3
Metrics for evaluation / comparison of wireless technologies
Bitrate or Bandwidth
Range - PAN, LAN, MAN, WAN
Stationary / Mobile
Two-way / One-way
Digital / Analog
Multi-Access / Point-to-Point
Applications and industries
Operating environment
Frequency / Wavelength
Notes: Bitrate or Bandwidth
Range - PAN, LAN, MAN, WAN
Two-way / One-way
Multi-Access / Point-to-Point
Digital / Analog
Applications and industries
Frequency – Affects most physical properties: Distance (free-space loss) Penetration, Reflection, Absorption Energy proportionality Policy: Licensed / Deregulated
Line of Sight (Fresnel zone)
Size of antenna
(determined by wavelength – )

## Slide 4
Frequency/Wave-Length –
Affects most physical properties: Distance (free-space loss) Penetration, Reflection, Absorption Line of Sight (Fresnel zone)
Size of antenna Energy proportionality
Policy & Law: Licensed / Deregulated
Metrics for evaluation / comparison of wireless technologies
Notes: Frequency is the number of cycles per second.
Wavelength is the length of each cycle (in meters).

## Slide 5
Todo:
Graph: Evolution of wireless communication – bit-rates over time
Notes: Evolution of wireless communication – bit-rates over time

## Slide 6
Modern art?
Notes: Allocated to license holders.
Occasionally (rarely) a chunk gets offered for bidding – for billions of dollars.
Is spectrum a scares resource or just poorly managed?

## Slide 7
Old mess!
Notes: Allocated to license holders.
Occasionally (rarely) a chunk gets offered for bidding – for billions of dollars.
Is spectrum a scares resource or just poorly managed?
Take away spectrum from old analog broadcasters
Enabled roaming (technically and politically).

## Slide 8
The Wireless Spectrum
Notes: FCC allocates spectrum to users – who are these?
Govt. itself (various agencies), military.
Public-safety.
Broadcasters
Telecommunications providers (aka operators) – license holders.
Different bands behave differently …
Most wave propagation properties are frequency/wave-length dependent:

## Slide 9: Common Wireless Standards
Cellular (Typically 800/900/1800/1900Mhz):
  2G: GSM / GPRS /EDGE / CDMA / CDMA2000/
  3G: UMTS/HSDPA/EVDO
  4G: LTE, WiMax
IEEE 802.11 (aka WiFi):
  b: 2.4Ghz band, 11Mbps (~4.5 Mbps operating rate)
  g: 2.4Ghz, 54-108Mbps (~19 Mbps operating rate)
  a: 5.0Ghz band, 54-108Mbps (~19 Mbps operating rate)
  n: 2.4/5Ghz, 150-600Mbps (4x4 mimo).
IEEE 802.15 – lower power wireless:
  802.15.1: 2.4Ghz, 2.1 Mbps (Bluetooth)
  802.15.4: 2.4Ghz, 250 Kbps (Sensor Networks)
9

## Slide 10: Wireless Link Characteristics
10
(Figure Courtesy of Kurose and Ross)
Notes: Naturally – there exist technologies for longer distances…
Also – we already have affordable off-the-shelf gear for gigabit+ speeds…
Why not use any of the outdoors technologies also indoors – surely it would work…?
802.11n can do much faster today – 600Mbps (4x4 MIMO)…

## Slide 11: WTF?

## Slide 12: Antennas / Aerials
An electrical device which converts electric currents into radio waves, and vice versa.
Q: What does “higher-gain antenna” mean?
A: Antennas are passive devices – more gain means focused and more directional. Directionality means more energy gets to where it needs to go and less interference everywhere.
Q: What are omni-directional antennas?
Gain: 2-3dB 8-12dB 15-18dB 28-34dB

## Slide 13: How many radios/antennas ?
WiFi 802.11n - 2.4 & 5Ghz (MiMo?)
2G – GSM “Quad band” 800/900 & 1800/1900
3G – HSDPA+
4G – LTE
Bluetooth
NFC
GPS Receiver
FM-Radio receiver (antenna is the headphones cable)

## Slide 14: What has changed?
Notes: I used to make calls from 40 miles away – not anymore…
Cellular towers climbed down from the mountain-tops in attempt to reduce/contain their footprint.
Analog / Digital
Antenna is bigger (a plus only if upright).
Power (and therefore battery) is higher.
Band 800Mhz AMPS.

## Slide 15: What Makes Wireless Different?
Broadcast medium… - Anybody in proximity can hear and interfere
Cannot receive while transmitting… - Our own (or nearby) transmission is deafening our receiver
Signals sent by sender don’t always end up at receiver intact
  Complicated physics involved, which we won’t discuss
  But what can go wrong?
Notes: Broadcast – anybody in proximity can hear and interfere (assuming the same channel)
Half-duplex: Not an engineering problem – but a fundamental physics that our strong transmission is deafening to our receiver.
Solve by different channels/bands for RX/TX

## Slide 16: Path Loss / Path Attenuation
Free Space Path Loss:
d = distance
λ = wave length
f = frequency
c = speed of light
Reflection, Diffraction, Absorption
Terrain contours (Urban, Rural, Vegetation).
Humidity
Notes: reduction in power density (attenuation) of an electromagnetic wave as it propagates through space.
Path loss may be due to many effects, such as free-space loss,refraction, diffraction, reflection, aperture-medium coupling loss, and absorption. Path loss is also influenced by terrain contours, environment (urban or rural, vegetation and foliage), propagation medium (dry or moist air), the distance between the transmitter and the receiver, and the height and location of antennas.

## Slide 17: Multipath Effects
Signals bounce off surface and interfere with one another
Self-interference
17
S
R
Ceiling
Floor

## Slide 18: Ideal Radios
(courtesy of Gilman Tolle and Jonathan Hui, ArchRock)

## Slide 19: Real Radios (courtesy of Gilman Tolle and Jonathan Hui, ArchRock)

## Slide 20: The Amoeboed “cell” (courtesy of David Culler, UCB)
20
Signal
Noise
Distance
Notes: 20

## Slide 21: Interference from Other Sources
External Interference
  Microwave oven is turned on and blocks your signal
  Would that affect the sender or the receiver?
Internal Interference
  Nodes (of the same network) within range of each other collide with one another’s transmission
We have to tolerate external interference and path loss, multipath, etc. but we can avoid internal interference?

## Slide 22: Bitrate (aka data-rate)
The higher the SNR (Signal to Noise Ratio) –
the higher the (theoretical) bitrate.
Modern radios use adaptive /dynamic bitrates.
Q: In face of loss, should we decrease or increase the bitrate?
A: If caused by free-space loss or multi-path fading -lower the bitrate.
If external interference - often higher bitrates (shorter bursts) are probabilistically better.

## Slide 23: Wireless Bit Errors
The lower the SNR (Signal/Noise) the higher the Bit Error Rate (BER)
We could make the signal stronger…
Why is this not always a good idea?
  Increased signal strength requires more power
  Increases the interference range of the sender, so you interfere with more nodes around you
    And then they increase their power…….
How would TCP behave in face of losses?
Local link-layer Error Correction schemes can correct some problems (should be TCP aware).
23

## Slide 24: 802.11
24
aka - WiFi …
What makes it special?
Deregulation > Innovation > Adoption > Lower cost = Ubiquitous technology
Notes: 24

## Slide 25: 802.11 Architecture
Designed for limited area
AP’s (Access Points) set to specific channel
Broadcast beacon messages with SSID (Service Set Identifier) and MAC Address periodically
Hosts scan all the channels to discover the AP’s
  Host associates with AP
25
802.11 frames exchanges
802.3 (Ethernet) frames exchanged

## Slide 26: Wireless Multiple Access Technique
Collision Detection?
  Where do collisions occur?
  How can you detect them?
Carrier Sense?
  Sender can listen before sending
  What does that tell the sender?
Notes: With CS – what’s the relation between propagation delay and probability of collision?

## Slide 27: Hidden Terminals
27
A and C can both send to B but can’t hear each other
  A is a hidden terminal for C and vice versa
Carrier Sense will be ineffective
A
B
C
transmit range
Notes: 27

## Slide 28: Exposed Terminals
28
Exposed node: B sends a packet to A; C hears this and decides not to send a packet to D (despite the fact that this will not cause interference)!
Carrier sense would prevent a successful transmission.
A
B
C
D
Notes: 28
Can both B send to A and C send to D at the same time? Yes! – no problem with that… however CS prevents such transmission … exposed node…

## Slide 29: 5 Minute Break
29
Notes: 29

## Slide 30: Key Points
No concept of a global collision
  Different receivers hear different signals
  Different senders reach different receivers
Collisions are at receiver, not sender
  Only care if receiver can hear the sender clearly
  It does not matter if sender can hear someone else
  As long as that signal does not interfere with receiver
Goal of protocol:
  Detect if receiver can hear sender
  Tell senders who might interfere with receiver to shut up

## Slide 31: Basic Collision Avoidance
Since can’t detect collisions, we try to avoid them
Carrier sense:
  When medium busy, choose random interval
  Wait that many idle timeslots to pass before sending
When a collision is inferred, retransmit with binary exponential backoff (like Ethernet)
  Use ACK from receiver to infer “no collision”
  Use exponential backoff to adapt contention window
Notes: Why do we wait?
Why not just send right away as medium becomes clear?

## Slide 32: CSMA/CA - Collision Avoidance
32
Before every data transmission
  Sender sends a Request to Send (RTS) frame containing the length of the transmission
  Receiver respond with a Clear to Send (CTS) frame
  Sender sends data
  Receiver sends an ACK; now another sender can send data
When sender doesn’t get a CTS back, it assumes collision
sender
receiver
other node in
sender’s range
RTS
ACK
data
CTS
Notes: 32

## Slide 33
33
If other nodes hear RTS, but not CTS: send
  Presumably, destination for first sender is out of node’s range …
sender
receiver
other node in
sender’s range
RTS
data
CTS
data
CSMA/CA - Collision Avoidance
Notes: 33

## Slide 34
34
If other nodes hear RTS, but not CTS: send
  Presumably, destination for first sender is out of node’s range …
  … Can cause problems when a CTS is lost
When you hear a CTS, you keep quiet until scheduled transmission is over (hear ACK)
sender
receiver
other node in
sender’s range
RTS
ACK
data
CTS
CSMA/CA -MA with Collision Avoidance
Notes: 34

## Slide 35: RTS / CTS Protocols (CSMA/CA)
35
Overcome hidden terminal problems with contention-free protocol
  B sends to C Request To Send (RTS)
  A hears RTS and defers (to allow C to answer)
  C replies to B with Clear To Send (CTS)
  D hears CTS and defers to allow the data
  B sends to C
B
C
D
RTS
CTS
A
B sends to C
Notes: 35
Does not solve the exposed terminal problem.
High overhead and especially increase latency.
assumes symmetric signal qualities - if node A hears node B - than also node B hears node A. - not always the case. (Especially local interference at receiver).

## Slide 36: Channelization of spectrum
36
Typically, available frequency spectrum is split into multiple channels
Some channels may overlap
26 MHz
100 MHz
200 MHz
150 MHz
2.45 GHz
915 MHz
5.25 GHz
5.8 GHz
3 channels
8 channels
4 channels
250 MHz
500 MHz
1000 MHz
61.25 GHz
24.125 GHz
122.5 GHz
Notes: 36

## Slide 37: Preventing Collisions Altogether
Frequency Spectrum partitioned into several channels
  Nodes within interference range can use separate channels
  Now A and C can send without any interference!
  Most cards have only 1 transceiver
  Aggregate Network throughput doubles
37
A
B
C
D

## Slide 38: Using Multiple Channels
802.11: AP’s on different channels
  Usually manually configured by administrator
  Automatic Configuration may cause problems
Most cards have only 1 transceiver
  Not Full Duplex: Cannot send and receive at the same time
Multichannel MAC Protocols
  Automatically have nodes negotiate channels
    Channel coordination amongst nodes is necessary
    Introduces negotiation and channel-switching latency that reduce throughput
38

## Slide 39
  Partition space into non-overlapping cells.
39
Preventing Collisions Altogether

## Slide 40: Large Multihop Network (courtesy of Sanjit Biswas, MIT)
1 kilometer

## Slide 41: Multi-Hop Wireless Ad Hoc Networks
R
A
B
C
D
S
Courtesy of Tianbo Kuang and Carey Williamson University of Calgary)
Notes: Maybe can be self-healing !
Maybe can be multipath?

## Slide 42
42
R
A
B
C
D
S
Multi-Hop Wireless Ad Hoc Networks

## Slide 43
43
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
(Assume ideal world…)
Multi-Hop Wireless Ad Hoc Networks

## Slide 44
44
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 45
45
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 46
46
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 47
47
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 48
48
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 49
49
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 50
50
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 51
51
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 52
52
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 53
53
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 54
54
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 55
55
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 56
56
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 57
57
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 58
58
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 59
59
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 60
60
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 61: Wireless Multihop Networks
Vehicular Networks
  Delay Tolerant (batch) sending over several hops carry data to a base station
Common in Sensor Network for periodically transmitting data
  Infrastructure Monitoring
    E.g., structural health monitoring of the Golden Gate Bridge

## Slide 62
62
R
A
B
C
D
S
The end of phone companies & ISPs?
  Self healing
  Multipath routing

## Slide 63: What Do YOU Think Really Happens?

## Slide 64
64
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Problem 1: node A can’t use both
of these links at the same time
- shared wireless channel
- transmit or receive, but not both
(Reality check…)
Relays needs to “Store and Forward”.
Multi-Hop Wireless Ad Hoc Networks

## Slide 65
65
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Problem 2: S and B can’t use both
of these links at same time
- range overlap at A
Multi-Hop Wireless Ad Hoc Networks

## Slide 66
66
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Problem 3: LOTS of contention for the channel
- in steady state, all want to send
- need RTS/CTS to resolve contention
RTS: Request-To-Send
CTS: Clear-To-Send
Multi-Hop Wireless Ad Hoc Networks

## Slide 67
67
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
RTS
CTS
Multi-Hop Wireless Ad Hoc Networks

## Slide 68
68
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 69
69
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
RTS
CTS
Multi-Hop Wireless Ad Hoc Networks

## Slide 70
70
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 71
71
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 72
72
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 73
73
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 74
74
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 75
75
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 76
76
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 77
77
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 78
78
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 79
79
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 80
80
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 81
81
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Problem 4: TCP uses ACKS to
indicate reliable data delivery
- bidirectional traffic (DATA, ACKS)
- even more contention!!!
Multi-Hop Wireless Ad Hoc Networks

## Slide 82
82
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 83
83
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 84
84
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 85
85
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 86
86
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
Multi-Hop Wireless Ad Hoc Networks

## Slide 87
87
S
R
A
B
C
D
1
2
3
4
5
6
7
8
9
10
11
12
1
1
1
2
2
Multi-Hop Wireless Ad Hoc Networks

## Slide 88
88
S
R
A
B
C
D
1
3
4
5
6
7
8
9
10
11
12
1
2
Multi-Hop Wireless Ad Hoc Networks

## Slide 89
89
S
R
A
B
C
D
1
3
4
5
6
7
8
9
10
11
12
1
2
Multi-Hop Wireless Ad Hoc Networks

## Slide 90
90
S
R
A
B
C
D
1
3
4
5
6
7
8
9
10
11
12
1
2
Multi-Hop Wireless Ad Hoc Networks

## Slide 91
91
S
R
A
B
C
D
1
3
4
5
6
7
8
9
10
11
12
1
2
Multi-Hop Wireless Ad Hoc Networks

## Slide 92
92
S
R
A
B
C
D
1
3
4
5
6
7
8
9
10
11
12
1
2
Multi-Hop Wireless Ad Hoc Networks

## Slide 93
93
S
R
A
B
C
D
1
3
4
5
6
7
8
9
10
11
12
1
2
2
Multi-Hop Wireless Ad Hoc Networks

## Slide 94: Lesson
Multi-hop wireless is hard to make efficient
Store and forward
Halves the bandwidth for every hop.
Doubles the latency for every hop.
Increases Interference.
Horrible idea for Internet access.
Even worse for interactive applications (such as video-conferencing).

## Slide 95: Summary
Wireless is a tricky beast
  Distributed multiple access problem
  Hidden terminals
  Exposed terminals
  Current protocols sufficient, given overprovisioning
Multihop even more complicated

## Slide 96: Questions ?
- Thank you -